# A firm based at glasgow

### Abstract

Smiths Corporation is a firm based at Glasgow. It needs an enterprise network to be designed, amended and tested. This network should have a performance which is easily scalable, manageable and reliable. In this network all major services are based on the head office and needs to be accessed by all staff. There are two other offices at Newcastle and Manchester. The head office at Glasgow is connected to Newcastle through a T1link (serial).

The next branch at Manchester is connected to Newcastle via a metro link. In case of emergency conditions like failure of a metro link or T1 link the firm insisted an ISDN backup link between Glasgow and Manchester. The routing protocols running across the company are OSPF and ISIS. The other services like DHCP and NAT are also used.

### 1. Aim

To design and implement an enterprise network for Smiths Corporation which is scalable, reliable and always available for service.

### 2. Objectives

- OSPF is to be run between Glasgow and Newcastle which is the back bone (area0).

- Glasgow is to be connected to 5 subnets which fall under area 1.

- ISIS is to be run between Newcastle (area1) and Manchester (area2).

- Each office has to be connected to 5 subnets of 20 devices each.

- Route redistribution is to be done at Newcastle.

- Route summarization is to be configured.

- VLSM is to be used.

- DHCP and NAT are the other services to be used at each site.

- Static route is to be used between ISP and Glasgow to prevent traffic originating from outside the network.

- The far end address of ISP is 194.2.3.9 /30 and ISP server is located at 134.120.10.10/24.

- A backup link is to be installed between Manchester and Glasgow through ISDN.

### 3. Scalability

It should be easier to create new subnets without affecting the addressing scheme. Also route summarisation has to be done as IP addresses are distributed.

In the network presented there are 5 local area networks in each site. Each LAN is given 30 hosts so the design can have 10 more hosts per LAN as the requirement is only 20 hosts. Also there are 3 more LANs are redundant which can be used in the future.

### 4. Performance

The networks performance is based on the through put, utilization and its speed of response. The factors that affect performance are the congestion, link speeds and device and protocol responses.

In this network the link between Glasgow and Newcastle is a T1 link and the link between Newcastle and Manchester is a Metro link. So the network will be faster and reliable.

### 5. Availability

Whenever a fault comes in one of the links the whole network is affected. So in order to make the network always available an ISDN link is installed between Glasgow and Manchester.

### Network Topology

### 6. IP Addressing Scheme

Addressing scheme is a important factor that affects the scalability of a network. In this network class A private address 10.0.0.0/8 is deployed through this network.

### 7. OSPF (Open Shortest Path First)