# Port-based Multi-homed Mobile

### Port-based Multi-homed Mobile IPV6

### Abstract—

Mobile technologies have been developing continuously and future communication technologies will be the high end of wireless networks. Future generation communication networks will use the multiple access technologies by integrating the different networks. Mobile Internet Protocol (Mobile IP) will be the key enabling technology to provide seamless roaming among different technologies. To enable this feature, end -user terminals should be able to maintain multiple active network connections while roaming in different technologies. Such a concept of multihomed mobile host will provide the active connections among different networks based on availability and required applications. The advanced version of mobile internet protocol is Internet Protocol Version 6 abbreviated as IPV6 has overcome the main problems of IPV4, especially the looming exhaustion of the IPV4 address space and improve the overall operation performance of the protocol. This journal proposes the concept of Mobile IPV6 with extending multihoming functionality to enable the mobile host to register multiple care of addresses at home agent to increase the performance of wireless network connectivity.

### Index Terms—

Mobile IPV6, Multi-homed MIPV6, Port based MIPV6, Policy based network management

### INTRODUCTION

In future network communications, wireless network areas will connect through different service providers integrating by different technologies like WI-FI, Bluetooth, GSM that these technologies will support wireless network connectivity to wired network infrastructures.

The need of Integrated Network Platforms:

The current technologies such as universal mobile telecommunication systems (UMTS), WLAN, Bluetooth are providing same type of data and media applications to mobiles but differ in their providing capabilities that GSM has a broad coverage and WLAN has high bandwidth. Because of these incompatible network platforms, mobile users are not able to be active anywhere and anytime. The best solution for this problem is Integration of different technologies with ultimate goal is to provide active connection to the user every time and anywhere.

The integration of different technologies is possible by the Mobile Internet Protocol (MIP). Mobile IP is IETF standard created to provide the integration services between wireless and wired network platforms.

The major advantages of integrated network platforms are as follows.

True global roaming: This is the main advantage of Mobile IP that enables a user always make an active connection regardless of location and whatever technology available at that moment. Finally Mobile IP provides roaming among all technologies, which support IP services.

Integration of services: Mobile IP has been developing continuously and extended towards telecommunication services. Mobile IP infrastructure can provide integration service among different technologies in a seamless manner through a single device.

Platform selection depending on network properties: There are different technologies available in the present telecommunications and the selection of particular network depends on the requirements of the active communications such as WLAN provides high speed data transfers than UMTS.

### MOBILE INTERNET PROTOCOL (IP)

The main components of the mobile IP solution are as follows.

Mobile Node: It is a mobile device, which can roam around the internetwork.

Home Agent:A router can work as home agent connected to the home network and contains the user's permanent IP address and other information. It is the responsible for collecting the datagrams from other networks while the mobile node is in roaming and it can forward that datagrams to the mobile node.

Foreign Agent:A router can work as foreign agent on foreign network to which the mobile node currently connected. I t can operate most of the home agent operations on device. Depending on the mode of operation, it can receive the datagrams from home agent and forward to the mobile node. It can support the sharing of mobility information among the available networks to make active connection for the mobile node.

### MOBILE IPv6: The Evolution of IP

Mobile IPis anInternet Engineering Task Force(IETF) standard communicationsprotocolthat is designed to allow mobile device users to move from one network to another while maintaining a permanent IP address.

The basic problem with supporting mobile devices in IP internetworks is that routing is performed using the IP address, which means the IP address of a device is tied to the network where that device is located. If a device changes networks, data sent to its old address cannot be delivered by conventional means. Traditional workarounds such as routing by the full IP address or changing IP addresses manually often create more problems.

The primary motivation for creating IPv6 was to rectify theaddressing problems in IPv4. The IPv6 addressing scheme is similar in general concept to IPv4 addressing, but has been completely overhauled to create an addressing system capable of supporting continued Internet expansion and newapplicationsfor the foreseeable future.

### Design Goals of IPv6

The problem of addressing was the main motivation for creating IPv6. Some of the most important goals in designing IPv6 are as follows.

Larger Address Space: IPv6 had to provide more addresses for the growing Internet.

Better Management of Address Space:It was desired that IPv6 not only include more addresses, but a more capable way of dividing the address space and using the bits in each address.

Easier TCP/IP Administration:The design of IPv6 hoped to resolve some of the current labour-intensive requirements of IPv4, such as the need to con IP addresses. Even though tools like DHCP eliminate the need to manually con many hosts, it only partially solves the problem.

Modern Design for Routing:In contrast to IPv4, which was designed before we all had any idea what the modern Internet would be like, IPv6 was created specifically for efficient routing in our current Internet, and with the flexibility for the future.

Better Support for Multicasting:Multicasting was an option under IPv4 from the start, but support for it has been slow in coming.

Better Support for Security:IPv4 was designed at a time whensecuritywasn't much of an issue, because there were a relatively small number of networks on the internet, and their administrators often knew each other. Today, security on the public Internet is a big issue, and the future success of the Internet requires that security concerns be resolved.

Better Support for Mobility:When IPv4 was created, there really was no concept of mobile IP devices. The problems associated withcomputersthat move between networks led to the need forMobile IP. IPv6 builds on Mobile IP and provides mobility support within IP itself.

### Multihomed Mobile IP

According to the standard operation of mobile IPV6, a mobile node can connect to only one wireless network at a time means single care of address while disconnecting from home network. The concept of multihome mobile IPV6 is to provide multiple connections to the mobile node that means multiple care of addresses. The extension of mobile IPV6 with multihoming will allow the correspondent node to associate the mobile nodes home agent with multiple care of addresses. In case of multiple registered care of addresses, the home agent and the correspondent node may use different care of addresses to reach the mobile node. Using multiple care of addresses is beneficial, if the total amount of traffic capacity needed extends the capability of one single interface. In that case flows can be sent via different interfaces.

Multi-homed mobile IP enhances the performance and reliability for mobile hosts connecting to WLANs. Wireless connections are prone to errors and changing conditions which must be considered to enable applications for desktop computers to be usable on mobile hosts connecting wireless. The multihoming is managed by the mobile IP and hidden from the IP routing, keeping IP routing protocols like the Routing Information Protocol (RIP) and Open Shortest Path First (OSPF) unaware. For a sender, multi-homed mobile IP can be considered an any-cast approach where a sender relies on the network protocol to use the best available destination for the packets. The available destination will be one of possibly multiple care-of addresses used by a mobile host. In IPV6, an any-cast address is used to reach the best available destination (server) among multiple destinations supporting the service required. The difference from the any-cast approach in IPV6 is that it is address-based instead of server-based and the destination will be the same host.

### THE PORT BASED MOBILE IP ARCHITECTURE

According to the following architecture, a mobile node should be capable to connect to different interfaces to send and receive the traffic.

The port based mobile IPV6 is the extension of multi-homed mobile ipv6 by including a flow mobility option header that specifies the port number and protocol when registering a binding. To do this a mobile node can make a binding between correspondent node and home agent that only supports only a single flow should be forwarded to the specific care of address. By including multiple flow mobility option headers in the binding unit can control multiple flows among multiple care of addresses. It is possible to enable flow mobility between devices by registering the multiple devices with the same home address.

The binding update has been modified by adding two flags that M-flag and S-flag, and a flow mobility option header contains port number and protocol number. The following shows the modified binding update header.

### Binding update header

The M-flag indicates a multi-homed binding that it can store the current registered bindings information. The mobile node can use the S-flag to inform the home agent and correspondent nodes of which care of address to use as default. The following shows the flow mobility option header.

### Flow mobility option header

The port number used to identify the destination port number of the mobile node and the protocol number indicates the transport protocol number. The following shows the bindings for both an IP address as well as for a protocol and a port.

### Binding cache

According to the normal operation of mobile IPV6, when a mobile node identify a foreign network, first it can obtain an IP address from that foreign network and it has to register this care of address with its home agent by sending a binding update. If this is the first registration , there is no need to send the binding update with the M-flag or S-flag that there is no more previous registrations available and that there is only one care of address selected means no need of S-flag.

When the mobile node identifies the second foreign network, it will send a new registration update to the home agent by adding M-flag to the binding update message. So, the new registration information will be stored in the M-flag. The new care of address will not be connected until an assessment takes place to check the performance of the new care of address while the first care of address is in operation. In case of findings provide better performance by new care of address compared with the existing one, then a new binding update message will be send to the new care of address with M-flag and S-flag.

### THE PROTOTYPE

There are three access network technologies WLAN (802.11), WI-MAX (802.16) and UMTS used to implement the prototype. The following shows the evaluation topology.

### Evaluation topology

When the correspondent node send the traffic to the mobile nodes home agent, than can be redirected to the mobile nodes selected care of address by making a tunnel between them. A tunnel will be created for each registered care of address. According to the conducted experiments, the movement pattern during the experiment is as follows: the mobile node starts at a place nearby an 802.11 access point and moves towards another 802.11 access point. Between these two access points there is bad WLAN coverage. Beyond the second 802.11 access point, both 802.11 and 802.16 have bad coverage. The 802.16 cell cover the area of both 802.11 cells and the UMTS network cover both the 802.11 and 802.16 cells. After some time using the UMTS access the mobile node turns and starts to approach the (second) 802.11 AP again.

### POLICY BASED NETWORK MANAGEMENT

Fundamentally, a policy is a set of rules and instructions that determine a network operation. The evaluation of a policy rule is triggered by an event which results in a policy decision been enforced on a specific network device. As policies are declarative, they can be adapted at run-time to flexibly control system behaviour and are therefore becoming increasingly popular in adaptive, run-time configurable networks and information systems.

The IETF proposed a policy model based on three main blocks that are Policy Decision Point (PDP) and Policy Enforcement Point (PEP) entities, extended with a Policy Repository (PR) entity. The following shows the policy based decision model.

### Policy-Based Decision Model

### A Policy Repository:

The policy repository contains the information such as user preferences, cost of the service and signal strength of available access networks and it can pass this information to the policy decision point according to the request about policy parameters. The policy repository can collect information of policy parameters through the measurements of the environment.

### A Policy Decision Point:

The policy decision point is the entire control point in this model by making decision based on policy parameters which are delivered by the policy repository. The policy decision made by policy decision point will deliver to the policy enforcement point.

### A Policy Enforcement Point:

The policy enforcement point receives policy decisions from the policy decision point and conducts the operations based on those policy decisions. The policy enforcement point is said to enforce the policy decision.

### POLICY PARAMETERS

A policy rule is specified in terms of a number of network and user parameters. These parameters are continuously updated and stored in a policy repository in both the network side and mobile terminal. Policy parameters include, network conditions, handover latency, power consumption, network coverage, cost, mobile speed and user priority.

### POLICY SYSTEM ARCHITECTURE

The following architecture shows the operation of policy based decision system.

### Policy system architecture

We propose policy system architecture for making policy-based access control decisions and network selection decisions in the network and at the user terminal respectively. Policy system architectures tend to focus on the relationship between the point where the outcome of a policy is enforced, e.g. the point in a network where admission control is enacted, and the point where the decision on whether a policy conditions are satisfied is taken, i.e. the Policy Decision Point (PDP). The PDP for network access control is implemented on a server within the network and uses an open communication protocol with enforcement points. This approach allows implementing the PDP at a location where network information such as data rate, coverage area, mobility support and current load are available, e.g. a base station, switch or a network router. Data required by the admission controller policy engine is maintained in a policy repository. The policy repository contains the policy parameters which are used in the decision making process.

This architectural approach also facilitates the updating of policy rules through the network. For the user the enforcement point is their mobile terminal, which is typically powerful enough to run a PDP. Condition state of user policies are however restricted to measurements that can be made by the terminal or are available to the user, such as packet round trip time, cost of usage, perceived subjective quality of service, etc. since open access to the providers'

Network measurements are unlikely. The policy rules within the PDPs are adaptive in nature so as to achieve load balancing across the heterogeneous networks operated by a provider. Adaptive policy rules enable each network to carry the maximum traffic load for the available spectrum as network load levels vary. The design of policy rules that achieve business goals has to be done carefully and with a good understanding of the networks operation. Conflicting policies can cause unexpected behaviour in the network and mechanisms are available for detecting certain conflicts before deployment.

### RESULTS

For the decision of which access network to direct a flow to a policy value is used being a weighted sum of normalized values of battery consumption, cost, and network performance. Results from experiments show that handover decisions are taken at the right time.

The calculated policy values for each access network at the MN. The bandwidth and jitter is also shown

In the above , each vertical line indicates the time when a handover was performed. The blue curve indicates the policy value for the WLAN 802.11 access, the red curve indicates policy value for the UMTS access and the yellow curve shows the policy value for the WI-MAX 802.16 access. The access network having the lowest policy value is selected. The upper black curve shows the bandwidth (kbps) received at the mobile node and the lower black curve shows the jitter (msec) of the received traffic.

The correspondent node sends constant bit-rate traffic (UDP) of 20 kbps. The 802.11 access points have a capacity of 11Mbps (5.5 Mbps in practice) and the 802.16 access point was set to 2.22 Mbps (BPSK ½ modulation). The UMTS network performed about 300 kbps downlink (depending on other on-going traffic). The evaluation started indoors and the first 802.11 access point was selected the first 9 seconds. At that time the mobile node's distance to the 802.11 access point render in an increasing policy metric due to increased Round Trip Time (RTT) and jitter metrics of mobile IP registration messages. At this time the 802.16 policy metric is the lowest and therefore is selected. The handover renders in a small increase in jitter metrics but the bandwidth is kept stable with small fluctuations. The short dip in bandwidth at 10 seconds from start indicates that the handover decision is taken at the right time. After 40 seconds from start the connection to the second 802.11 access point is considered better than the 802.16 access regarding RTT and jitter metrics. This is illustrated by the jitter plot showing lower jitter metrics for the received traffic, after handover from the 802.16 access network to the 802.11 access network. The bandwidth is shown to be stable during this handover as well. However, a small increase in fluctuation of measured bandwidth is experienced. After 83 seconds from start, the mobile node leaves the indoor environment (where the 802.11 and 802.16 access networks are installed) and enters an outdoor environment. Handover to the UMTS access network takes place after 86 seconds from start due to both the 802.11 and 802.16 radio signals being faded by the wall of the left building. Since today's UMTS networks prioritize circuit switched traffic before packet switched (IP) traffic, the jitter increases as well as the fluctuations of both the bandwidth and the jitter metrics. The trend of the bandwidth and jitter plots shows that the handover decision is taken at the right moment, since this trend is kept while using the UMTS network. When returning back into the building (after 111 seconds from start) handover takes place to the 802.11 access network, rapidly increasing both the bandwidth and jitter metrics.

### CONCLUSION

This paper has described how Mobile IPv6 can be extended to handle port-based multihoming. The extension allows different flows that can be directed to the destination through different interfaces on the mobile node leveraging differences in coverage, Quality of Service, cost, bandwidth, delay etc. among different wireless and fixed access networks. The results presented in this paper show that load and capacity can be measured on the different interfaces. The results from the measurements can be used to perform load balancing between different interfaces, both between the mobile node and multiple correspondent nodes and multiple flows between mobile node and a single correspondent node.

### References

[1] CiprianPopoviciu, EricLevy-Abegnoli, PatrickGrossetete, “Deploying IPV6 networks (Book style with paper title and editor)”, Indianapolis: Cisco Press, 2006

[2] Qing Li, Tatuya Jinmei, Keiichi Shima, “Mobile IPV6: Protocols and Implementations (Book style with paper title and editor),” Massachusetts: Morgan Kaufmann Publishers, 2009.

[3] Christer Ahlund, Arkady Zaslavsky, “Multihoming with Mobile IP (Periodical style—Submitted for publication)”. Sweden: Lulea University of Technology. Available: http://citeseerx.ist.psu.edu/viewdoc/download?doi= 10.1.1.106.5973&rep=rep1&type=pdf

[4] Ken Murray, Dirk Pesch, “Policy basd admission control across heterogeneous wireless networks”, Ireland: Cork Institute of Technology. Available: http://www.aws.cit.ie/personnel/Papers/Paper226.pdf

[5] Sebastien Pierrel, Topi Erlin, Janne Roslof, “A prototype for policy driven control of heterogeneous network access (Periodical style—Submitted for publication)”. Finland: Turku polytechnic, School of telecommunications and e- business. Available: http://www.cs.hut.fi/~pmrg/publications/ VHO/2004/ Pierrel_Erlin_Roslof_APPDCHNA.pdf

[6] Christer Ahlund, Robert Brannstrom, Karl Andersson and Orian Tjernstrom, “Port-based multihomed mobile IPv6 for heterogeneous networks (Periodical style—Submitted for publication)”. Sweden: Lulea University of Technology, submitted for publication. Available: http://www.ltu.se/polopoly_fs/1.22583!port- based%20multihomed%20mobile%20ipv6%20for%20heterogeneous%20networks.pdf

[7] Justino santos, Nuno Senica, Susana Sargento and Rui Aguiar, “Mobility in Heterogeneous networks: Integration Process”, Aveiro: University of Aveiro. Available: http://ubicomp.algoritmi.uminho.pt/csmu/proc/santos-145.pdf

[8] N.A. Fikouras, C. Gorg, I. Fikouras, “Achieving Integrated Network Platforms through IP”, Bremen: University of Bremen. Available: http://www.comnets.uni-bremen.de/~niko/ publications/ wwrf01.pdf

[9] Christer Ahlund, Robert Brannstrom, Karl Andersson and Orian Tjernstrom, “Multimedia flow mobility in heterogeneoue networks using multihomed mobile IPv6 (Periodical style—Submitted for publication)”. Sweden: Luleå University of Technology. Available: http://www.tt.luth.se/staff/robert/pub/momm06.pdf

[10] Claude Castelluccia, “A Hierarchical Mobile IPv6 Proposal”, Rapport technique, November 1998

[11] Introduction to IP Version 6 (white paper), Washington: Microsoft Corporation, 2000

[12] “Internet Protocol Version 6 (IPv6) / IP Next Generation (IPng)” Available: http://www.tcpipguide.com/free/t_InternetProtocol Version6IPv6IPNextGenerationIPng.htm