# Eliminating handoff latencies in 802.11 wlans using multiple radios

### Introduction

### Authors Background

Eliminating handoff latencies in 802.11 WLANs using multiple radios: applications, experience, and evaluation is an article that was published in Berkeley, CA

(2005) by three authors at Internet Measurement Conference Proceedings of the 5th ACM SIGCOMM conference on Internet Measurement. Two of these authors, namely Vladimir Brik and Suman Banerjee, are from the Department of Computer Sciences, University of Wisconsin-Madison, WI and the other one, Arunesh Mishra, is from the Department of Computer Science, University of Maryland, College Park, MD.

### Topic Background

Wireless Local Area Networks (WLANs) have seen a good acceptance from both public and private sectors in recent years. They are being used in many companies, hot spots, universities and homes due to their ease of installation, reasonable prices, and the high data rates that they support. Since at beginning these wireless networks (WLANs) were designed for indoor usage, the access points (APs) that build them have limited coverage range (50m - 300m) (Tsao & Cheng, 2007). Thus, uninterrupted connectivity is one of the important requirements in WLANs based IEEE 802.11 that provides mobility during the utilizing of the network; however, the handoff process when a station moves from its current base station range to another is still considered an issue in the IEEE 802.11 specification. This problem is especially considered critical for sensitive real-time applications such as Voice over Internet Protocol (VoIP) that can affected during the time consumed by handoff process. For this reason, many alternative handoff schemes have been proposed in order to support seamless handoff in WLANs. In Eliminating handoff latencies in 802.11 WLANs using multiple radios: applications, experience, and evaluation a new mechanism was proposed to eliminate the total handoff latency. In this paper, we critically review the quality of their paper to show the strengths and weaknesses of this proposed scheme as well as evaluating the results and conclusions.

### Body of Critical Review

By reading title of the paper, Eliminating handoff latencies in 802.11 WLANs using multiple radios: applications, experience, and evaluation, the reader can get an idea of what is proposed inside. The idea in the title shows that how to eliminate (or totally remove) the handoff latencies (since the entire handoff process combines three types of delay that are scanning delay, re-authentication delay, and re-association delay (Pack et al, 2007) in WLANs by using multiple radios. However, it is still difficult for the reader to predict how this method works from the title.

The authors divided their work in this article into several sections. Firstly, they started with an abstract to summarize their paper. In the abstract section, they showed the need for eliminating the handoff latency in WLANs and then briefly presented their mechanism (called MultiScan) and some of its advantages comparing to other existing schemes such as the ability to implement this mechanism without the need for any modificatiosn in the existing Access Points (APs). However, they did not show any weaknesses of their scheme like the cost needed to modify the existing clients' stations in order to have two working network cards. At the end of the abstract, they described the contents and flow of the paper and a real example used to evaluate the performance of the scheme, namely Skype (a popular commercial VoIP application).

In the first part of the introduction part, the authors started it by talking about the IEEE 802.11 based WLANS showing how this standard is being popular nowadays and equipped in most of the mobile devices in order to provide access to the internet or other local area networks LANs. Then they showed some limitations in the access range of this stranded that lead to the handoff process. After that, they explained how this handoff process is critical to the real time applications when the user needs to use the network while passing thorough several handoffs. Since each handoff process takes between 60 ms and 400 ms in the current 802.11 standard, it is critical to real time latency-sensitive applications such as Voice over Internet Protocol VoIP. At the end of the first part of the introduction, the authors emphasized again about the goal of their paper and the proposed solution to achieve that. (For seamless VoIP application, it is desired that full latency does not exceed 50 ms (General characteristics of international telephone connections and international circuits. ITU-TG, 114, 1998.)).

In the second part of the paper, the authors argue the need for the two radios (two wireless cards) in order to implement their mechanism and how these radios could help to totally eliminate the handoff process. This was followed by comparing their method to mechanisms (Neighbor Graphs and SyncScan approaches) that were proposed by other people. However, the authors did not show the advantages of these approaches, but they focused only on their disadvantages which were followed by showing the same advantage of their new mechanism (requires implementation in the client side only) without mentioning any drawback of their mechanism comparing to other ones such as total cost the power consumption of using two radios.

In the third and last part of the introduction (exploiting multiple radios) which I think it should be under the “Handoff in MultiScan” section since it provides some details related the usage of the two radios used in their mechanism, the authors argued why in their method only one radio is being used at time (they call it the primary interface) while the other one is used to facilitate a fast “make-before-break” handoff process. The reason behind using only one interface at a time is the interference between these two radios even when they are operating on non-interfering channels. They showed this in an experiment of “ping flood” in the single and double operating interface(s). A figure was also plotted to demonstrate the difference in performance between these two approaches. At the end of the introduction part, they briefly highlighted again the rest of the paper's contents and the need for their new mechanism for real-time applications.

In second section of the paper, Background, the authors of the paper gave some explanation on the standard handoff process showing its three phases, namely scanning, authentication, and association. This was followed by giving some insights on which of those three phases most of the handoff time is spent (90% of the time spent in scanning phase) and which will be eliminated by the use of their new scheme.

The background section was followed by the “Handoff In Mutliscan”, where the authors explained in detail how their new mechanism works. In this section, the authors showed clearly that there method is valid and it meets the objective of the study by eliminating the total handoff latency at the 802.11 standard. They also briefly motioned one of the disadvantages of their scheme that is packs loss during the handoff process. This was due to the fact of packets queued in the primary interface will not be accepted in the old AP, if this current AP learns that the station is associated to another AP. However, the authors did not mention that this drawback is considered critical to the real-time applications. At the end of the section, there was a sub-section, namely “Address Management”, in which some of the requirements for the MultiScan scheme were presented.

In the next section, Experimental Evaluation, the authors presented validness of their scheme by showing two sets of experiments. In the first experiment, they showed that ICMP ping floods experienced no perceptible delay due to MultiScan handoffs. In this experiment, the authors performed 10 handoffs using MultiScan module within1 minute period. Furthermore, they also showed two figures to support their experiment which were easy to understand and their titles clearly stated. At the end, they compared the performance of this experiment to the one that uses single interface to show that their method meets the objective of the study. Another figure was also used to support their argument. In the second experiment, the authors used a real-time application, namely Skype, to test their mechanism. In the Skype experiment, they looked at two different metrics, namely, end-to-end latencies and the sound quality. However, in the results, they showed only audio quality metric assuming that the other metric will have no difference from the first performed experiment. In this experiment, the authors also compared their mechanism to the one that uses one radio interface and they showed that theirs is better. This performance comparison was demonstrated by showing when a client using a single interface performs a single handoff; the signal quality will drop more than if a client using the MultiScan scheme performs 10 similar handoffs. Also, they showed this comparison in simple two figures whereby a significant difference can been seen between the two audio signals.

In the second last section, Related Work, the authors presented some work that was done by other people related to the same area of reducing the handoff delay in WLANs. All of they presented work was related in the sense of enhancing handoff performance, but not eliminating it as was described in their scheme. In addition, the authors mostly focused on the drawbacks of those mechanisms. Also, two of the related schemes (Neighbor Graphs and SyncScan) were explained again in this section in addition to the introduction part. At the end of this section, a simple table shows a comparison of different handoff mechanisms with the new MultiScan mechanism.

At the last part of the paper which is the conclusion, the authors summed up the strengths of the need to use two radios in the mobile devices showing that its advantages overweight the disadvantage of the implementation cost. At the end of this section, they briefly explained their future work that was to extend the MultiScan mechanism to handle Inter Access Point Protocol (IAPP).

### Conclusion

In conclusion, I believe that every article has got strengths and weaknesses as well as in this article. For this reason, while I was reading through this article, I have noticed some great strength as well as some weaknesses that this article got. Firstly, the idea of the new mechanism was totally new, at the time when the article was published; no scheme was able to eliminate the total handoff latency except MultiScan. This point is the most important strength that this article has got. Secondly, the test of the new proposed scheme was in real time manner and by using one of the most popular applications, Skype, to show the effectiveness of MultiScan. Thirdly, the figures and tables used were self-explanatory with titles that clearly state their contents. However, there are also some drawbacks in this article. For instance, the authors were always focusing at the strengths of their mechanisms without stating its weaknesses that might be critical considerations to people. For example, as the need to modify current mobile stations to have two radios which might be impractical to some people especially for modifying handheld devices. The other drawback of this mechanism is its power consumption which is due to the fact that using two radios consumes more power. And the last drawback of this mechanism would be the cost considerations. Furthermore, another weakness that I have seen in this article is the formatting. For instance, most publishes papers include at the beginning some headings such as Categories and Subject Descriptors, General Terms, and Keywords. However, these headings were missing in the article. Another thing to point out in the formatting is that some of the sub-sections were not numbered while some were numbered (for example, sub-sections under Experimental Evaluation and sub-sections under the Introduction part). The last thing about the weaknesses in this paper that I believe that it would be better if some section and sub-section were arranged in different sections. For example, the Related Work section, I think it would be better if this section was after the Background section rather at the end of the paper. However, even though this paper got some drawbacks, I believe that is article is one of the most interesting papers that I have read on handoff since it, once again, until now the only article that presents the mechanism to eliminate that total handoff in WLANs to 0 s.