# Internet Group management protocol

Internet Group management protocol (IGMP), a multicasting protocol in the internet protocols family, is used by IP hosts to report their host group memberships to any immediately neighboring multicast routers .

If any host on the internet want to join the multicast group (identified by class D multicast address) it send a membership report to the nearest router. And the router sends a membership query message to its sub network to find is there anyone who still wants multicast traffic. It means there are two types of messages in the IGMP.

- Membership Report.

- Membership Query.

When a router receives a multicast message it first check is there any receiver in its subnet that is interested in this packet. if there is any host the router will send packet to the destination and router continue to send packets until no one interested any more member of multicast group. Routers used IGMP to perform these tasks.

If there is more than one multicast router then one of them becomes designated router and this router will be the query router and responsible to check active hosts in the network.

### IGMP v1:

Hosts can join multicast groups. There were no leave messages. Routers were using a time-out based mechanism to discover the groups that are of no interest to the members .

In the IGMP version 1 only two types of packets one is membership query and other is membership report. In membership query router send message after every one minute to check out that is there any alive multicast group member. The second packet is membership report. It is send by the host to query router to request to join the some multicast group. There is no leave process exist in the IGMP v.1. The query router wait for the 3 minutes if there is no membership report it prune the interface. A pruned interface stops receiving the multicast feed for that group .

### IGMP v2:

Leave messages were added to the protocol. Allow group membership termination to be quickly reported to the routing protocol, which is important for high-bandwidth multicast groups and/or subnets with highly volatile group membership. For the improvement of IGMP functionality IGMP version 2 introduced with backward compatibility and also add some new features. Leave Group message - hosts can now notify routers that they no longer wish to receive traffic for a specific multicast group.

Group-Specific Query message - the router can query in the context of a specific group instead of all groups. When IGMPv2 routers receive a Leave Group message, they will put a Group-Specific Query message on the wire, asking if there are any group members left. If there's no response, the router can quickly stop forwarding multicast traffic for that group onto that segment.

Maximum Response Time field - a new query message field the router uses to specify the MRT. Used when you want to tweak the response time for the Host Membership Report, which can be helpful when there's a large number of multicast groups active on a segment. MRT can be tweaked to reduce floods of responses.

Querier election process - routers will elect a preferred router to send query messages when multiple multicast routers are attached to the same segment. Note that queries are sent every 125 seconds by the elected querier by default. In IGMPv1, the querier would send every 60 seconds.

### IGMP v3:

Major revision of the protocol. It allows hosts to specify the list of hosts from which they want to receive traffic from. Traffic from other hosts is blocked inside the network. It also allows hosts to block inside the network packetsthat come from sources that sent unwanted traffic.

The IGMP Version 3—Explicit Tracking of Hosts, Groups, and Channels feature enables a multicast router to explicitly track the membership of all multicast hosts in a particular multi-access network. This enhancement to the Cisco IOS implementation of IGMPv3 enables the router to track each individual host that is joined to a particular group or channel. The main benefits of this feature are that it provides minimal leave latencies, faster channel changing, and improved diagnostics capabilities for IGMP .

### References:

- http://www.networkdictionary.com/protocols/igmp.php.

- http://www.javvin.com/protocolIGMP.html.

- http://etutorials.org/Networking/Lan+switching+fundamentals/Chapter+9.+Implementing+Multicast+on+Catalyst+Switches/Understanding+IGMPv1+and+IGMPv2/.

- http://www.cciecandidate.com/?p=141.

- http://www.cisco.com/en/US/docs/ios/12_2t/12_2t8/feature/guide/ft_xtrk.html.

- http://www.soi.wide.ad.jp/class/99007/slides/25/06.html.

- http://www.soi.wide.ad.jp/class/99007/slides/25/07.html