# Local area network

### Introduction

The purpose of the assignment is to design and create a Local Area Network that can be used for a new Police Headquarters. The requirements for the new network design include a computer network, a telephone system and two-way voice communications with patrolling police officers.

The network should be designed in a manner to accommodate communication between the various districts of the Police Department, a Serious Crime Squad Unit and a Staff group for General Administration purposes and also provide a connection to the internet.

### Types of Topologies

### Ring Topology

In a ring topology each device is connected to the following device in line. The first and last devices are also connected to each other forming the ring.

Data is transmitted in one direction around the ring which helps prevent any possible data collision. The data in the form of a packet travels around the ring in the form of a token.

The token in turn communicates with each device as it passes to identify if it has arrived at the correct destination to send the message, if it the appropriate destination, a confirmation message is sent to the sender to communicate safe delivery.

However, if the token stops at a device which is not the intended destination, the signal is regenerated and continues around the ring till it reaches its correct destination.

### Star Topology

In a star topology all the nodes are connected to a central device, known as a hub. In this type of topology each node has its dedicated line which makes data transmission faster and more efficient

When a node sends a message it passes across the hub, where the message is read and the data is refreshed. The hub then sends the message directly to the intended node destination.

The star topology also allows data to be transmitted in several directions at a time and is not limited to one direction only, like ring topology.

In a star topology because of the centralized interconnectivity, any failure in the hub would result in the entire network to stop working.

### Extended Star Topology

Extended star topologies contain a central device known as a switch. The switch allows several sub units known as hubs to be connected to it, which is in turn connected by computers and other devices.

In an extended star topology, once a message is sent from one device, it passes across the switch which refreshes the message, sends it to the appropriate hub which then sends the messages to the intended device.

Extended star topologies operate similar to star topologies in that they provide extra functionality because they allow more devices to be interconnected over larger distances and also provide each device with its own dedicated cabling line.

Unlike a star topology, failure in an extended star topology doesn't result in the entire networking breaking down if one of the sub hubs weren't operating.

### Mesh Topology

In a mesh topology network, each node is interconnected to every other node within that network.

A mesh topology network allows message delivery to be more reliable since there are various routes for messages to take in order to reach their destination. Therefore if there was cable failure from one node to the next, it is still possible for the messages to use an alternative route to reach its desired destination.

This type of network however is difficult to install since it requires an extensive amount of cabling and logic to ensure that the computers are connected and communicating in the correct manner.

### Topology Recommendation

In my opinion the topology best suited to setup the in-house network (LAN) for the Police Department would be the Extended Star Topology, using Fiber Optic cabling.

This topology allows several computers and devices to be connected to hubs and several hubs to be in turn connected to a centralized switch. The various departments of the Police Station are spread throughout various floors therefore the Extended Star Topology can accommodate this type of arrangement.

The Police Department designates each floor for the various districts Northern, Southern, Eastern and Western, therefore a hub or two can be placed on each level. There is also a Serious Crime Squad Unit and Civilian Staff Area, in which hubs can also be placed to interconnect the many computers and devices. A main switch together with a backup switch can then be used to interconnect all the hubs.

The backup switch is added as a security feature to ensure that even if the main switch were to encounter problems the alternate device is readily available to maintain communication.

The Extended Star Topology allows hundreds of devices to be interconnected and also provides each with its dedicated line. This in turn allows faster transmission of messages across the network as well as desired efficiency.

Cabling is also an important component in terms of how effective communication can occur therefore fiber optic cabling is most suited. It is the most secure, high speed means of long distance data transmission. The cable length allows devices to be connected over large locations, meanwhile maintaining the connection signals for timely and precise data transmission.

### Internet Services

### Digital Subscriber Line

Digital Subscriber Line (DSL) is a type of high speed internet connection which makes it possible to connect to the internet and use telephone line at the same time. This type of connection can encode more data, therefore allowing individuals to have faster and stronger connection speeds ranging between 128Kbps up to 8Mbps.

Leased Lines

According to Network Magazine India, Issue 2001, Leased lines are dedicated circuits provided by Basic Service Providers (BSPs), which provide permanent connectivity to the Internet. The line directly connects the user to the premises of the Internet Service Provider. The connection is secure, private and generally reliable and provides a much faster bandwidth speed. It also experiences less interference like other connection types.

### Wireless Internet Connections

Wireless Internet allows devices to connect to the internet through radio frequency bands. The computer's adapter transmits a signal using an antenna, which is picked up by an available wireless router. Once the signal is received it decodes the data and sends it to the internet through a physical wired Ethernet connection.

Wireless speeds range between 384Kbps to 54Mbps, however connection transmission is determined primarily on an individual's proximity to a router.

### Cable

A cable internet connection provides a connection to the network through the same type of cabling used to provide television cable channels. Signals are sent along the cables and reaches and connect to the devices through a cable modem. The cable modem is used to separate the digital data from television signals. A coaxial cable is the attached to the modem which activates internet connection.

Telecommunications Services of Trinidad and Tobago (TSTT) offers a wider range of services at the most affordable prices. They provide DSL broadband, dial-up, wireless and leased line services to corporate establishments. Prices vary based on the packages chosen and the length of the contracts.

Flow and Carib-Link are two new internet service providers which provide competition against TSTT however, they do not provide as wide a variety of internet communication services. Flow and Carib-Link both offer DSL broadband services only.

### Recommendation

The Internet Service Provider whose services will be most appropriate to implement within the police department would be those offered by Telecommunication Services of Trinidad and Tobago (TSTT). TSTT has a wider variety of corporate services to choose from such as DSL, Wireless and leased lines at lower rates than its competitors. It also provides services that aren't available from other providers.

The most suitable service which can be implemented for the police department would be a combination of the leased line service and DSL. Leased line connections are considered the best choice since the internet provider can supply a dedicated line from its establishment to the police headquarters.

The private internet service allows internet access on a 24hr basis, and allows only devices incorporated under that specific network to have access. The fastest speed offered is 1544Kbps which cost about $4,988 a month.

DSL can also be incorporated into the police station because it allows for an even faster and larger bandwidth for transfer of data. The largest bandwidth allows 6Mbps down and 768 Kbps up. This speed is greater than the leased line and can therefore communicate larger volumes of data at even greater speeds. This DSL speed cost about $5249 per month.

TSTT's services are much cheaper and its speeds are much faster than the competitors therefore this combination becomes the determining factor for which service provider is better suited.

### Full Duplex

Full Duplex transmission makes it possible for communication between devices to occur simultaneously. This suggests that communication can occur at the same time, in both directions without any interference.

In a full duplex communication system, transceivers located on the same intermediary channel make it possible to transmit and receive frequencies. As frequencies are sent a network frequency converter divides the bandwidth of the data into a single sideband, one of which is used for sending and the other for receiving data.

The intermediary channels used to send data include connections that are wireless, or through cabling such as coaxial or twisted pair. If a coaxial type of cabling is used it is necessary to install two cables to create a full duplex connection. If twisted pair cabling is used, it contains four separate wire pairs within a single sheath, one of which is dedicated to incoming traffic and one to outgoing traffic.

Wireless frequencies in full duplex allows data to be converted into radio signals which are then transmitted using an antenna, once the receiving device has obtained the signal, it is decoded. The type of frequency determines heavily how much data can be sent at a time.

### Half Duplex

Half Duplex communication allows communication to occur between two devices, however not at the same time. In this type of communication if data is being sent from one user, the other must wait until they have received the data and transmission has completely stopped before data can be sent back.

Half Duplex systems use the entire bandwidth of the channel as it either sends or receives data. The communication process is generally time consuming because of the time delay between sending and receive data. However, it is much cheaper and requires less cabling compared to full duplex since both transmission and reception of data occurs on the same cabling.

### Legal Requirements

The Telecommunications Act of Trinidad and Tobago is responsible for granting licenses to authorize the operation or use of any radio-communication service or any radio-transmitting equipment, which can include that on board any ship, aircraft or other vessel in the territorial waters or airspace of Trinidad and Tobago.

In order for the Police Department to impose any type of operating systems within the country, they must apply for a license from the Telecommunications Authority of Trinidad and Tobago.

There are three types of licensing categories:-

- Spectrum License - This license allows the licensee to operate radio-communication systems within a specified frequency band on a technology neutral basis.

- Station License - This license allows the licensee to operate the specified station in accordance with technical parameters determined by the Authority.

- Class License - This authorizes persons to use specific radio-communication devices within specific technical and operational parameters, and which would generally apply to low-powered mass-market consumer devices.

The next step requires the establishment to complete the forms with all the required information such as the applicants business or residential address, contact telephone/facsimile number, email address, name of the applicants and be accompanied by all the supporting documentation to be considered eligible.

Once the form has been completed it is submitted to the Telecommunications Authority of Trinidad and Tobago, Ben Court, 76 Boundary Road, San Juan, Trinidad, West Indies. The applicants must also pay fees at this location either by manager's cheque, money order, linx, credit card or cash.

If the application has been approved the establishment usually receives there license within 90 days.

The table below obtained from Telecommunications Authority of Trinidad and Tobago, (http://www.tatt.org.tt/) shows some of Trinidad and Tobago's frequency allocation ranging between, 9KHz to 1000GHz. The left column of the table shows the current ITU-R Region 2 frequency allocations whilst the right column shows specifically Trinidad and Tobago's allocations.

### Limitations of Full Duplex

- It is possible during peak times when communication is occurring for there to be more transmission traffic on the network.

- The control of data flow is difficult since more traffic may move across bridges or switches which it cannot handle.

- It requires twice as many cabling compared to half duplex.

### Limitations of Half Duplex

- Communication occurs on same frequency which allows one party to transmit information at a time.

- Accommodates only a short range distance for communication

- Slow data transfer speeds, between 3 to 4 Mbps of communication speeds.

- Loss of data occurs when the line is busy.

- Data collision is possible

### Recommendations

Setting up voice communication at the police station is a complex task, simply because departments are spread across a general area. There are also certain areas of the police station which are more entitled to receive and transmit information.

Full Duplex communication should be implemented throughout the police departments (Northern, Southern, Eastern and Western) because these departments require high speed reception and transmission of information.

The police officers who patrol on foot and the police cars should all be equipped with devices which enable full duplex communication between them. This is necessary if an emergency occurs, it can be communicated to the various parties immediately.

The ideal unit in which full duplex devices should be fully implemented would be the Serious Crime Squad as well as the unit cars. This area of the police station is involved with dangerous high security and high risk crimes therefore it is necessary that they be able to send and receive large amounts of information at faster rates between sender and receiver.

Full duplex allows for communication to occur over long distances with limited to no interference. It is however more costly to install but definitely more effective when communicating and transferring information.

### Bibliography

### Books

- Tomsho. G, Tittel. E, Johnson.D, 2007, Guide to Networking Essentials, 5th Edition, Galatea Training Services Limited.

### Online

- A guide to Networking, [Online], (Updated: January 26th, 2008), Available from: http://learn-networking.com/network-design/a-guide-to-network-topology, Date Accessed: October 22nd, 2009.

- Network Topologies, [Online], Available from: http://compnetworking.about.com/od/networkdesign/a/topologies.htm, Date Accessed: October 22nd, 2009.

- Networking - Star Topology, [Online], Available from: http://www.exforsys.com/tutorials/networking/star-topology.html, Date Accessed: October 23rd, 2009.

- Advantages and Disadvantages of Different Network Topologies, [Online], Available from: http://www.buzzle.com/articles/advantages-and-disadvantages-of-different-network-topologies.html, Date Accessed: October 23rd, 2009.

- Mini -Tutorial on Network Topologies, [Online], Available from: http://www.antionline.com/archive/index.php/t-228441.html, Date Accessed: October 23rd, 2009.

- Thin Ethernet, [Online], Available from: http://www.maznets.com/tech/10base-2.htm, Date Accessed: October 24th, 2009.

- Ethernet Standards, [Online], Available from: http://k-12.pisd.edu/currinst/network/if2_4st.pdf, Date Accessed: October 24th, 2009.

- Brown B. Networking Fundamentals - Network Topology, [Online], Available from: http://uva.ulb.ac.be/cit_courseware/NETWORKS/pt2_0.htm, Date Accessed: October 24th, 2009.

- Boehlke J, How does cable internet work?, [Online], Available from: http://www.ehow.com/how-does_4569915_cable-internet-work.html, Date Accessed: October 25th, 2009.

- Network Magazine, [Online], Available from: http://www.networkmagazineindia.com/200110/basics1.htm, Date Accessed: October 25th, 2009.

- How Stuff Works, [Online], Available from: http://computer.howstuffworks.com/wireless-network1.htm, Date Accessed: November 6th, 2009.

- Full Duplex Transmission, [Online], Available from: http://www.networkdictionary.com/hardware/fdt.php, Date Accessed: November 6th, 2009.

- What is Simplex, Half Duplex and Full Duplex? , [Online], Available from: http://www.cabledepot.com/05DTHFDUP.html, Date Accessed: November 6th, 2009.