# Machine vision

### Introduction;-

Machine vision (MV) is the application of computer vision . Whereas computer vision is general discipline to make computers to see. Machine Vision is a subfield of engineering that is related to computer science, optics, mechanical engineering, and industrial automation. Machine vision, being an engineering discipline, is interested in digital input/output devices and computer networks to control other manufacturing equipment such as robotic arms and equipment to eject defective products. One of the most common applications of Machine Vision is the inspection of manufactured goods such as semiconductor chips, automobiles, food and pharmaceuticals just as human inspectors. Machine vision systems use digital cameras, smart cameras and image processing software to perform similar inspections.

Computers do not 'see' in the same way that human beings are able to. Cameras are not equivalent to human optics and while people can rely on inference systems and assumptions, computing devices must 'see' by examining individual pixels of images, processing them and attempting to develop conclusions with the assistance of knowledge bases and features such as pattern recognition engines.

Example of machine vision system is:-

### Automated guided vehicle

An automated guided vehicle or automatic guided vehicle (AGV) is a mobile robot that follows markers or wires in the floor, or uses vision. They are most often used in industrial applications to move materials around a manufacturing facility or a warehouse.

Automated guided vehicles (AGVs) increase efficiency and reduce costs by helping to automate a manufacturing facility or warehouse. AGVs can carry loads or row objects behind them in trailers to which they can autonomously attach. The trailers can be used to move raw materials or finished product. AGVs are employed in nearly every industry, including, pulp, paper, metals, newspaper, and general manufacturing. Transporting materials such as food, linen or medicine in hospitals is also done.

Lets see how a system with machine- vision work.

### Components of a machine vision system:-

Hadware and software component used in Machine vision are :-

- For taking image one or more digital cameras.

- Frame grabber which is used as the camera interface for making the images available for processing.

- A processor often a PC or embedded processor, such as a DSP.

- In some cases, all of the above are combined within a single device, called a smart camera.

- Input/Output hardware or communication links to report results.

- Lenses to focus the desired field of view onto the image sensor.

- Specialized, light sources it can be LED illuminators, fluorescent or halogen lamps etc.

- A program to process images and detect relevant features.

- A synchronizing sensor it may be optical or megnatic for part detection .

- Some form of actuators used to sort or reject defective parts.

The synchronizing sensor determines when a part is in position to be inspected. The sensor triggers the camera to take a picture of the part and often synchronizes a lighting pulse to freeze a sharp image.

The lighting used to illuminate the part is designed to highlight features of interest and to minimize the appearance of features that are not of interest . LED panels of suitable sizes and arrangement are often used to this purpose.

A framegrabber is a digitizing device that converts the output of the camera to digital format and places the image in computer memory so that it may be processed by the machine vision software.

The software will typically take several steps to process an image. Often the image is first manipulated to reduce noise or to convert many shades of gray to a simple combination of black and white . Following the initial simplification, the software will count, measure, and/or identify objects, dimensions, defects or other features in the image. As a final step, the software passes or fails the part according to programmed criteria.

Most machine vision systems rely on "black-and-white" cameras, the use of colour cameras is becoming more common. Smart cameras can be used for direct connection rather than a camera and separate framegrabber, which reduces cost and simplifies the system.

### Processing methods:-

Commercial and open source machine vision software packages typically include a number of different image processing techniques such as the following:

- Pixel counting: counts the number of light or dark pixels.

- Thresholding: converts an image with gray tones to simply black and white.

- Segmentation: used to locate and/or count parts .

- Barcode reading: decoding of 1D and 2D codes designed to be read or scanned by

### Machines.

- Optical character recognition: automated reading of text such as serial numbers.

- Gauging: measurement of object dimensions in inches or millimeters.

- Edge detection: finding object edges.

- Template matching: finding, matching, and/or counting specific patterns.

### Applications of machine vision:-

The applications of machine vision in:-

- Large-scale industrial manufacture

- Short-run unique object manufacture

- Safety systems in industrial environments

- Inspection of pre-manufactured objects (e.g. quality control, failure investigation)

- Visual stock control and management systems (counting, barcode reading, store

interfaces for digital systems)

- Control of automated guided vehicles (AGVs)

- Quality control and refinement of food products

- Retail automation.

applications of machine vision are not only limited to these area it has many applications in the other areas.

### Some robots with the machine vision property are as follow:-

### An9-PR Robot:-

Sohgo Security Services Co Ltd, a security company in Japan, will release an autonomous robot that can be used for digital signage. It is an autonomous robot for guidance and advertising The robot, "An9-PR," features a 19-inch touch panel LCD monitor on the front, two 12-inch LCD monitors on the back and a ring-shaped electric bulletin board on the top. The robot is expected to be used in shopping centers, public facilities, etc. For example, it is possible to show a facility guide and advertisements, and visitors can run a search for shop information by using the touch panel.,it has sensor for detecting people and objects around the robot,camera on the top of robot with which robot can take the picture,process and send it to a mobile phone of visitor. Advertisements and guides shown on the monitors can be changed in accordance with the location of the robot.

Also, equipped with a FeliCa reader/writer and an infrared communication function, it is possible to send shop information and coupons to mobile phones compatible with FeliCa as well as to take a picture with the camera, process and send it to a handset. Furthermore, because the images shot by the camera can be checked through LAN, the An9-PR can be used for simple remote surveillance. The robot is 160cm in height and 200kg in mass. It is similar to a cylinder with a circumference of 4m. With four tires at the bottom, it can operate continuously for about an hour. When running out of battery, it automatically goes to a battery charging stand. The maximum movement speed of the robot is 4km/h, but it normally moves at a speed of about 1km/h. Expecting that the An9-PR will be used in crowded places, Sohgo Security Services paid attention to safety. In addition to the range sensor and ultrasonic sensor on the front, the robot has an infrared sensor around its body and can detect people and objects within a distance of about 50cm. Also, it is mounted with a far-infrared human presence sensor.

### AIBO robot:

AIBO (Artificial Intelligence robot) was one of several types of robotic pets designed and manufactured by Sony.Being able to walk, "see" its environment via camera, and recognize spoken commands, the AIBO robotic pets are considered to be autonomous robots, since they are able to learn and mature based on external stimuli from their owner or environment, or from other AIBOs.

### Security Camera Robot:-

coolest security camera robot is little robot can be controlled over the Internet, so you can log into it from work and drive it around your home.Completely wireless, it enables you to view live high resolution video and sound as it roams around your home.It also features a two-way microphone allowing full communication with people or pets in your home. The robot can be programmed to patrol your home in up to 10 predefined paths, avoiding any obstacles using a beam of infrared light. It's equipped with 3 wheels which allow it to turn 360 degrees in the same spot.

The security camera is located on a boom which can be raised for a better advantage point, sending back 640×480 images through an Internet connection. It can also be programmed to periodically email you photos during its patrol.It requires a wireless router to connect to the Internet, which is commonly found in many homes these days. The robot can run up to 2 hours on a single charge.

### Conclusion:-

During the last 15 years machine vision applications crop up in many industries, including semiconductor, electronics, pharmaceuticals, packaging, medical devices, automotive and consumer goods.Machine vision systems offer applications for inspecting and identifying parts, accurately measuring dimensions, or guiding robots or other machines during pick-and-place and other assembly operations.Machine vision must include three characteristics in order to be useful in most manufacturing industries. First, they must be fast enough to keep up with ever-increasing production rates. Second, they must be intuitive and easy to use. Finally, they must be intelligent enough to deal with part-to-part or other process variations.

*************

### Bibliography:-

www.google .com

www.wikipedia.com