# Micro controller based temperature indicator

### A BRIEF INTRODUCTION TO 8051 MICROCONTROLLER:

Single chip that contains the processor (the CPU) is a microcontroller, non-volatile memory for the program (ROM or flash), volatile memory for input and output (RAM), a clock and an I/O control unit.

89s52:

This is a ( AT89S52) is a low-power, high-performance CMOS 8-bit microcontroller with 8K bytes of in-system programmable Flash memory.

The Flash chip or on-chip Flash allows the program memory to be reprogrammed in system or by a conventional nonvolatile memory programmer.

The Idle Mode stops the CPU while allowing the RAM, timer/counters, serial port, and interrupting system to continue functioning. The Power-down mode saves the RAM con-tents but freezes the oscillator, disabling all other chip functions until the next interrupt

The hardware is driven by a set of program instructions, or software. Once familiar with hardware and software, then any user can then apply the microcontroller to the problems easily.

The pin diagram of the 8051 shows all of the input/output pins unique to microcontrollers:

Microcontroller Capabilities:

ROM and RAM( Internal)

I/O ports with programmable pins

Timers and counters

Serial data communication

8051 architecture :

- (DPTR)

- (PSW)

- (SP)

- Internal ROM 4k

- Internal RAM of 128 bytes.

- 4 register banks, each containing 8 registers

- 80 bits of general purpose data memory

- 32 input/output pins arranged as four 8 bit ports:P0-P3

- Two 16 bit timer/counters: T0-T1

- Two external and three internal interrupt sources

- Oscillator and clock circuits

Power Supply Importance:

Power supply plays very important role in any electronic project.

For voltage regulation I am using LM 7805 and 7812 to produce ripple free 5 and 12 volts D.C constant supply.

### DS 1820 Temperature Sensor:

The DS18S20 digital thermometer providing 9-bit Celsius temperature measurements and has an alarm function with nonvolatile user-programmable upper and lower trigger points. The DS18S20 communicates over a 1-Wire bus that by definition requires only one data line (and ground) for communication with a central microprocessor. It has an operating temperature range of -55°C to +125°C and is accurate to ±0.5°C over the range of -10°C to +85°C. In addition, the DS18S20 can derive power directly from the data line (“parasite power”), eliminating the need for an external power supply.

### DS18S20 Block Diagram

PRECAUTIONS while soldering:

- Soldering iron bit should be kept clean with the help of file at time to time.

- The soldering wire should be of smaller thickness.

- We should not use extra solder because it may be a cause of short circuit in the conductive path.

- The components should not be overheated.

- The leads of the components should be clean before soldering, by the send paper.

- The bit of a new soldering iron should be clean properly before soldering.

- The joint should be heated up to required temperature by which, the solder melts and comes around the joint. The joint should not be disturbed before setting the solder. The good joint looks pointed spot.

### b.) DURING USING POWER SUPPLY:

- switches and fuses should be used in a project circuit.

- Earthing is essential in wiring.

- We should use insulated wires.

- Power supply should be switched off, when it is not required.

- If there is a fault in the circuit, then firstly we should repair it. After repairing it connect again the power supply.

### c.) DURING TESTING OF PROJECT:

- Each component should be checked before checking the project.

- Potentiometer should be adjusted at proper range.

- Battery of the testing equipment should be properly checked otherwise it will not measure the actual reading.

- The components, which are not doing function properly, should be changed as soon as possible; otherwise, other components may also be damaged by it.

- Testing equipment should be in proper range when output measured at any point of the circuit, or component. Otherwise testing equipment may be showed the wrong reading.

### LEARNING OUTCOMES:

- Understanding the hardware detail of a 8051 microcontroller

- Microcontroller programming

- 7 segment display interfacing and use of Temperature Sensor

- Introduction to DC motor