# Module based framework for communication in heterogeneous networks

### Abstract

Next generation mobile networks are expected to achieve a high degree of inter-networking so that the mobile users can truly experience ubiquitous access through switching between heterogeneous networks. We mean that the device neither requires user intervention nor does it disrupt the existing session during the radio switching process. IP based networking is the key to turn this vision into a reality. Future clientele devices tend to be equipped with multiple network interfaces. Mobile devices that cater to one type of access technology have the ability to roam among networks of the same type are referred to as horizontal handoff. Seamless access to services between various access technologies such as WLAN, WCDMA, Cellular networks, WiMAX etc, irrespective of the radio technology being used is referred as vertical handoff.

Furthermore, our proposed solution is a data link layer approach to vertical handoff. We develop a module framework that accomplishes the handoff process between various radio interfaces supporting IP. This module addresses seamless, handoff decision & interface selection problems faced during the vertical handoff. The handoff can be achieved at the client devices and there is no need of any handoff agents or servers required. Linux being the fastest growing operating system for wireless devices and the flexibility it offers for the developer makes it the most suitable for the implementation of this solution. This module is implemented at the kernel level that makes the handoff process to be very fast thereby, reducing the latency significantly.

### Introduction

Nowadays there is a gradual trend towards using not only one wireless network, but to utilize all interfaces available on a mobile device. The computation power and storage capability on mobile devices are increasing rapidly, and together with new interactive services this creates a demand for more bandwidth. To keep track of this evolution, the use of heterogeneous networks has gained focus. Heterogeneous Networks means networks of different types. Instead of only using one type of network, it is desired to utilize all interfaces available on a device, and hence choose the one best suited for communication. The challenge in this context will be to provide handoff without user interaction.

On most of the devices today wired and wireless LAN cards have become basic components, apart from supporting other radio access technologies such as Bluetooth, GPRS etc. If these devices are to connect to various networks and perform a continuous data transmission whatever location they roam to, while switching from one network to another, technique of vertical handoff is needed.

### Problem

WLAN, Bluetooth, GSM, WiMAX etc are the various complementary access technologies developed with service intended to cater to different sections of mobile users. Each of these technologies has its own diverse set of standards, protocols and support homogeneous network mobility in their own way. For example, a mobile device can move between Access Points of a WLAN or WiMAX, handoff occurs when there is movement between cells of the same network type. With the current infrastructure and the increase in heterogeneous networks, it frequently possible to have wireless access of one type or another everywhere, yet there is not a single strong architecture, which embraces all these technologies and provides seamless interoperability between these disparate interfaces. Since these wireless infrastructures have developed independently of each other, we now have to integrate them in order to achieve seamless roaming.

There are several key issues that are associated with the implementation of vertical handoff 1) Seamless Continuity 2) Handoff Decision & 3) Interface Selection. First, we have to ensure that the device makes a switch between hardware interfaces to connect to the best available network. In our case, whenever a connection to a WLAN is available, we connect to it and switch to the Cellular Network when beyond the available range of the WLAN. Next, the switching between the networks has to be transparent to the user. The wireless user should not have to configure anything for the switch to occur. In the homogeneous network handoff mechanism, the network infrastructure makes it possible for wireless devices to move without disrupting the existing connection. Similarly, heterogeneous network switching should also ensure that the ongoing session is maintained. We have to make sure that the switching is fast enough so that the user connection is kept intact at the TCP layer.

### Assumption

Existing devices cannot incorporate unlimited number of interfaces and so we restrict the experiment to have two different networks interface cards 1) Ethernet NIC 2) WLAN NIC each having the same IP address. It is also assumed that the proposed architecture also suits different network interface cards supporting IP. We use a 2.6.32 version of the Linux Kernel that is suitable for running on a Laptop or an embedded device with higher computing power.

### Related Work

Today, there is a significant trend toward using not only one wireless network, but to utilize all carriers available on a mobile device. In addition, for real-time applications like voice, it is desired to make a seamless change of network without user interaction. To keep track of this evolution, the use of heterogeneous networks has gained focus. Instead of only using one type of network, it is desired to utilize all carriers available on a device, and hence choose the one best suited. Furthermore it is proposed an application-layer handover scheme for session continuity in heterogeneous networks [3]

Conducting the handover process at a higher layer can provide providing transparency to the heterogeneous seamless handover. By that way, efficient handover decisions for vertical handover are made with more number of constraints that will lead to high performance, accessibility and low cost. Making this possible is by providing Quality of Experience (QoE) and obtaining current information of the throughput by measurements in the network. Analyzing and interpreting the statistics collected through measurements are vital in terms of decision-making and to decide when to perform vertical handover. This project consists of the implementation of measurement module in two different approaches (Payload Dependent Approach and Payload Independent Approach) that will provide these statistics to the storage module in PERIMETER project. [1]

Now a days mobile devices support several interfaces although the protocol stack used in each interface tends to be interface specific at the lower layers. This limits the ability of a device to switch back and forth between networks as need and opportunity dictates. As a step towards providing a more flexible handover infrastructure, this project addresses the issue of integrating heterogeneous, mobile ad-hoc networks that use different MAC layer protocols. The goal is to provide an end-to-end communication abstraction that hides heterogeneity. [2]

Another solution is to introduce handoff servers to realized vertical handoff. In USHA [4] system, all mobile hosts connect to the Internet with the help of a handoff server, which is equipped with multiple network interfaces with heterogeneous physical properties. Hence, mobile hosts can communicate with the handoff server in various physical connections. The IP tunneling technique (IP encapsulation) is used in USHA with the handoff server functioning as one end and the mobile host as the other. Upper layer communications are bounded to a virtual interface - the tunnel interface, instead of physical interfaces. All data packets are transmitted through this IP tunnel. When the handoff event occurs, the underlying physical connection of the virtual tunnel is automatically switched to the new physical interface. In the meantime, the mobile host also notifies the handoff server of its change in physical connection. However, USHA tries to keep the upper layer TCP connection during the vertical handoff, and then the data packets can only be transmitted using UDP connections between mobile hosts and the handoff server. This causes new problems. In addition, similar to the mobile IP scheme, the handoff server may be overloaded, as the network scale is getting large.

### Proposed Architecture

Across heterogeneous networks, when a user is in roaming state and still wishes to maintain all active sessions, an automatic handoff mechanism is needed to change the communication flow and the physical radio interface in use. This mechanism also needs to address the issue that handoff to be achieved without changing the IP address of the mobile host device. This means that all the handoff processes need to be completed below the network layer in the TCP/IP network stack. Then, under an infrastructure network, the gateway should be notified of the handoff events so that it can adjust the communication flow for the incoming packets. Moreover, the handoff mechanism should be user unaware, so that the handoff process can be handled smoothly.

Figure [] provides a high-level view of the Linux network stack. The top most layer is the application layer, which defines the users/clients of the network stack. The next layer, responsible for peer-to-peer communication is the transport layer. Below the transport layer is the network layer, which is responsible for forwarding packets to their destinations. At the bottom of the stack is the link layer. The link layer refers to the device drivers providing access to the physical layer mediums, such as serial links or Ethernet devices or WLAN devices etc [5]. Now, depending on the active device drivers the link layer chooses the NIC card through which packets have to be transmitted. This NIC card is bound till the session is completed. The problem we face here is that during the vertical handoff there needs to be a switching between different NIC cards depending on the availability of the active cards. Currently the linux network stack doesnot have a support for vertical handoff.

Our proposed solution is a data link layer approach to achieve vertical handoff. We develop a module framework that accomplishes the handoff process between various radio interfaces supporting IP. We integrate our handoff module directly into the Linux kernel. It consists of two sub modules 1) Decision Maker 2) Interface Selector. Firstly, the decision maker module takes decisions when to perform a handoff. Secondly the interface selector chooses the best interface through which packets can be transmitted and received.

During the packet transmission, all the packets from the applications are directed to our vertical handoff module. These packets are then put forward to the interface chosen by the interface selector module. Then the respective packets are transmitted through this interface. But, when the decision maker module suggests for a handoff, the interface selector sends an ARP packet that contains the IP and MAC address of the newly selected interface to the immediate node. The immediate node will then update its ARP table with the new MAC address.

The proposed handoff process can be achieved directly at the client devices and there is no need of any handoff agents or servers required. This module is completely implemented at the kernel level of the Linux operating system that makes the handoff process to be very fast thereby, reducing the latency.