# Most WLAN hardwares

Most WLAN hardwarehas gotten easy enough to set up that many users simply plug it in and start using the network withoutgiving much thought to security.Nevertheless, taking a few extra minutesto configurethe security features of your wireless router or access pointis time well spent.Here are some of the things you can do to protect your wireless network:

- Secure your wireless router or access point administration interface

Almost all routers and access pointshave anadministrator passwordthat's neededto log into the device and modify any configuration settings. Most devices use a weak default passwordlike password or the manufacturer's name, and some don't havea default password at all.As soon as you set up a new WLAN router or access point, your first step should be to change the default password to something else. You may not use this password very often, so be sure to write it down in a safe place so you can refer to it if needed. Without it, theonly way to access the router or access point may be to reset it to factory default settings which will wipe away any configuration changes you've made.

- Don't broadcast yourSSID

Most WLAN access points and routers automatically and continuallybroadcast the network's name, orSSID (Service Set Identifier). This makes setting up wireless clients extremely convenient since you can locate a WLAN without having to know what it's called, but it will also make your WLAN visible to any wireless systems within range of it.TurningoffSSID broadcastfor your networkmakes it invisible to passers-by (though it will still be detectible by WLAN sniffers).

- EnableWPA encryption instead of WEP

802.11's WEP (Wired Equivalency Privacy) encryption has well-known weaknesses that make it relatively easy for a determined user with the right equipment to crack the encryption and access the wireless network. A better way to protect your WLAN is with WPA (Wi-Fi Protected Access). WPAprovides much betterprotection and is also easier to use, since your password characters aren'tlimited to0-9 and A-Fas they are with WEP.A more recent version, WPA2, is found in newer hardware andprovides even stronger encryption.

- Remember that WEP is better than nothing

If you findthatsome of your wirelessdevices only support WEP encryption (this is often the case withnon-PC devices like media players, PDAs, and DVRs); avoid the temptation to skipencryptionentirely because in spite of its flaws, using WEP is still far superior to having no encryption at all. If you do use WEP, don't usean encryption key that's easy to guess like a string of the same or consecutive numbers.Also,although it can be a pain, WEP users should changeencryption keys often-- preferablyevery week.

- Use MAC filtering foraccesscontrol

Unlike IP addresses,MAC addresses are uniqueto specificnetwork adapters, so by turning on MAC filtering you can limit network access to only your systems (or those you know about). In order to use MAC filtering you need tofind (and enterinto the router or AP) the 12-character MAC address of every system that will connect to the network, so it can be inconvenient to set up, especially if you have a lot of wireless clients or if your clientschangea lot.MAC addresses can be "spoofed" (imitated) by a knowledgeable person, so while it's not a guarantee of security,it does add another hurdle for potential intruders to jump.

- Reduce your WLAN transmitter power

you won't find this feature on all wireless routers and access points,but someallow youlower the power of your WLANtransmitter and thus reduce the range ofthe signal. Although it's usually impossible to fine-tune a signal so precisely that it won't leak outside your home or business, with some trial-and-erroryou can often limithow faroutside your premises the signal reaches, minimizing the opportunity for outsiders to access your WLAN.

- Disableremote administration

Most WLAN routers have the ability to be remotely administered via the Internet. Ideally, you should use this feature only if it lets you define a specific IP address or limited range of addresses that will be able to access the router. Otherwise, almost anyone anywhere could potentially find and access your router. As a rule, unless you absolutely need this capability, it's best to keepremote administrationturned off. (It'susually turned off by default, but it's always a good idea to check.)

http://www.practicallynetworked.com/support/wireless_secure.html