# Necessary to discuss

### PATA (parallel ATA):

### Introduction:

Before discussing about the parallel ATA, it is necessary to discuss about one important term "ATA". It is the abbreviation for Advanced Technology Attachment and is the official name for IDE (Integrated drive electronics) given by group X3T10 under American National Standard Institute and uses the IDE technology. It is also referred by the name AT attachment.

It is most often misunderstood that ATA and IDE are different but they both refer to the same, an external electronic controller attachment that integrates the controller of the device from within the device. It's an interface for the connection of storage devices such as hard disks, CD-ROM in computers, it is preferred to install internally due to its short cable length.

The ATA technology was first invented by Compaq in 1986 and was developed later with the help of other groups like Western Digital (WD), Imprimis and Conner Peripherals. ATA technology was standardized in 1988 and final version was released in 1990.

After the release of first version of ATA by X3T10, many amendments were made to the then existing technology and different standards were released with bandwidth and Ultra DMA modes as main areas of improvement. The other versions include ATA-2 which is also referred as Fast ATA, ATA-3, Ultra-ATA (version in which support to ultra DMA modes was introduced), ATA/66, ATA/100 and ATA-7 (ATA/133).

Parallel ATA or PATA is the other name for ATA. After the development of Serial ATA technology in 2003, ATA devices are renamed as Parallel ATA (PATA) devices to show the variation between the two.

The other versions in ATA-4 and ATA-5 standards are not given as the bus speeds are less than their previous versions.

### 2) PATA Timing diagram

### 3) PATA Pin diagram

The ATA cable consists of 2or 3 pins of which one is male pin which is connected to the controller and peripherals and the rest female pins. Both the pins consist of 40 pins each with slight modifications. Fig 4 and Fig 5 shows the pin layout of male and female pins respectively. The pin functions for both male and female pins are same and the data transfer between the pins is carried out in parallel.

### 4) Functions of various pins

Basic PATA uses 5 address signals, two read/write signals, a16 bit bi directional bus and an interrupt signal, and these signals are used to access the two blocks of 8-bit registers and one 16-bit register in the ATA or ATAPI device. These registers are used to send command to a device, to receive status from the device and to transfer data in what is called PIO mode. Most PATA implementations also support a data transfer mode called DMA, DMA requires two additional signals. There are two DMA protocols: the old ISA Multiword (MW) DMA and the newer Ultra DMA.

The ATA devices are connected to the IDE interface by use of PATA cable. As per the ATA standards, the maximum cable length should be 18 inches or 46 cms. This allows the connection of devices inside the unit. The data transfer is carried out by 40-wire ribbon cable to which the male and female pins are connected. With the advancement of technology and higher data transfer speeds, a new cable with 80 wires was introduced from ATA-5 standard. Fig 6 shows the thickness of wires in 40 wire and 80 wire cables for PATA devices.

The major difference between 40-wire and 80-wire cable is the thickness of the cable which is reduced to fit in 80 wires. Though 80 wires, the pin layout remains the same with 40 wires attached to the 40 pins and the rest to ground to minimize the effect of cross talking that occurs during high rate of data transfer speeds. PCMCIA PC Card ATA or Compact Flash is another popular interface used by ATA devices.

### 5) Procedure for Installing PATA hard drives:

- Plan the installation: Decide which drive bay and IDE controller and ribbon you will be using, and any Master/Slave configuration.

- Configure drive jumpers: Set the drive jumpers to Master, Slave, Cable Select, or single.

- Mount the drive: To mount the drive, slide it in to the drive bay, lining up the front end of the drive with the front of the bay, you may need to use screws to hold the drives in place. You can install a3.5" drive in to a 5.25" drive bay , by using a 5.25" to 3.5" rail mounting kit .

- Connect to the drive interface: Connect the ribbon cable to the IDE interface and to the drive

- Connect to the power supply: Connect the power cable to the power supply

- Power up the PC: Reconnect any devices you may have disconnected in order to mount the drive and power on the PC .Confirm that the BIOS recognize the drive.

### SATA (Serial ATA)

SATA is a new transfer protocol for hard drives

- It's an internal storage interconnect designed to replace PATA technology

- Computer bus technology designed for data transfer to and from a hard disk

- Transmits data serially

- Signaling voltage is reduced from 5 volts to 0.5 volts

- Due to above factors cable length is more

SATA has two separate connectors

- One for data lines

- One for power lines

### 1) SATA Hard ware Details

- Supersedes: ---Parallel ATA

- Capacity: ---1.5, 3.0.6.0 G Bit/s

- Style: ---serial

- Hot plugging: ---yes

- External: ---yes (e-SATA)

### 2) Timing Diagram for SATA

Simple asynchronous serial interface

### 3) SATA pin diagram

SATA Signal names are with respect to the host.

### 4) Types of SATA

### SATA/150(150MBps)

- First generation of SATA interfaces

- It Runs at 1.5 Gigahertz

- Its data transfer rate is up to 1.2 Giga bits per second

### SATA-IO

- It provides the transfer rate of up to 3Gb/s ,Increased power management and cable length up to 8 meters

### Features:

- Port multipliers :These devices allow up to 15 SATA devices to use the same bus

- Native command queuing :Instead of having to execute hard drive requests in the order they are received ,SATA drives can respond to sets of commands in the most efficient way

### External SATA (e-SATA)

It is be used as external device replacing USB 2.0 and FireWire bringing the following benefits

- It is up to six times faster than existing storage solutions

- Robust and user friendly

- High performance, cost effective expansion storage

- Up to 2-m shielded cables and connectors

### 5) Procedure for Installing and Configuring SATA Hard Drives

- Plan the installation: Installing a SATA hard drive is virtually identical to installing an ATA Hard drive expect for the following considerations

- Data cable: The SATA data cable is much narrower than the PATA ribbon, and uses keyed connectors. Because SATA does not use Master/Slave configuration, a separate cable is needed for each SATA drive

- Power connector: Serial ATA drives use a specific type power connector that may not be an older power supply. However, you can purchase adapters to convert SATA power connectors to Molex connectors.

- SATA hard drives are hot pluggable: They can be connected to the PC while it is running

### SATA and PATA differences

### Hot -Plug capability

PATA cannot support hot plug drives. Before the failed drive can be replaced, Any PATA based RAID solution requires the host bus in to which the degraded array's RAID controller is plugged to be powered off or the other way is to continue using the degraded array that offers reduced throughout capability. In an enterprise level environment neither of it are accepted, Since 240 availability and high performance are important requirements in a Enterprise level environment which are not met , It is easy to see why SCSI and Fiber Channel that support hot-plug drives have not yielded any ground to PATA in the enterprise space in spite of ATA'S cost advantage. SATA remedies this deficiency with its support for Hot-plug drives.

### Decreased Width and Increased length of cables

Parallel ATA'S introduces the 80-conductor cable with 40 conductive elements serving as ground to reduce cross talk between adjacent signal lines and improve signal integrity. Though the increase in number of conductive elements did not increase cable width over the existing 40 conductor cables due to use of thinner gage wires, the width of these cables nevertheless impeded air flow necessary to cool a server and constrained chassis design. Furthermore PATA limited cable length to 18 inches that prevent efficiency routing of its cables with in chassis to reduce clutter and improve accessibility to components in the system

### Increased bandwidth

The first generation SATA offers a band width of 1.5Gbps using 10bit signaling per byte of data which is equivalent of data byte of 150MB/sec. The SATA road maps envisions two succeeding generations SATA II and III to be completed at approximately three years interval with each generation doubling bandwidth over the preceding one. However the bandwidth 150MB/sec may not be immediately realized with native PATA drives that use dongles, i.e. serial to parallel adaptors to offer a SATA interface. Nevertheless, SATA's bandwidth is designated to scale with that of the mature high end such as fiber channel and SCSI. Fiber channel and SCSI are well positioned to reach the 10 Gbps bandwidth plateau within the next three to four years and SATA will not be far beyond with an offering of 6 Gbps in that approximate line. Conceivably, SATA'S higher order bandwidths may influence host connectivity to entry level external RAID subsystems to be based on SATA itself.

These are remaining differences SATA and PATA:--Enhanced integrity of connectivity, Enclosure management Command, Queuing and reordering, Decreased operating voltage.

### References:--

- http://searchcio-midmarket.techtarget.com/sDefinition/0,,sid183_gci213788,00.html

- http://www.mondofacto.com/facts/dictionary?Advanced+Technology+Attachment

- http://media.wiley.com/product_data/excerpt/00/04700740/0470074000-1.pdf

- http://www.buildorbuy.org/atapi.html

- http://rtfm.vtt.net/pinouts/data/AtaInternal_pinout.shtml.htm

- http://www.allpinouts.org/index.php/ATA_(Advanced_Technology_Attachment)_Internal

- http://www.pcguide.com/ref/hdd/if/ide/z_000524wires4080.jpg