# One of the main concerns

### Chapter 4 XML-based X.509 digital certificate

This chapter introduce X.509 digital certificate and revocation approaches. Based on X.509, this chapter improves it to alleviate the time cost of X.509 certificate validation. An evaluation also has been described to illustrate the efficiency of improved X.509 certificate.

### 4.1 Introduction

One of the main concerns associated with digital certificate is that mechanism for revocation of certificate is required (Nielsen and Hamilton, 2005; Rivest, 1998; Housley et. al, 2002; Liu et. al, 2008; Noor, 2008). Certificate revocation is the action of declaring a certificate invalid before its validity period. There are two major techniques to check validity of a certificate status including Certificate Revocation List (CRL), and Online Certificate Status Protocol (OCSP).

CRL is a list issued and digital signed by a Certificate Authority (CA), which contains the serial number of certificates that should no longer be used after they are expired. This list is dated and also has an expiration date after which user must download a new CRL. However, it is widely recognized that CRLs are too bandwidth and can not provide a good degree of timeliness (Myers et. al, 1999; Micali, 1997, Goyal, 2004; Arnes, 2000; Benjumea et. al; 2007; Wazan et. al; 2008). Several CRL relative approaches have been proposed. Certificate Revocation System (CRS) was introduced by Micali, which enables system to answer the user query with exceptional efficiency (Micali, 1997; Micali, 2002). The main problem with CRS is that it is not suitable in a distributed query answering system. The communication between CA and directory is too frequent, which shoots up the overall bandwidth cost of the system (Naor and Nissim, 1998; Aiello et. al, 1998). Aiello proposed an improvement to CRS aimed at reducing this communication but their approach had several problems (Aiello et. al, 1998). Certificate Revocation Tree (CRT) is the third well-known technique for certificate revocation (Kocher, 1998). Although the CA to directory communication is low, the data volume which needs to be downloaded is still large, so the overall cost of the system is still relatively high.

Another technique for certificate revocation is the Online Certificate Status Protocol (OCSP) designed by IETF (Myers et. al, 1999). In OCSP, the CA simply signs the response to a certificate status query. The protocol requires the security client to send a request to an OCSP responder which is the server returning status information about a specific certificate when asked. Thus, OCSP may provide high degree of timeliness but it is recognized to be non-scalable since the CA is required to compute a signature for answering every query. Furthermore, OCSP has no distributed implementation, i.e., it can not be used in the settings where there should be a number of untrusted directories answering the user query.

Investigation of X.509 digital certificate has demonstrated that traditional techniques for certificate revocation are the bottleneck of a PKI or XKMS system. To alleviate this problem, the thesis proposes a novel idea to make certificate revocation handling and validation easier by using XML signature technology. This thesis focuses on improvement of X.509 certificate based on XML technology. The improved certificate is named as X-certificate. XML signature technology enables a user to sign arbitrary portions of the message. Thus, after the XKMS issued a new certificate each time, and then the certificate owner can add additional information for the latest status of the certificate with his or her signature. Certificate owner's signature is only used to provide evidence for revocation information of the certificate. There is no need to query XKMS or CA for revocation information of such certificate, because the certificate already contains the status information. The proposed approach is an off-line certificate validation service, and it is easy to be deployed. Through evaluation, the approach proposed in this paper has a higher efficiency than existing revocation checking approaches, such as CRL, OCSP.

### 4.2 X.509 certificate

X.509 was initially issued on July 3, 1988 and was begun in association with the X.500 standard by International Telecommunication Union (ITU-T) (ITU-T, 1997). It assumes a strict hierarchical system of certificate authority for issuing the certificates. Version 3 of X.509 provides the flexibility to support other topologies like bridges and meshes. The structure of an X.509 v3 digital certificate in XML format is shown in figure 4.1 (ITU-T, 1997).

### 4.3 XML-based X.509 certificate (X-certificate)

Based on advantages of XML signature technology, this paper makes an improvement on X.509 certificate to improve the efficiency of digital certificate revocation validity. Presented X-certificate consists of two parts, the first is the X.509 digital certificate, and the second is the status information added by certificate owner. The definition for presented X-certificate and relative proof is discussed as follows.

### 4.3.1 Definition for X-certificate

Based on Eq (4.1) and certificate owner's signature, this paper defines the X-certificate in Eq (4.2). The basic idea is that after certificate owner A received from CA, he or she can attach revocation information at the end of to generate new certificate.

Where, is the certificate issued by CA. This certificate provides the binding of entity A to relative public key. "||" denotes the concatenation operator.

- denotes revoked certificates, and . where,denotes the reference number of previous revoked certificates. This information can be got from CA and checked by certificate owner.

- is the time-stamping of certificate signed by certificate owner.

- is a one-way hash function which is used to generate digest value.

- denotes signing function of certificate authority, is the message to be signed, andis the private key. Thus, the Eq (4.2) should include two signatures generated by CA and certificate owner respectively, they only sign information which they are responsible for. This is the new feature of XML signature, it support signing portions of data in the same message.

Based on above definition, when a client holds an entity's certificate, if "Series Number" belongs to, then it is an invalid certificate, otherwise, the client can confirm present status by verifying two signatures without querying a CA or OCSP. If one of the two signatures is invalid, it means the certificate is invalid.

### 4.3.2 Two-party authentication process based on X-certificate

In practice, a digital certificate can be used to encrypt information, or to verify a digital signature. In such application scenario, the paper describes the protocol for authentication and confidentiality of X-certificate as follows.

### 4.4 Evaluation

The evaluation of X-certificate is divided into two parts. Firstly, a size evaluation for message storage overhead of the required data structure is calculated. Secondly, the efficiency is measured by the transferred data volume in revocation.

### 4.4.1 Size evaluation

The size of the data structure required for the certificate management is conformed to (Arnes, 2000; Perlines et. al, 2006), and it is a basis for evaluating the data transferred volume. This paper only computes the size of X-certificate, the other parameters and relative values adopt the result in (Arnes, 2000; Perlines et. al, 2006).

### 4.4.2 Efficiency evaluation

In a real world scenario, a CA can be supposed to manage a range between and users. As the purpose of this evaluation is not to research on PKI with distributed CA, but to evaluate the revocation schemes, thus, the evaluation is based on a system with a single CA. A typical validity period of the issued certificate is one year. For the probability of certificate revocation, this paper take 10%, i.e. the probability that a certificate will be revoked before it expires. Table 4.2 lists the parameters which are measured.

For CRL model, the data volume transferred during one day depends on the amount of users interested in status verification. Eq (4.3) will serve to determine the transferred data volume during this one day (Perlines et. al, 2006).

In the OCSP scenario, parameters to be studied are the amount of data needed for each requesting userassuming that out of users perform such a status request. Consequently, Eq (4.4) describes the data volume generated during one day (Perlines et. al, 2006).

The data volume of X-certificate generated is related to amount of content providersout of offering signed status information as well as to the rate of usersrequesting certificate from certificate owner. Additionally, each user will request the certificate from the certificate owner for each request. Thus, Eq (4.5) shows the data volume generated using X-certificate during one day.

Figure 4.3 shows the data volume transferred during one day for users of 1,000. In a situation of, the OCSP model tends to perform worst in most of the cases. This means the usage of OCSP create the biggest data volume. The CRL model performs better than the OCSP model except for and. X-certificate on the contrary always shows the best performance in data volume transferring, beating all other two approaches.

For users of, the CRL model is obviously the most cost alternative as shown in figure 4.4. The OCSP perform better, and X-certificate shows again the best efficiency because of its simple status information validation process.

### 4.5 Analysis

The discussion criteria presented in this section are based on a list of general criteria from (Perlines et. al, 2006; Arnes, 2000; Adams et. al, 2001; Zhang, 2003).

- Timeliness

The timeliness of CRL depends on the length of the period between the updating. The direct way to improve timeliness for CRL is to short the update period. However, the more often CRL will have to be requested, and the more network load increase significantly. The timeliness of OCSP heavily depends on what approach the OCSP responder is used to gather the revocation information. Even though OCSP provides real-time replies, the revocation information it carried may not be fresh if the OCSP responder acquires its information through the use of CRL or any other cached mechanism. When a certificate has been invalided, the certificate owner is the first entity knowing certificate status. Based on this fact, X-certificate can update status information in time. Thus, when an entity gets an X-certificate from certificate owner, this X-certificate has the latest status information.

- Scalability

This criteria means the scheme itself is scale. Scalability is another challenge for CRL. The CRL of the U.S. Department of Defense (DoD) approached 40MB in 2005 (Nielsen and Hamilton, 2005). Imagine the required bandwidth for each DoD client to download 40MB only for certificate revocation every day. The problem will be exacerbated if some users also have to download external CRLs while external partners have to download the DoD CRL. This enormous task also becomes meaningless when taking into account that as much as 99% of the downloaded information may be completely irrelevant to users because it concerns revoked certificates with which they have no contact. OCSP solved the problem of scalability experienced by CRL, because it requests certificate status on demand and only for specific certificate. The periodic download of large files is no longer necessary. As to X-certificate, the status information has been contained in the certificate content, there is no need to download revocation information, and thus, the X-certificate has a good scalability.

- Security

When revocation information generated, it means that the information is from an authenticated entity, and non-repudiation. As the CRL scheme is 2-party. Only the CA has to be trusted. OCSP is a 3-party scheme, since both CA and the OCSP server have to be trusted. The OCSP server have to be trusted to gather authenticated revocation information and produce correct and digital signed responses to each request. X-certificate also is a 2-party scheme. It provides integrity, authentication, and non-repudiation through two digital signatures. The signature generated by CA ensures the public key and relative identity, and certificate owner's signature provides revocation information. Thus, X-certificate can not only provide the binding of public key to relative identity securely, but also can ensure revocation information not being forged, e.g. prevent man-in-the-middle attack.

- Simplicity

Simplicity means that the revocation scheme is easy to be employed in practice. The CRL scheme is easily managed by adding a new entry to current revocation for each update period and distributed this CRL to its repository. OCSP specifies the behavior of the OCSP server and the OCSP end-entity. However, the management of the OCSP server is a time-consuming task, since the number of server can be quite high. X-certificate only need to register at CA after revocation information has been changed by owner, thus, it will not increase additional service compared to CRL and OCSP.

- Compatible with XKMS

The presented X-certificate is an improvement of X.509 certificate. It still adopt the architecture of X.509 certificate, thus, it can be used as an

### 4.6 Summarize

In order to alleviate the public key revocation management, this chapter presents an X.509 digital certificate based on XML signature technology. The proposed X-certificate contains the latest revocation information. This approach reduces the complexity of XKMS or PKI systems because it eliminates the requirement for additional revocation checking from XKMS or CA, and in consequence, there is no need to provide additional mechanisms such as CRL and OCSP. The evaluation result shows that revocation checking of presented approach has a high efficiency. Analysis shows that X-certificate offers obvious advantages including the ability to leverage the existing syntax of certificate for a new purpose and therefore make CRL and OCSP redundant.