# Pakistan's telecommunication authority to block access to youtube

On the 24th of February 2008, the telecommunications authority of Pakistan blocked access to a popular video streaming site called "Youtube". The 'accident' that took place blocked global access to Youtube servers for approximately two hours. The cause of the entire mayhem was due to an anti-Islamic video that caused a public outcry in a country such as Pakistan. Thus, PCCW, Pakistan's telecommunication authority inadvertently blocked access to youtube. This report will focus on the detailed cause of the actions that took place, the methods that were implemented, the impact that was brought about, and finally the steps that administrators at Youtube has taken to prevent such cyber disasters from happening.

### Background of Case

Pakistan initially blocked the access to Youtube, a popular video streaming website, on 24th of February 2008 due to a rather offensive anti-Islamic content that was seen by its viewers. The anti-Islamic video was reportedly a trailer to a film directed by a Dutch politician Geert Wilders which depicted a pig underneath the word "Allah" (Sigel,2008). Of course, widespread violence was not limited to just Pakistan but eventually in other Muslim countries that found caricatures of the Prophet as a violent man to be extremely offensive. In order to quell or reduce the protests and backlash from the protestors "evidently, PieNet took this step to enforce a decree from the Pakistani Government that ISP's must block access to YouTube because it was a source of blasphemous content" (Stiennon, 2008). Initially in 2006, Pakistan was rocked by a violent wave of protests nationwide in response to the blasphemous caricatures of the Prophet Muhammad that was printed in the Jyllends Posten, a Danish newspaper (Pennington, 2006).

### Explanation of Approach and Impact

Pakistan's Telecommunication Authority(PTA) received an order from the government to block all access to YouTube in response to the offending clips. In essence, PTA began to advertise a false route to YouTube (208.65.153.0/24) which in specific terms is a much more detailed route than the one used officially by YouTube (208.65.152.0/22)- (208.65.155.255) globally. In layman terms, Pakistan claimed that YouTube was located on their network in order to block the access. According to Daneil Karrenberg, a RIPE NCC Chief Scientist, "Misconfigurations of iBGP (internal BGP the protocol used between the routers in the same Autonomous System) happen regularly and are usually the result of an error" (Marsan, 2008). The BGP (Border Gateway Protocol) is a network of ISPs that have a list of similar routing policies. There are eventually two types of BGPs that exist: external and internal. External BGPs allow routing between many different ASes or ISPs. Internal BGPs are mainly used to route traffic between similar networks such as universities or businesses. BGP calculates the best route to a destination by various factors such as weight, local preference, origin, AS_path, and next hop ("Border Gateway Protocol", n.d.). In traditional BGP routing, anything with a subnet of /25 or greater are filtered because most routers do not recognize the larger prefixes. Pakistan's network propagated a route for YouTube with a subnet of /24 which is a specific route. Thus, routers would rather send traffic to the specific route as announced by PT (Brown, 2008, February 24). To explain the entire routing procedure involved, when you type in an address such as www.bbc.co.uk, it is converted into a numeric address (also called an IP address) by the DNS (Domain Name System). This is then transferred to the router which inexplicably builds a routing table that figures the next hop address to which the packet should be sent (McCullagh, 2008, February 25). This packet is sent through AS's (Autonomous Systems) which are a system of networks that "appears to other ASes to have a single coherent interior routing plan, and presents a consistent picture of the destinations that are reachable through it" (Meinel 2008). Multiple prefixes are resolved when looking up www.youtube.com which has a prefix range of /24. However, in order to successfully block access to a site, either one of two things should be done: block all the inbound and outbound traffic from a particular IP address and the latter would be to route all traffic to a 'black-hole'. To begin, Pakistan builds a routing table with the /24 prefix that points to YouTube addresses (Balakrishnan, 2009).

Unfortunately, Pakistan's Telecommunications Authority broadcasted the false route for YouTube by injecting a route where YouTube was not hosted using a small network portion from a list of legitimate IPs (Meinel 2008) which was then advertised to PCCW , a Hong Kong based communications and upstream provider for Pakistan, which then began transferring global traffic of any YouTube requests to Pakistan's IP for YouTube (Hunter, 2008). According to a detailed technical description recorded by Martin Brown's blog, PCCW (AS path of 3491) advertised PT's route (208.65.153.0) as it was not verified to be a false route. Typically, most service providers would validate the route before propagating it. As a result of the invalidation sequence, PCCW began propagating the invalid route (Brown, 2008, February 24).

A much more detailed timeline has been adopted from Martin Brown's Blog:

By inference we see that the PCCW carries Pakistan Telecom's advertisement for YouTube (17557). In less than a minute, after propagation of false network by PCCW, several providers became infected. It's seen that many AS's have been hijacked and it takes YouTube approximately 80 minutes before it propagates its own route 36561. Until then, most of the traffic still flows into PT as it's the nearest and most preferable route. We can see that around a total of 97 ASes have been infected with the hijacked route. However, after YouTube propagates is specific prefix of 208.65.153.0/25, routers, in less than a minute, drop the bad route from the routing tables and adopt the subnet route of /25 as a preferable route. In accordance, the hijacked route is taken out from PCCW's routing tables and PCCW disconnects PT from the internet until it can fix the damage. The time between maximum impact and the start of the hijack spans almost one and a half minutes. It can be noted that PCCW did not validate PT's advertised route, which is necessary to check if the route is valid and thus was the cause of the routing mayhem that we can see above. Since Pakistan depends on its upstream provider, in this case PCCW, to manage the connection to the internet, routing changes are more or less difficult to notice within the network in comparison to the changes that are made outside the network (Meinel 2008). In addition, the main reason that the routers carried the hijacked route was because of the specific /24 prefix which was advertised to other neighbors (Balakrishnan, 2009).

### Preventions Plans

As we see from the timeline above, we can interpret from the timings that YouTube sprung into action as the routes were hijacked. The first line of defense that YouTube initiated was attempting to announce an identical IP address with the same prefix as the one that Pakistan Telecom announced (208.65.153.0/24). However, owing to the fact that since both IP addresses were exactly identical, and according to the BGP policy, the shortest path to the destination must be taken, and in this case Pakistan Telecom was still 'hosting' YouTube and accepting traffic. In the second stage, YouTube starts to announce a more specific route (208.65.153.128/25) and (208.65.153.0/25) to direct traffic back to its servers. Due to the longest match prefix policy, which states that address with the highest subnet mask, is the more preferred route. Therefore, in this case, YouTube's subnet was /25 in comparison to PT's subnet which was /24 and is "less visible on the Internet than the /24 prefix" (YouTube Hijacking: A RIPE NCC RIS case study, 2008). YouTube added an even more specific additional broadcast claiming just 64 addresses--which, under the Border Gateway Protocol, is more specific and therefore should overrule the Pakistani one (McCullagh, 2008). Thus, by policy more routers started to divert traffic back to YouTube as per greatest prefix.

In reality, however, YouTube could only implement a more specific prefix in order to allow other routers to update their routing tables for the proper address. The technique that YouTube used to mitigate the hijack session was "lifesaver" scheme. This procedure involves "shortening the real routes through condensing the entire AS path into an AS_SET" (Oliviera, Lad, & Zhang, 2008). As mentioned earlier, YouTube was seen advertising a specific prefix. Unfortunately, this won't constitute on a long term basis as iBGP (internal BGP) errors can cause an internet routing mayhem. In order to protect against this incident that took place, there are various ways defend against prefix hijacks. One such way is to "protect the routes to top level DNS servers by letting each router observe the origin ASes and AS over time, and deferring the adaption to any sudden route changes until the changes can be verified" (Oliviera et al, 2008). In PGBGP (Pretty Good BGP), ASes are monitored by routers using the PGBGP routing system in order to detect each prefix and filter out new prefixes. The PGBGP system verifies the origin of the route before accepting the route change. In the mean time, the new prefix is given a low local preference while verification exists. In low local preference, alternate routes are given more priority than the new route (Oliviera et al, 2008). In this incident, it's almost certain that a secure BGP policy or routing system is necessary. S-BGP (Secure-BGP) is probably one of the major solutions in safe guarding against trusting BGP routes very easily. S-BGP, just like PGBGP, certifies and authorizes the new routes before implementation. Unfortunately, this solution comes with an upgrade cost to boost the power needed to certify and authorize the route changes (Hruska, 2008). S-BGP is followed by a couple procedures that includes certificates to "enable routers to validate the authorization of other routers to represent ISPs" (Kent, 2008). S-BGP incorporates a public key infrastructure which is a certificate that is given to ISPs that own an address space or prefix. "Certificates issued under this PKI also represent the binding between an ISP and the AS numbers allocated to it. The PKI allows each ISP to issue certificates to its routers, certifying that these routers represent the ISP and hence, the ASes owned by the ISP" (Kent, 2008). In the incident that surrounded YouTube's two hour demise, as PT had added their own address space to block YouTube, this was certainly a misconfiguration that passed unnoticed by PCCW.

### Conclusion

In this report we have outlined the cause of Pakistan's Telecommunication Authority to block access to YouTube due to the blasphemous anti-Islamic clips that were published on YouTube on 24th of February 2008. The clips come as a reprisal after the recent offensive caricatures of the Islamic Prophet published in a right-wing Dutch Newspaper that sparked widespread violent protests. The command to block YouTube was enforced by the Government of Pakistan on Pakistan Telecom. However, in order to block YouTube, PT advertised a false route that allowed all the traffic that goes to YouTube to enter a blackhole. This was rather a misconfiguration in the BGP routing policy that because PCCW did not validate the route, all other ASes started carrying the hijacked route. It was only till later on that YouTube initiated a more specific prefix (208.65.153.128/25) which caused all other routers to drop the hijacked route and prefer this one as it is more specific. We investigated that BGP is not as trusted as it is in this current age of hackers and network mishaps. However, in short term prevention, YouTube increased their prefix from /22 to /25. In the long term scenario, it seems that ISP and providers need to implement a more secure BGP protocol and routing policy. Such prevention mechanisms exists such as : PGBGP and S-BGP. PGBGP quarantines the new route change while it is being validated and S-BGP issues authorization certificates to allow validation of the new route change. It is certain that if PT's upstream carrier, PCCW, had implemented or validated the route changes advertised by PT itself using S-BGP or PGBGP, then there wouldn't have been an internet mayhem.