# Performance evaluation of CDMA

### 1. Introduction

CDMA is a 3G Multiple Access technique. Its gives: - high data rates, high tolerance to multi-path fading, orthogonality, security and no interference. In CDMA each user data is spread many times by multiplying its assigned Walsh code. Hence the power of the spread spectrum signal is spread over 100 - 1000 times the original bandwidth [1]. Consequently, the magnitude of the power exceeds the maximum amplitude of the PAPR [2]. These high peaks or amplitude tends to reduce the efficiency of the Power Amplifier (PA). Since the PA works properly in its linear region, so it is necessary to decrease the high peaks [6, 7, 8]. Therefore, to lower the values of the high peaks, error correcting codes needs to be added to the message. There are codes available for the PAPR reduction [3, 4, 7, 8, 9, 10] and measurement [2, 6] respectively.

### 2. CDMA System

In CDMA multiple users share the same frequency band simultaneously. It uses spread spectrum technique, which provides high data rates to enhance the signal bandwidth far beyond the requirement for a given data rate. Each user has its own code words, which is approximately orthogonal to other code words. This feature makes the system bandwidth efficient and no interference among the users. Each user's data is secured, because of unique assigned code. Spread spectrum also resists to multi-path problem [4, 5].

Block diagram of CDMA system is shown in figure 1 [4]. Since the human speech is in the analog signal, so it has to be first converted into digital form. This function is performed by the source encoding module.

After the source information is coded into a digital form, redundancy needs to be added to this digital message or data. This is done to improve performance of the communication system by enabling the signal to better withstand the effects of channel impairments, such as noise and fading. The goal of channel coding is, reliability or alternatively, given an achievable , to reduce the probability of error, but the trade off is more bandwidth.

Redundancy is implemented in the form of bits, which are also called Error-correcting codes, when these codes applied to channel coding improve the error performance of the system. The purpose of the added bits to the message or data, is that if the receiver found erroneous data, so it should be corrected [4].

After the message or data has been channel coded for error control, the signal is further transformed to allow access to multiple users. Multiple access by different users means to the sharing of a common resource i.e. RF spectrum.

### 2.1 Generation of Walsh Codes

In order to avoid mutual interference on the uplink, Walsh codes are used to separate individual users while they simultaneously occupy the same RF band. Walsh codes as used in IS-95 are a set of 64 binary orthogonal sequences. These sequences are orthogonal to each other, and they are generated by using the Hadamard matrix. Recursion is used to generate higher order matrices from lower order ones; that is [4],

Where contains the same but inverted elements of . The seed matrix is

### 2.2. Modulator

BPSK is the simplest type of PSK (phase shift keying) as shown in Figure 2 [4].

1, it will transmit a negative co sinusoid [4]. The analytic expression for BPSK is1, it will transmit a positive cosinusoid; whenever the transmitter wants to send a It uses two phases of difference 180° (0° and 180°). It is, however, only able to modulate at 1 bit/ symbol. Let's examine its performance in a Gaussian noise environment. The concept is simple. Whenever the transmitter wants to send a

### 2.3 Demodulator

The purpose of the BPSK demodulator is to recover the original signal. The demodulator procedure is based on the matched-filter approach. In this approach the buried signal is extracted from the noise. The received signal has two components: the originally transmitted signal where 1; and noisecould be either +1 or - , which has been introduced by the channel. The received signal is multiplied by the reference signals +1 (that is. The multiplied result is then integrated over one bit interval T [4]. If the transmitter sent a ), then the integrated result is

Where the first term is the signal term that is utilized by the decision threshold to make the decision and the second term is the noise contribution. In the absence of noise, we see that the first term reduces to [4]

### 3. PAPR as measure for CDMA

As mentioned in earlier discussion that the high peaks degrades the performance of the CDMA. Therefore, a measure should be devised in evaluating the performance of the CDMA system. One such measure is called PAPR, which can be formulated as follows [11]

Where is the peak power and is RMS value.

### 4. Using codes to reduce PAPR

As discussed in section 1 that codes are used in the form of redundant bits which when are added to the message, provide reliability with lower power level. The objective of PAPR reduction can be obtained from the following formula:

### 5. Simulation results

In this section some results are present, which showed the performance of CDMA system. In simulation, Walsh code of 64-bit length, M-ary=8, and hamming code has been used. Figure 3 shows correlation coefficient between time and probability of error verses coded PAPR. Graph reflects that optimized values of coded PAPR and Correlation Coefficient (i.e., 4, 16) respectively at high coded PAPR there is a less value of correlation coefficient, which means PAPR is a measure for CDMA system.

Simulation result of graph shown in Figure 4 also reflects that using hamming code PAPR is reduced from 35dB to 4dB. There is a separate graph of PAPR coded verses error rate as shown in Figure 5.

### 6. Conclusions

In this paper the performance of CDMA system has been studied in terms of power measurement and reduction. It reveals that high peaks degrade the CDMA efficiency. However, good measure such as PAPR and codes to reduce PAPR are available. There are some open issues in this area, which need to be investigated like error correcting codes such as BCH, Reed Muller, Golay etc., may be used to reduce PAPR further to 1 dB [9].

### References

[1]. Raymond L. Pickholtz, Fellow, ZEEE, Laurence B. Milstein, Fellow, ZEEE, and Donald L. Schilling, Fellow, ZEEE "Spread Spectrum for Mobile Communications" IEEE TRANSACTIONS ON VEHICULAR TECHNOLOGY, VOL. 40, NO. 2, MAY 1991 313

[2]. R. Neil Braithwaite "Using Walsh Code Selection to Reduce the Power Variance of Band-Limited Forward-Link CDMA Waveforms" IEEE Journal on Selected Areas on Communications, VOL. 18, NO. 11 NOVEMBER 2000.

[3]. Tony Ottosson "Precoding in Multicode DS-CDMA Systems" 1997 IEEE

[4]. Samuel C. Yang: "CDMA RF SYSTEM ENGINEERING", Artech House, INC, 685 Canton Street Norwood, MA 02062, 1998

[5]. Theodore S. Rappaport: "Wireless Communication, Principles & Practices", 2nd Edition, Pearson Education, 2002

[6]. Ali Behravan & Thomas Eriksson "PAPR and Other measures for OFDM Systems with Nonlinearilty,"