### Power Over Ethernet

PoE (Power Over Ethernet) is defined by the IEEE standard 802.3af and was approved by IEEE in 2003 (PowerOverEthernet Staff, 2003). PoE involves sending power along with data over an Ethernet twisted pair wire for the purpose of powering devices without actually providing an extra power supply cable. In this paper I will briefly explain the hardware and layout of this IEEE standard and discuss the potential cost savings that can be realized from choosing to install a PoE device which requires one Ethernet cable over installing a standard network device that requires an Ethernet cable and a power cable.

IEEE standard 802.3af calls for 48 volts DC to be available on 2 of the 4 twisted pairs of an Ethernet cable for the purpose of powering a device (Coleman & Wescott, 2006). The 48 volts is delivered by a PSE (Power Sourcing Equipment) to a PD (Powered Device). The PSE can provide power to the twisted pair cable either at the beginning (defined as Endspan) or between the PSE and PD (defined as Midspan). The Endspan and Midspan PSE's are also referred to as injectors. The Endspan method basically means that there is a hardware device such as a PoE capable switch at the beginning of the twisted pair cable. A PoE capable switch simply defines a switch that has the capability of transmitting DC voltage over the twisted pair cable along with data. The other method, known as Midspan, provides power on the twisted pair cable at some point after the switch/router but before the device you are powering. An example of a Midspan device would be something like a Single Port PoE injector (Planet3 Wireless, 2005). A Single Port PoE injector has a port for the incoming Ethernet cable, a cord for the power supply, and an outgoing Ethernet port. This Midspan injector takes the data only of the incoming twisted pair cable and combines it with the DC voltage to provide a data/DC voltage

combination that is applied to the outgoing Ethernet port. At the PD end of the twisted pair cable is a device known as a cap. The cap provides for a power port that fits the PD's power cable (Duntemann, 2003). It is at this point that the PD can also be connected in line with the data stream on the Ethernet cable to allow the PD to transmit data to the network.

One of the major potential benefits of PoE is the difference in cost of installing a standard network device as compared to a PoE device. When a standard device is going to be attached to a network, a network cable must be installed along with a 110AC power supply cable and outlet. Anytime power outlets are installed requires the services of a professional electrician and building codes must be adhered to (Planet3 Wireless, 2005). The installation of a PoE device, however, does not require the services of an electrician because the cable supplying the power is low voltage. This means there is a significant cost savings in relation to the services of the electrician along with the added material cost for the 110AC cable and outlets. A network technician can install the required Ethernet cable because there are few to none building codes that pertain to twisted pair cable (Planet3 Wireless, 2005).

PoE is a dynamic technology that allows for a device to be powered over a network cable without the need for installing power cable. In this paper I have explained the layout and hardware that make it possible to configure a network for the IEEE 802.3af standard and discussed the potential savings that can be realized by utilizing this technology.

### Bibliography

Coleman, David D., Westcott, David A. (2006). CWNA: Certified Wireless Network

Administrator Study Guide (Exam PW0-100). Indianapolis: Wiley Publishing.

Duntemann, Jeff. (2003). Jeff Duntemann's Drive-By Wi-Fi Guide. Scottsdale:

### Paraglyph Press

Planet3 Wireless. (2005). CWNA Wireless Network Administrator Official Study Guide:

Exam PW0-100, Third Edition. Berkeley: McGraw-Hill/Osborne

PowerOverEthernet Staff. (2003, April 11). White Paper on Power Over Ethernet

(IEEE802.3af)- a Radical New Technology. Retrieved February 18, 2010 from: