# Protocol Wireless Nodes

Chapter 3: Directional Mac Protocol

In this chapter the new directional MAC (DMAC) protocol is proposed for 802.11 to enhance the performance of wireless Ad Hoc local area network (WLAN) by using directional antennas. This protocol will also overcome the deafness problem caused by directional antennas.

3.1 Wireless Node Model & Properties

For our proposed protocol we have fixed wireless nodes (not mobile) .In these wireless nodes we are replacing the omnidirectional antennas by using predefined fixed beam pattern directional antennas.

| (a) Wireless node with 4 Ideal directional antennas | (b) Ideal pattern |
| --- | --- |

Fig.3.1 The Ideal Antenna Pattern

Now consider the ideal directional antenna pattern for our wireless node. In fig3.1b we considered the ideal pattern of directional antenna with 90o beam width which has 10dbi of directional gain and 40db of front to back ratio. And four antennas with this specification can cover the whole area of 360 o by covering 4 different directions. This pattern has ideal shape and it gives the desired full reception in one direction and on reception in other directions.

But practically this perfect beam shape directional antenna pattern is not possible. So we consider the commercially available realistic directional antennas with side lobes as shown in fig 3.2. This realistic directional antenna has 65o horizontal beam width, 15.1 dbi of directional gain and about 30db front to back ratio [14]. Four antennas can cover the whole 360o area by covering 4 different directions.

- realistic directional antennas with side lobes(horizontal and vertical views)

b) Wireless node with 4 realistic directional antennas

Fig.3.2 The realistic Antenna Pattern [4] [19]

Now we assume that our each wireless node has four of these antennas to cover all directions and it can switch between these antennas to focus the required direction. But these antennas will overlap each other in some areas.

As proposed in [15] to design and development a smart antenna for a wireless local area Network (WLAN) card for wireless nodes the radial switches or RF switch are required, which perform the switching between the directional antennas [15].The wireless nodes cab also check the signal level on all beams and select the best beam with highest signal strength. So to implement our Directional MAC protocol at each node we required4 directional antennas and 4 RF chips to switch these antennas as shown in fig 3.3.

Fig 3.3 architecture of the directional MAC protocol

3.2 The proposed 802.11 DMAC protocol

3.2.1 The protocol Basic Elements

In this section we will discuss in detail the essential basic elements required by our proposed protocol.

32.1.1 Resource Allocation Table (RAT)

Every node will maintain a Resource Allocation Table to maintain the neighbour nodes location with the help of their addresses and used antennas. The required fields of RAT are created in every wireless node. Every node will get the information to fill the appropriate fields of resource allocation table (RAT) from the RTS and CTS frames and also through the carrier sensing mechanisms. The need of such kind of table was proposed by Thanasis Korakis ,Gentian Jakllari and Leandros Tassiulas in [10], where they use Location Table to maintain the neighbour nodes location information. We enhanced this approach by adding more fields to overcome the problems related to wireless media access and we will discussed later.

The Resource Allocation table is explained in fig 3.4. The use and working of RAT will be explained in detail in the protocol basic procedure section.

Fig 3.4. The Resource Allocation Table (RAT)

My Address: Node itself.

Neighbor's Address: the station from which it has heard a packet.

My Antenna: The Antenna on which Neighbour`s Packet is received.

Neighbor's Antenna: Neighbor`s antenna from which packet was sent.

Blocking Antenna: which antennas I have to block?

3.2.1.2 Frame Formats

The 802.11 MAC protocol use RTS and CTS frame exchange to avoid collision, they inform other nodes about the transmission between two nodes and reserve the wireless medium for limited time period as discussed in chapter 2. In our DMAC protocol we have enhanced the RTS & CTS frame formats by adding more fields, these will b used not only to reserve medium (CSMA/CA) but also for providing the location information of communicating nodes.

Directional RTS (DRTS) Frame Format

The enhanced form of RTS is called directional RTS (DRTS), is shown in fig 3.5 with an extra field of “Transmitter Antenna Number”.

Fig 3.5 Directional RTS (DRTS) frame

Duration: Total time duration of the communication.

Transmitter Antenna Number: Transmitter`s antenna no. from which frame was sent.

Transmitter Address: Address of the STA transmitting the RTS frame.

Receiver Address: Address of the STA that is the intended immediate recipient of the next Data or Management frame.

Directional CTS (DCTS) Frame Format

The enhanced form of CTS frame is Directional CTS (DCTS) is shown in fig 3.6 , which has extra fields of transmitter address, transmitter's antenna number, receiver's best antenna number and transmitter's best antenna number.

Fig 3.6 Directional CTS (DCTS) frame

Duration: Time Duration of the communication.

Transmitter Address: Address of the STA transmitting the RTS frame.

Receiver Address: Address of the STA that is the intended immediate recipient of the next Data or Management frame.

Transmitter Antenna Number: Transmitter`s antenna no. from which frame was sent.

Transmitter Best Antenna Number: Transmitter`s antenna no. on which communication will b carried out.

Receiver Best Antenna Number: Receiver`s antenna no. on which communication will b carried out.

3.2.2 802.11 DMAC Protocol Basic Procedure

In this section we will describe protocol basic operational procedure and steps over a scenario given in fig 3.7.

Omni-DRTS Mode

In our scenario node A wants to send data packet to node B. So Node A work in Omni-DRTS mode, in which it sends the DRTS packet from all of its directional antennas in every direction. It will use the DRTS frame format described above; from now on we will use the following notation for DRTS,

DRTS [Transmitter Antenna, Transmitter address, receiver address]

When every node gets the DRTS which is from node A to node B will open it and read the fields entries, so they will be aware of communication between node A and node B.

Every node will check for the receiver field. If it is the required receiver destination, then it will look for the antenna with maximum received power in the direction of transmitter node. And mark that antenna for data exchange with transmitter node.

All other nodes block there antennas in that direction .So that they will not interfere communication of between node A and node B also not interfered by the communication of nodes A and B. (When every node will receive the DCTS packet from node B it may remove its blocking condition on antennas in the direction of node A, if these blocked antennas are not interfering the communication between node A and B).

D-NAV

While blocking the antennas, now every node will also setup the Directional Network Allocation Vector (D-NAV) [16], after reading the duration field of received DRTS.D-NAV was presented in [16] which is similar to 802.11 NAV but here it is for a specific direction. The antennas will b released after the DNAV timer will expire.

Fig.3.7 Nodes receiving DRTS from Node A (Omni-DRTS Mode)

- Let us consider the node B , After receiving the DRTS[3, A,B] packet it will make the entries in RAT, it will enter its receiving best antenna no which is 1 as in fig 3.7 ,that will be used for the communication with node A. It is the best receiving beam because at antenna 1 node B gets a signal with maximum SNR from node A. As node B is the receiver of Node A signal, so it will block all antennas except its best antenna.

- When node C from the same scenario gets the DRTS [3, A,B] ,it reads the fields and record the entries in his RTS. It records node A its neighbor, antenna no 3 as the neighbor`s best antenna, and its best antenna towards the direction of node A on which it received the DRTS from node A ,which is its antenna no 1. Important point is that node C is not the receiver so it needs to block the antennas in the direction of communication between node A and node B ,But it will add “no” in the blocking filed of its antenna no.1, because it is unaware of the direction of communication at the moment as it do not aware of the location of node B. So after getting the DCTS from node B C will add “Yes ”in the blocking field of its antenna no.1 not to interfere the communication between node A and node B. fig 3.8 shows the configuration of RAT at each node after receiving the DRTS from node A.

| My Address | Neighbor`s Address | My Antenna | Neighbor`s Antenna Blocked Antenna Ant. 0 Ant. 1 Ant.2 Ant.3 |  |
| --- | --- | --- | --- | --- |
| B | A | 1 | 3 | Yes | No | Yes | Yes |
| C | A | 1 | 3 | No | No | No | No |
| D | A | 2 | 0 | No | No | No | No |

Fig 3.8 configuration of RAT after getting DRTS from node A

Omni-DCTS Mode

In Omni-DCTS mode the station B will send DCTS packets in all directions from its all 4 directional antennas, just like node A in Omni-DRTS mode (fig 3.9).

When Node A will receive DCTS from node B it will find that the wireless medium is available for communication. After reading DCTS fields node a will select its antenna no 3 for sending data packets, which is in the direction of node B. But it is important to avoid the packet collision that all other nodes must not interfere with the communication.

Fig.3.9 Nodes Receiving DCTS from Node B (Omni-DCTS Mode)

Now consider the node C, when it will get the DCTS packet from node B it will read the fields and get aware that antenna no 1 of node B is in the direction of antenna no 3 of node A. In the DCTS packet, the field Transmitter`s Best antenna (which is antenna no 1) will inform all nodes, that B will communicate with node A by using this antenna.

Now node C will notice that in DCTS the fields of transmitter`s best antenna and transmitter`s antenna are the same, both are antenna no 1 of node B. So node C will block its antenna no 3, by which it received the DCTS packet. And also it will also observe that node A will use its antenna no3 from the receiver`s best antenna field of DCTS. From RAT we can see that antenna no 1 of node C is in the direction of antenna no3 of node A so if node C try communicate with node A there will b collision. So Node C will check the RAT and block its antennas no1 that is in the direction of node A. Antennas 1 and 3 of node C are blocked, transmission is allowed from antenna 0 and antenna 2 to prevent the collision with communication between node A and node B.

The Node D will get the DCTS packets by its antenna no2. It will read the fields of packet and get notice that this packet is coming from antenna no 0 of node B but B will use its antenna no 1 for communication. So antenna no 0 of Node D will not interfere the communication of node C. It will also take notice that this is for node A and node A will communicate from its antenna no.3. Node D will check its Resource Access Table (RAT) and find out that it has the entry of node A, but its antenna no 2 is in the direction of antenna no 0 of node A which will not interfere the communication between node A and node B. So node D is in the safe zone and none of its antenna will interfere with the communication between node A and node B.

| My Address | Neighbor`s Address | My Antenna | Neighbor`s Antenna Blocked Antenna Ant. 0 Ant. 1 Ant.2 Ant.3 |  |
| --- | --- | --- | --- | --- |
| A | B | 3 | 1 | Yes | Yes | Yes | No |
| B | A | 1 | 3 | Yes | No | Yes | Yes |
| C | A | 1 | 3 | No | No | No | No |
| C | B | 3 | 1 | No | Yes | No | Yes |
| D | A | 2 | 0 | No | No | No | No |
| D | B | 2 | 0 | No | No | No | No |

Figure 3.10 Updated Resource Access Table (RAT) after DCTS frame of Node B.

Directional Data Transfer Mode

Node A and Node B will start directional data communication after the handshake of DRTS & DCTS frames. Node A will send the directional data packet from its antenna 3, which node B will receive at its antenna1.see fig 3.11. The directional data transfer mode will reduce the interference from neighbour nodes and create a highly reliable wireless medium for better quality data communication between nodes.

Fig.3.11 Directional Data Transfer from Node A (antenna 3) to Node B (antenna1)

Spatial division multiple access (SDMA)

Spatial division multiple access (SDMA) is a wireless communication mode that optimizes the use of radio spectrum and minimizes system cost by taking advantage of the directional properties of smart antennas. In SDMA, the smart antennas transmit signals to numerous zones in different directions. The antennas are highly directional, allowing duplicate frequencies to be used for multiple zones [17]. In the example scenario our protocol is providing support for SDMA, if the wireless medium and antennas are available. Suppose while the communication between node A and node B, node D can also communicate with node C. Because nodes have blocked their interfering antennas in each other`s direction, so they can communicate without interference.

Communication between Node D and node C (SDMA)

Directional-DRTS/DCTS mode

Node D has no blocked antenna so it will want to communicate with node C ,it will send DRTS frame from its all four antennas. Node B and node A has blocked there all three antennas in different directions except the direction of each other, so they will not receive the DRTS packets from node D. On the other hand node C will receive DCTS at antenna 0 and reply it with DCTS packet. But node C has blocked its antennas in the direction of node A and node B and will not unblock them until end of the communication between node A and node B. So node C will send DCTS packet from antenna 0 and 2.

Fig.3.12 Spatial division multiple access (SDMA)

As node C received the DRTS on antenna 0 so this is its best antenna, it will block its antenna 2 and update its D-NAV for antenna 1 and 3 by new D-NAV after reading the duration from DRTS of node D. When node D will get the DCTS of node C from its antenna 2 it will block its antennas 0,1 and 3. After the DRTS and DCTS handshake the node D will send data packet from its antenna 2 and also wait to receive ACK from node C from the same antenna. See Figure 3.12 and 3.13. No network throughput is doubled as 4 nodes are communicating at a same time in same basic structure of nodes. Our protocol has made possible the Spatial division multiple access by optimize use of radio spectrum from its directional antennas.

Fig.3.13 Communication of Nodes (SDMA)

SDMA mode - Smart Packet Scheduling

For SDMA we need to do the packet scheduling. Normally in wireless ad-hoc local area network (WLAN) every node try to communicate with other nodes, for that every node create a packet and competing to gain control of the channel. As they are omnidirectional nodes so they capture the whole channel for the communication with other nodes, and all other nodes wait for them to free the channel and avoid the collision. But for the case of nodes with directional antennas, the SDMA or spatial reuse of channel is possible for that we need to use a smart packet scheduler.

As in our protocol every node has to maintain a RAT, so it knows which nodes and its own antennas are in blocked state, where it cannot send the packet. For example node A and node B are communicating so node D or C must not send the packet to avoid the collision.

So if any node has the packet for the node which is idle because of communication with another node, this node should have to send packet back to queue and process the next packet. So if any packet is for the node which is in idle state then node should have try to process and send next packet from the queue, and send the 1st packet back to queue. After completing the transmission of 2nd packet, node can check the state of destination node of 1st packet and compete for the channel to transmit the 1st packet. The state diagram of smart packet scheduler is given in fig 3.14.

Fig.3.14 Smart Packet Scheduler

The smart scheduling has the information of the neighbor node`s location and their status. It will use the Resource Access Table to make decision whether a packet can be send to the destination node or wait, as RAT can also provide the status information of the nodes. And if the destination node is not in the list of RAT the node will send the DRTS packet to find out the location and status of the destination node. With these changes in scheduler we can maximise the SDMA, and it will also helpful to avoid the redundant unsuccessful retries and unnecessary queue waiting times.

Proposed Solution of Deafness Problem (switching Omni-Data Transfer)

Several existing protocols attempt to maximize the benefits of directional antennas, and suffer from the problem of deafness as a trade-off [18]. Deafness is caused by unawareness of a node from the communication of other nodes with directional transmission. When we introduce the SDMA support then during the communication of node A and node B, the other 2 nodes node C and node D can also start a new transmission as in fig 3.12 & 3.13. This situation can come up with two possible scenarios:

- If the length of the data packet of node A for node B is greater than the length of the data packet of node D for node C , then the transmission between node D and node C will be completed before the transmission between node A and node B. So on completion of communication between node A and B, then NAV of these nodes and DNAV of node C and node D will expire ,and these all four nodes will Back-off and they will fight for the control of channel. And winning node will again work in Omni-DRTS mode; it will send DRTS frame in all direction and inform all other nodes with the next communication.

ii. If the length of the data packet of node D is greater than the length of the data packet that is transmitted from node A, the data exchange between C and D will be completed after A and B exchange. However, because of deafness, node A and node B will be unaware of the communication between C and D, both nodes will sense the packet from their 0th beam, which has been transmitted from the second beam of node D. These dummy bits will give no information to nor node A neither node B. However, since CSMA/CA algorithm is employed, the signal will be sensed the nodes will defer their communication during the ongoing communication between node C and node D without decoding the packet. After receiving of the dummy bits, the nodes will wait defer some amount of time;

_ (3.1) DEFERTSIFSACKDURATIONDIFS=++

to protect the ACK of node D that is destined to node C, so that collisions at node D are avoided as shown in the timing diagram in Fig.3.11. After deference, nodes A and node B will recheck the medium.

Consider the case that data is to be transmitted from node C, although nodes A and B sense the medium, because of the directional transmission, they will both be unaware of the ongoing communication between C and D. At this time, if node A wants to transmit a new data packet, it will send a new AN-RTS packet in all directions because it didn't block any of its beams. Sending a signal from the 0th beam of node A will interfere the node D's second beam because it is receiving the data packet over it. If the signal is powerful, the packets will collide and than node D will want to retransmit the same data packet, which will degrade the overall performance of the network.

As considered above, the performances of the medium access protocols that are designed to work with directional antennas are limited to some scenarios because of the deafness problem. However, by the addition of new precautions in our protocol, these problems can be prevented.

Fig.3.13 Node C warns node A because of its ongoing transmission

In Fig.3.13, if a user (like node C) wants to send a data packet during communication of others (A and B) and if it knows that A and B are communicating (as in our sample scenario), it will calculate the required time to initiate a new transmission and data exchange of its own. Then it will compare the remaining time of D-NAV duration and the required time to transmit a data frame. If it is enough to complete the data exchange in this remaining time, it will send an AN-RTS packet over its unblocked antennas. Doubtless, node C will finish transmission before A to B communication, node A and B will not interfere with the ongoing transmission between C and D. Then all nodes will re-contend for the channel. If the calculated time is greater than the remaining time, node C may wait for the completion of the A to B communication and then it will contend for the channel. If the back-off of node C is smaller than node A, node C will gain the channel and will start its transmission. This will decrease the expected network capacity with the use of directional antennas and give the same performance of omni directional system of current WLANs. On the other hand if the calculated time is greater than the remaining time, node C may send data to D as explained in section 3.2.2. After the completion of A to B communication, D-NAV in node C will expire. Node C may inform A and B by a simple method. After the expiration of D-NAV, node C will open all blocked antennas and send power from

those antennas, too (Fig.3.13). Only sending the remaining part of the data packet over all antennas via RF switches [32]. By this way, the surrounding nodes will be aware of the ongoing transmission. These nodes only get dummy bits but this will make them to defer their transmissions because of carrier sensing mechanisms and additionally wait for TDEFER (Equation 3.1) time to protect ACK. At the end of communication between C and D, all nodes will back-off and re-contend for the channel.