# Router Connection Internet

- Considering the fact that there are six workstations connected to the router, it is probable that the router also acts as a switch or if not, an external one needs to be used. The NAT enabled router would use the single ISP provided ip address configured into it and would enable conversion into different ip addresses keeping the original for the internet connection. Without the ISP ip address, the connection to the internet world would not be possible. The router can be connected to the external internet by means of different connection methods, as in PPPOE, STATIC IP (provided by the ISP) etc. Since the number of workstations is six, the router would get its connection to the internet from another CPE, which could either be another router or a modem, dsl or cable. The wan port of the router would be connected from the wan port of the modem or router through a crossover Ethernet cable, which provides the internet connection. Considering the NAT enabled router to also house a four-port switch configuration, three ports would be connected to individual workstations using a straight through Ethernet cable. The fourth unused port is connected using another straight through cable to a compatible 8 or 16 port Ethernet switch. The cable from the router to the switch would form the input for the switch. The remaining workstations can now be connected using three more Ethernet cables which run from the ports of the switch.

The basic purpose of NAT is to multiplex traffic from the internal network and present it to the Internet as if it was coming from a single computer having only one IP address. The TCP/IP protocols include a multiplexing facility so that any computer can maintain multiple simultaneous connections with a remote computer. It is this multiplexing facility that is the key to single address NAT.

A modern NAT gateway must change the Source address on every outgoing packet to be its single public address. It therefore also renumbers the Source Ports to be unique, so that it can keep track of each client connection. The NAT gateway uses a port mapping table to remember how it renumbered the ports for each client's outgoing packets. The port mapping table relates the client's real local IP address and source port plus its translated source port number to a destination address and port. The NAT gateway can therefore reverse the process for returning packets and route them back to the correct clients. When any remote server responds to an NAT client, incoming packets arriving at the NAT gateway will all have the same Destination address, but the destination Port number will be the unique Source Port number that was assigned by the NAT. The NAT gateway looks in its port mapping table to determine which "real" client address and port number a packet is destined for, and replaces these numbers before passing the packet on to the local client. This process is completely dynamic. When a packet is received from an internal client, NAT looks for the matching source address and port in the port mapping table. If the entry is not found, a new one is created, and a new mapping port allocated to the client. Packets received from external device, they undergo a reverse translation process. The packets whose destination port numbers are not in current mapping table are just dropped. Each client has an idle time-out associated with it. Whenever new traffic is received for a client, its time-out is reset. When the time-out expires, the client is removed from the table. This ensures that the table is kept to a reasonable size. The length of the time-out varies, but taking into account traffic variations on the Internet should not go below 2-3 minutes. Most NAT implementations can also track TCP clients on a per-connection basis and remove them from the table as soon as the connection is closed. This is not possible for UDP traffic since it is not connection based.

- Once the connection is made, the way the connected workstations get an ip address depends on configuration of the router. Most NAT enabled routers are capable to be configured through a browser interface. If the router has DHCP enabled, then the workstations would be assigned an ip address automatically with an ideal lease time of 24 hours before the lease expires. Alternatively, the DHCP function can be disabled on the router and the ip addresses can be assigned explicitly to the workstations by hard coding them on each workstation in the TCP/IP settings.

- The router which provides the source for the connection get its internet ip address either dynamically through the internet, or can be explicitly assigned a static ip address provided by the internet service provider. Whatever be the individual ip addresses of the workstations, they would be identified on the internet only by the address that is given to the router either dynamically, or an explicitly assigned static ip address. When connected to another router, the router providing the connection would be bridged and then connected to the router which connects to the workstations, either hard coding the static ip address details or obtaining an ip automatically. Another option also includes a PPPOE connection which would require a username and a password given by the ISP, after connecting to which would be assigned an ip address to the PPP adapter.

Task 3 Answers:

A) Persistent Connections:

An HTTP persistent connection, also called HTTP keep-alive, or HTTP connection reuse, is the idea of using the same TCP connection to send and receive multiple HTTP requests/responses, as opposed to opening a new one for every single request/response pair. It is similar to re-using the same connection instead of the use-and-throw idea. Using persistent connections is very important for improving HTTP performance.

By using persistent connections, we can achieve the following advantages:

- Network friendly. Less network traffic due to fewer setting up and tearing down of TCP connections.

- Reduced latency on subsequent request. Due to avoidance of initial TCP handshake.

- Long lasting connections allowing TCP sufficient time to determine the congestion state of the network, thus to react appropriately.

The advantages are increased with HTTPS or HTTP over SSL. Instead of new security associations for every HTTP request/response, a single association can be used for all the secure traffic over the same connection. Therefore, persistent connections may reduce the number of costly SSL/TLS handshake to establish security associations, in addition to the initial TCP connection set up.

Pipelining:

HTTP pipelining is a technique where multiple requests are written out to a single interface socket without waiting for the corresponding responses. Pipelining improves the efficiency of the bandwidth of an internet connection. It results in a dramatic improvement in page loading times, especially in connections where there is a high latency such as satellite internet connections.

Since several HTTP requests can be transmitted over a single TCP packet, fewer TCP packets can transferred over the network hence reducing network load.

HTTP pipelining requires both the client and the server to support it. HTTP/1.1 conforming servers are required to support pipelining. This does not mean that servers are required to pipeline responses, but that they are required not to fail if a client chooses to pipeline requests.

Conditional GET:

In HTTP, the GET method means to retrieve whatever information (in the form of an entity) is identified by the Request-URI. If the Request-URI refers to a data-producing process, it is the produced data which shall be returned as the entity in the response and not the source text of the process, unless that text happens to be the output of the process. The semantics of the GET method change to a ‘conditional GET' if the request includes an If-Modified-Since, If-Unmodified-Since, If-Match, If-None-Match, or If-Range header field. A conditional GET method requests that the entity be transferred only under the circumstances described by the conditional header field(s). The conditional GET method is intended to reduce unnecessary network usage by allowing cached entities to be refreshed without requiring multiple requests or transferring data already held by the client.

B) Mail Retrieval Protocols:

- POP3: POP3 stands for post office protocol version 3. It lies in the application layer and is used to retrieve email from a remote server over a TCP/IP connection. Many individual ISP users access their email with client software that uses POP3. The design of POP3 and its procedures supports end-users with intermittent connections such as dial-up connections, allowing them to retrieve email when connected and then to view and manipulate the retrieved messages without needing to stay connected. Although most clients have an option toleave mail on server, e-mail clients using POP3 generally connect, retrieve all messages, store them on the user's PC as new messages, delete them from the server, and then disconnect.

- IMAP: IMAP stands for Internet Message Access Protocol. It is an application layer protocol operating on port 143 which allows a local client to access email on a remote server. IMAP supports both connected (online) and disconnected (offline) modes of operation. E-mail clients using IMAP generally leave messages on the server until the user explicitly deletes them. This and other facets of IMAP operation allow multiple clients to access the same mailbox. Most e-mail clients support either POP3 or IMAP to retrieve messages, however fewer ISPs support IMAP.

- SMTP: SMTP is short for Simple Mail Transfer Protocol. It is a relatively simple, text-based protocol, in which one or more recipients of a message are specified (and in most cases verified to exist) along with the message text and possibly other encoded objects. The message is then transferred to a remote server using a procedure of queries and responses between the client and server. SMTP is a "push" protocol that does not allow one to "pull" messages from a remote server on demand. To do this a mail client must use POP3 or IMAP. The SMTP client initiates a TCP connection to server's port 25 (unless overridden by configuration).

Task 4 Answers:

1) IntServ or integrated services is an architecture that specifies the elements to guarantee quality of service (QoS) on networks. IntServ can for example be used to allow video and sound to reach the receiver without interruption. IntServ specifies a fine-grained, flow-based QoS system. The idea of IntServ is that every router in the system implements IntServ and every application that requires some kind of guarantees has to make an individual reservation. "Flow Specs" describe what the reservation is for, while "RSVP" is the underlying mechanism to signal it across the network.

Flow Specs:

There are two parts to a flow spec:

- What does the traffic look like? Done in the Traffic SPECification or TSPEC part.

- What guarantees does it need? Done in the service Request SPECification or RSPEC part.

TSPECs include token bucket algorithm parameters. The idea is that there is a token bucket which slowly fills up with tokens, arriving at a constant rate. Every packet which is sent requires a token, and if there are no tokens, then it cannot be sent. Thus, the rate at which tokens arrive dictates the average rate of traffic flow, while the depth of the bucket dictates how 'bursty' the traffic is allowed to be.

TSPECs typically just specify the token rate and the bucket depth. For example, a video with a refresh rate of 75 frames per second, with each frame taking 10 packets, might specify a token rate of 750Hz, and a bucket depth of only 10. The bucket depth would be sufficient to accommodate the 'burst' associated with sending an entire frame all at once. On the other hand, a conversation would need a lower token rate, but a much higher bucket depth. This is because there are often pauses in conversations, so they can make do with fewer tokens by not sending the gaps between words and sentences. However, this means the bucket depth needs to be increased to compensate for the traffic being burstier.

RSPECs specify what requirements there are for the flow: it can be normal internet 'best effort', in which case no reservation is needed. This setting is likely to be used for web pages, FTP, and similar applications. The 'Controlled Load' setting mirrors the performance of a lightly loaded network: there may be occasional glitches when two people access the same resource by chance, but generally both delay and drop rate are fairly constant at the desired rate. This setting is likely to be used by soft QoS applications. The 'Guaranteed' setting gives an absolutely bounded service, where the delay is promised to never go above a desired amount, and packets never dropped, provided the traffic stays within spec.

RSVP:

The Resource Reservation Protocol (RSVP) is described in RFC 2205. All machines on the network capable of sending QoS data send a PATH message every 30 seconds, which spreads out through the networks. Those who want to listen to them send a corresponding RESV (short for "Reserve") message which then traces the path backwards to the sender. The RESV message contains the flow specs.

The routers between the sender and listener have to decide if they can support the reservation being requested, and, if they cannot, they send a reject message to let the listener know about it. Otherwise, once they accept the reservation they have to carry the traffic.

The routers then store the nature of the flow, and also police it. This is all done in soft state, so if nothing is heard for a certain length of time, then the reader will time out and the reservation will be cancelled. This solves the problem if either the sender or the receiver crash or are shut down incorrectly without first canceling the reservation. The individual routers may, at their option, police the traffic to check that it conforms to the flow specs.

2) Differentiated Services or DiffServ is a computer networking architecture that specifies a simple, scalable and coarse-grained mechanism for classifying, managing network traffic and providing Quality of Service (QoS) guarantees on modern IP networks. DiffServ can, for example, be used to provide low-latency, guaranteed service (GS) to critical network traffic such as voice or video while providing simple best-effort traffic guarantees to non-critical services such as web traffic or file transfers. DiffServ is a coarse-grained, class-based mechanism for traffic management.

DiffServ operates on the principle of traffic classification, where each data packet is placed into a limited number of traffic classes, rather than differentiating network traffic based on the requirements of an individual flow. Each router on the network is configured to differentiate traffic based on its class. Each traffic class can be managed differently, ensuring preferential treatment for higher-priority traffic on the network. The DiffServ model does not make judgement on what types of traffic should be given priority treatment since that is left up to the network operator. DiffServ simply provides a framework to allow classification and differentiated treatment. DiffServ does recommend a standardized set of traffic classes to make interoperability between different networks and different vendors' equipment simpler. DiffServ relies on a mechanism to classify and mark packets as belonging to a specific class. DiffServ-aware routers implement Per-Hop Behaviors (PHBs), which define the packet forwarding properties associated with a class of traffic. Different PHBs may be defined to offer, for example, low-loss, low-latency forwarding properties or best-effort forwarding properties. All the traffic flowing through a router that belongs to the same class is referred to as a Behavior Aggregate (BA).

A group of routers that implement common, administratively defined DiffServ policies are referred to as a DiffServ Domain. Network traffic entering a DiffServ domain is subjected to classification and conditioning. Traffic may be classified by many different parameters, such as source address, destination address or traffic type and assigned to a specific traffic class. Traffic classifiers may honor any DiffServ markings in received packets or may elect to ignore or override those markings. Because network operators want tight control over volumes and type of traffic in a given class, it is very rare that the network honors markings at the ingress to the DiffServ domain. Traffic in each class may be further conditioned by subjecting the traffic to rate limiters, traffic policers or shapers.

One advantage of DiffServ is that all the policing and classifying is done at the boundaries between DiffServ clouds. This means that in the core of the Internet, routers can get on with doing the job of routing, and not care about the complexities of collecting payment or enforcing agreements. That is, DiffServ requires no advance setup, no reservation, and no time-consuming end-to-end negotiation for each flow, as with integrated services. This leads DS relatively easy to implement.

3) The problem with IntServ is that many states must be stored in each router. As a result, IntServ works on a small-scale, but as you scale up to a system the size of the Internet, it is difficult to keep track of all of the reservations. As a result, IntServ is not very popular. One way to solve this problem is by using a multi-level approach, where per-microflow resource reservation (i.e. resource reservation for individual users) is done in the edge network, while in the core network resources are reserved for aggregate flows only. The routers that lie between these different levels must adjust the amount of aggregate bandwidth reserved from the core network so that the reservation requests for individual flows from the edge network can be better satisfied.

Task 5 Answers:

- ISO/IEC 17799:2005 establishes guidelines and general principles for initiating, implementing, maintaining, and improving information security management in an organization. The objectives outlined provide general guidance on the commonly accepted goals of information security management. ISO/IEC 17799:2005 contains best practices of control objectives and controls in the following areas of information security management:

- security policy,

- organization of information security;

- asset management;

- human resources security;

- physical and environmental security;

- communications and operations management;

- access control;

- information systems acquisition, development and maintenance;

- information security incident management;

- business continuity management;

- compliance.

The control objectives and controls in ISO/IEC 17799:2005 are intended to be implemented to meet the requirements identified by a risk assessment. ISO/IEC 17799:2005 is intended as a common basis and practical guideline for developing organizational security standards and effective security management practices, and to help build confidence in inter-organizational activities.