# Routing

Routing is the process of selecting best paths for moving information from source to destination .routing is usually performed by a intelligent device which called a router. basically router operating under two main function.

Routing Table creation

Routing table is a electronic table stored in router memory which called router information base (RIB).RIB contain all information of network such as neighbour address, link speed, network id, cost, protocols details interface and it associated with address ..etc. depend on routing protocols and router's memory capacity routing table can be sized. router create routing table by it self and getting from neighbour. Which change dynamically with topology changes .

Chose best parth

One or many routing algorithm running inside the router. Which get information about network statues from routing table to choose best path . routing algorithm are vary protocols to protocol . for eg link state algorithm use metric to select path and distant vector algorithm use no of hops to find parth.

Router use two type of routing to find destination network which are static routing and dynamic routing. Static routing is manually entered destination network no need to process algorithm, dynamic routing is a running application in the router which discover destination network dynamically which need algorithm.

Routing in mobile ad hoc network

A MANET are self-configuration and self-organisation network of mobile nodes connected by wireless links. in the absence of proper infrastructure to initiate and maintains network function routing is necessary for MANETs. each node has to perform in order to connect with destination node or enable connection between nodes if destination node out of range source sending information through intermediate node so there is need of routing procedure. in wireless network access point can meet all nodes without routing by via broadcasting message but in case of MANETs each node must be able to forward message through intermediate node to reach destination node .the destination node hidden by network if destination node out of source node converge area.

Features of mobile ad hoc routing protocols

- Distributed operation

The protocol should be adapt as soon as quickly with topology changes and quickly establish a routes .this not depended on any centralised device such as access point. Ad hoc nodes are mobility any time can enter and leave from network. hence the protocol must be distributed.

- Loop free

The routing protocols should provide loop free routing which improve packet delivery, avoid misuse of bandwidth and power consumption.

- Demand base operation

The routing protocol minimized the control over head in the network due to exchange of routing message with topology changes .the protocol should not broadcast periodically control information. which can increase the available bandwidth and reduce the collision

.

- Multiple path

The protocol should provide multiple path from source to destination and this will solve the problem of delay and congestion. which improve the network QOS. If Routing keep track all the available path to destination it can save the router path discovery process.

- Power conservation

The routing protocol should support to sleeping nodes in the network.

- Security

- In wireless network contain Most vulnerable .the protocol must adapt it.

Mobile ad hoc Routing protocols issues

- Asymmetric link

In wired network is symmetric due to node are fixed by cable .but in ad hoc is opposite case all node are mobile moving device and they are frequently entering and exciting to the network .so link between sour to destination rely as asymmetric.

- Routing overhead

The routing repeat path discovery process many times Due to randomly change of mobile node .the router protocols dynamically changing table and update it with each other .so router use additional overhead in network .these are the some reason for so router use repeat process such as mobile node leave from path , no of new node arrival in to the path line, path break those are the reason

- Interference

This is the major problem in MANETs. Once connection establish betweens nodes all of neighbour overhear it and neighbour can transmission same time .if neighbour start transmission same time the total transmission will corrupt.

- Dynamic topology

In wired network topology not change fixed so it take routing table update minimum time period 30 sec. But ad hoc network topology change with sec to sec so this updating time value lower that wired network.

Clarification of dynamic routing protocols

The wired network routing protocols cannot be used for mobile ad hoc networks due to mobility of networks. There are a lot of protocols are available in MANETs all depend on net work structure and routing strategy. according to network structure the MANET routing protocols classified as flat routing ,hierarchical routing and geographic potion assisted routing. While depending on the routing strategy routing protocol classified as proactive and reactive .the main classification of MANETs routing protocols shown fig

Fig ad hoc network routing protocols .

Proactive routing protocols

Proactive mobile ad hoc routing protocols is also called as table-driven protocols .in table driven protocols each nodes constant maintains of more than one routing table which contain routing information to every other node in the MANET. Every single node an absolute the figure of the network. if any single topology changes occurs the nodes propagate update packet through network to all nodes in order to maintains topology table .all nodes periodically sent and receive routing updating message so use of proactive routing protocols every nodes in the network have up to date routing table. so easy and quick path or routing creation for message transaction.

There are some issue appear in this protocols while apply MANETs . the periodic updating router packet contain all network information up to date so that packet contain amount of information size large and that packet sent to all nodes periodically. This size of packet consume additional over head when transferring periodically. Every node must be in wake up state in additional power wastage .some ad hoc device work under battery power which can get totally off.

Example of table –driven protocols

- DSDV –Destination Sequence Distance Vector.

- OLSR – Optimized Link State Routing.

- FSR- Fish eye State Routing.

- CGSR-Cluster head gateway switch routing protocols.

Reactive protocols

In this protocols reduce the overhead problem which occurs in proactive protocols .this is called as on-demand protocol also. reactive protocol all up to date routers are not maintained at every nodes. A node don't have to an image entire network topology . The route between two nodes is created when it is needed .the route is valid until destination reachable otherwise it no longer needed. The source and intermediate nodes are responsible to create route and those maintains the router until finish massage transition. if router break or topology changes the route have to be repaired.

Here small size of router information pass to discover route and minimum periodic packet transition .once router path created no of router packet reduce in network so sleeping nodes to need to wake up when neighbour nodes message exchange .so power consumption and network over head reduce than proactive protocols.

The reactive protocols start to find route on- demand basic when any source node initiate to transfer message which it has no route to destination. it must flood router request (RREQ) and router reply (RREP) packets. By help of router request message and intermediate nodes the source nodes find the target node . The target node sent conform message such as router reply (RREP) to establish connection . in the established path each node contain routing table which update only neighbour s details not more node details .

The kind of On Demand protocols are

- Ad hoc on demand distance vector (AODV).

- Dynamic source routing protocols (DSR).

- Temporary ordered routing algorithm (TOAL).

- Signal stability-based adaptive routing (SSA).

- Associative base routing (ABR).

Hybrid routing protocols

Hybrid method use both reactive routing protocols and Proactive routing protocols ,it balance both when routing . a small network use Proactive routing protocols and large or outside the domain network use reactive routing protocols. Examples are

- Wireless ad hoc routing protocols (WARP).

- Zone routing protocols (ZRP) .

Hierarchical routing protocols

Hierarchical routing protocols introduce to solve the flat protocols limitation .which reduce the overhead and suitable for larger ad hoc network. Example of Hierarchical routing protocols are

- Hierarchical state routing (HSR) .

- Zone Routing Protocol (ZRP) .

- Landmark Ad Hoc Routing Protocol (LANMAR) .

- Cluster-head Gateway Switch Routing Protocol (CGSR) .

Geographical Routing Protocols

This protocol based on geographical location of nodes .a source node must know the geographical location of the destination node to which it wise to sent ,the packet labeled with that destination and it' s location. the intermediate node only know it's own location and it's neighbors locations. This is enough information to transfer packet to destination .but problem is every node must know it's geographical location. Example of Geographical Routing Protocols

- Geographic Addressing and Routing(GeoCast) .

- Location – Aided routing protocols (LAR) .

- Greedy Perimeter Stateless Routing(GPSR) .

- Distance Routing Effect Algorithm for Mobility(DREAM) .