# Signal processing

### I. Introduction

To meet the users' requirements taking into account those issues like cost effectiveness, quality with less distortion, BER, low signal power and noise tolerance during the design of an optimized communication system, CDMA, though having many advantages for instance dynamic channel sharing capacity, reuse factor with low dropout rate and ease of cell planning, still have deficiencies in respect of multiuser interference (MAI), Inter symbol Interference(ISI), and Multiuser Detection (MUD) algorithm [1]. In order to solve these problems, new 4G systems the IDMA has been proposed to get rid of this entire problem and meet them in a nice way to get spectral efficient and high transmission efficiency. We could get it via multiuser detection technique for design of IDMA transceiver. The two main concepts behind the development of this system are, use of interleaving, by which users are assigned inter-leavers not codes. Interleavers randomize the data and thus channel effects are minimized. The second concept is the multiuser detection, which is a receiver designed procedure to detect the desired signals from interference and noise.

### II. SURVEY OF THE RELATED WORKS

To increase the capacity of Gaussian multiple access channel, interleaved low-rate codes together with chip by chip iterative decoding strategy was adopted [1,2]. And the purpose of this adoption was to get a suitable performance by the use of turbo-Hadamard codes.

Some work was also done for performance analysis of IDMA in Gaussian and Qausi-static channel which proved IDMA as better than multicarrier code division multiple access(MC-CDMA) in respect of mitigating against fading, multipath effects and asynchronous transmission [4].

### III. Problem Statement and Main Contribution

The main purpose of this paper is to design a communication system which meets the high data transmission and high satisfactory requirements of users.

IDMA is the suitable choice for multicarrier communication system and the MUD algorithm can refine IDMA system to meet the requirements of the BER and channel capacity.

This paper includes modeling applications of IDMA, it's implemented via MATLAB and verified by results and simulations.

### IV. Problem Solution

Multi user detection issue can easily be solved in IDMA via the design of an optimal receiver. On the receiver, multiuser detection algorithm is implemented via elementary signal detection (ESD) which estimates the data for different users. The statistical properties of the signals are judged by a posteriori (APP) decoder, helps to give out log logarithmic ratio (LLR) for each user data bits. Through this extrinsic information sharing between multiuser detector algorithm blocks and the statically decoder, we finally succeed to get data for next iteration of the signal estimation in MUD algorithm block. Thus this refined the detection, finally results in reduced complexity of the receiver compared to CDMA thus providing joint MAI and ISI cancelation.

Secondly the interleavers uncorrelation also results in reduction of MAI of different users and also helps in convergence of the detection process.

## A. IDMA TRANSCIEVER

The principle behind IDMA is the same as that of CDMA [3], but the only difference is the use of inter-leavers instead of signature codes. And it basically provides to increase the coding gain. This also helps to reduce the MUD structure.

The IDMA transceiver structure is given in Figure 1; Data transmitted by N users, is interleaved and mapped to transmit over channel. The channel is assumed to be multipath faded and AWGN type, also add these effects to signal. Channel output is passed into receiver. Now after matching filtering, data is processed by MUD algorithm and recovered for each user safely.

## B. Mathematical modeling

Mathematically, a multi user system can be described as:

MUD relies on statistical method; in our case we used maximum likelihood function estimation. Also some forward error correction technique is used like turbo encoding and decoding.

The algorithm is designed also reduce the cross entropy. FEC used, for different users with ISI relationship (1) as constraint of the possible distributions of data symbols. The main goal here is to get the resultant distribution with constraints having minimum cross entropy (MCE) w. r .t initial distribution. The use of MCE is good, because it's an iterative approach in which each constraint can be independent treated as, to achieve convergence.

Now by using MCS and maximum posterior (MAP) detector, a posteriori distribution and maximum probable symbols are detected.

All this can be described by the following equation:

Where Vm is a constant which normalized the probability mass over all X(i). The relationship (2) is based on the assumption that initial probabilities of the symbol vector are independent. So finally we will get from

From (3) finally we get at receiver, the recovered signal, and by comparing with (1) we see that our estimated signal is almost the same as in (1).

## C. Results of Simulations

For the simulations in this paper used MUD algorithm results are taken using MATLAB. Figure 2 shows the performance of the system in terms of calculating the BER of system using different number of users indicated by different color and markers. Using Multiuser Detection Algorithm makes it possible to increase the BER performance of the system though the number of users is increased.

Moreover the channel capacity is also increased due to BER and SNR of the system, verified through varying data block size. Increased number of users causes the MUD to resolve MAI from different users efficiently thus increasing the BER of the system and resource utilization in terms of channel capacity.

### V. Conclusion

The relationship between multicarrier communication systems and efficient bandwidth utilization is used in IDMA which is a modern communication system for efficient bandwidth utilization with suitable BER and channel capacity. Multi user detection algorithm used in IDMA is a chip-by-chip detection technique which removes the deficiencies of DS-CDMA, to get a desired performance and an optimized system.

Interleavers are developed to provide solutions for all impairments but still they are computationally heavy. An efficient approach is needed to be developed to overcome this problem. So an interleaver pattern which is economically and computationally efficient is needed.

### References

[1] L.Liu, J.Tong, and L.Ping, “Analysis and Optimization of CDMA Systems with Chip-level Interleaves,”IEEE J.Select.Areas Communications, vol.24, pp.141-150, Jan.2006.

[2] R.H.Mahadevappa and J.G.Proakis, “Mitigating Multiple Access Interference and Intersymbol Interference in Uncoded CDMA Systems with Chip-level Interleaving,”IEEE Trans.Wireless Communications, vol.1, pp.781-792, Oct.2002.

[3] L.Ping et al., “On Interleave-division Multiple-access,”Proc.IEEE ICC'04, Paris, June 2004, pp.2869-73.

[4] M.Moher and P.Guinand, “An Iterative Algorithm for Asynchronous Coded Multi-user Detection,”IEEE Communications Lett., vol.2, pp.229-231,