# Signaling Network Routing

Signaling System 7 Network Element

SS7 network is separated from the network voice that it supports itself. Which contain some node or Signaling Point that will provides specific functions. In the SS7, all network nodes are called Signaling Points (SPs). In signaling network, there are three main Nodes: Service Switching Point (SSP), Signal Transfer Point (STP) and Signal Control Point (SCP). The three main nodes commonly connected using point-to-point with bit rate 56 kbps. The data is being transferred with the connection (point to point) using packet-switching. These three nodes have to be able to create, receive and response SS7 message.

SS7 Signaling Points

A. Service Switching Point (SSP)

Actually SSP is a digital switch which provides voice access and call routing which have been added with hardware interface and software that related to SS7 application. Usually SSP is a Local Exchange (LE) or an Inter exchange circuit's switches and mobile switching centre. In this world, GSM, MSC act as SSP in SS7 Network. An SSP may also send a query message to an SCP to decide how to route a call (e.g., a toll-free 1-800/888 call in North America). An SCP sends a response to the originating SSP containing the routing number(s) connected with the dialed number. If the primary number is busy or the call is unanswered an alternate routing number may be used by the SSP within a specific time. Actual call features vary from network to network and from service to service. Because signaling messages will either create or terminate within them, SSPs are considered "end points" on a network. SSP has 2 main functions:

- To make a set-up call and terminate that connection, using ISUP messaging. When SSP need to make a set-up call to the other switch, SSP has to be able to formulae and send SS7 message with correct address information.

- To make and to launch SS7 message which has been prepared to database external.

B. Signal Control Point (SCP)

SCP is parameter which has been produced from the interface for database application and intelligence to control the signaling traffic. The message from SSP being sent to SCP is used to get routing information and service information. SCP is not a data base but it provides an access to database application. For example, translation database from toll-free (800- ) is supported with SCP. When there's a call for toll-free, switch LE will delay that call process and send message to SCP in order to get an exact Carrier Identification Code (CIC) so that the call can be routed to the correct switch. Without SCP, LE won't be able to know where it is should be route. Some STP consumer started to provide the database application for their own STP. So that SCP can be functioned as STP. In SS7 network, this application still looks like SCP database and network functions routing.

C. Signal Transfer Point (STP)

Network traffic between signaling points may be routed via a packet switch called an STP. Main functions from STP are switch and addressed SS7 messages. An STP routes each received message to an outgoing signaling link based on routing information contained in the SS7 message. Because it acts as a network hub, an STP provides improved utilization of the SS7 network by eliminating the need for direct links between signaling points. Some SSP or SCP needed access to the signaling before their connected to one STP. An STP can also act as a "firewall" in SS7 messages screen exchanged with other networks. An STP is a packet switch that acts as a hub to transfer messages to other STPs, SCP databases, or SSPs. Main functions of STP are physical connection at SS7 network, Message routing through Message Transfer Part (MTP), Message addressing through Global Title Translation (GTT). Because an STP's main function is to route signals, the need for direct connections between end points on a network is discarded. The STP routes messages by checking routing information attached to each signaling message and sending it (via the proper link) to the desired signaling point.

Three level of STPs:

- National STP

A National STP usually use in the national network (will vary with the country). They use the same national standard of protocol to transfer messages. Messages can be passed to an International STP, but can not be converted by the National STP.

- International STP

An International STP functions within an international network. They using the International Telecommunication Union-Telecommunication Standardization (ITU-TS) standard protocol and it provides for SS7 interconnection of all countries. To connecting to an International STP, all nodes must use the ITU-TS protocol standard.

- Gateway STP

A Gateway STP used to converts signaling data from one protocol to another protocol. Normally Gateway STPs are used as an access point to the international network. National protocols are converted to the ITU-TS protocol standard. Some location on the some situation, the Gateway STP must be able to use the International and National protocol standards together.

Six types of Signaling links use in the SS7 signaling network:

SS7 Signaling Link Types

| A Link: Access link | Access link (A link) is a link that used to connect between an SCP or SSP and an STP. |
| --- | --- |
| B Link: Bridge link | Bridge link (B link) is a link that used to connect between one STP to another STP. |
| C Link: Cross link | Cross link (C link) is a link that used to connect between STPs that have same function into a mated pair and used only when STP doesn't have any other available route to a destination. |
| D Link: Diagonal link | Diagonal link (D link) is link that used to connect between second STP like local or regional to a first STP like inter-network gateway. |
| E Link: Extended link | Extended link (E link) is link that used to connect from an SSP to other alternative STP. |
| F Link: Fully associated link | Fully associated link (F link) is link that used to connect between sender and receiver. |