# TCP-Illinois achieves high throughout

Abstract—TCP-Illinois is congestion control algorithm used for high speed networks. TCP-Illinois uses packet loss information to determine whether the window size should be increased or decreased, and uses queuing delay information to determine the amount of increment or decrement. TCP-Illinois achieves high throughput, allocates the network resource fairly, and is compatible with standard TCP. We perform simulations to demonstrate the performance of TCP Illinois and alter various parameters.

Keywords—TCP, Congestion Control, Throughput

### I. INTRODUCTION

TCP, the most widely used protocol in the transport layer on the Internet (e.g. HTTP, and SMTP), plays an important role in determining overall network performance The TCP protocol is used by the majority of the networks all our the world. TCP performance is strongly influenced by its congestion control algorithms that limit the amount of transmitted traffic based on the estimated network capacity and utilization. The four algorithms, Slow Start, Congestion Avoidance, Fast Retransmit and Fast Recovery.

When a TCP connection first begins, the Slow Start algorithm initializes a congestion window to one segment, which is the maximum segment size (MSS) initialized by the receiver during the connection establishment phase. When acknowledgements are received by the receiver, the congestion window increases by one segment for each acknowledgement returned. Thus, the sender can transmit the minimum of the congestion window and the advertised window of the receiver, which is simply called the transmission window. At some point the congestion window may become too large for the network or network conditions may change such that packets may be dropped. Packets lost will trigger a timeout at the sender. When this happens, the sender goes into congestion avoidance.

In the Congestion Avoidance algorithm a retransmission timer expiring or the reception of duplicate ACKs can implicitly signal the sender that a network congestion situation is occurring. If congestion was indicated by duplicate ACKs, the Fast Retransmit and Fast Recovery algorithms are invoked.

When three or more duplicate ACKs are received, the sender does not even wait for are transmission timer to expire before retransmitting the segment (as indicated by the position of the duplicate ACK in the byte stream) If however more than two duplicate ACKs are received by the sender, it is a strong indication that at least one segment has been lost. This process is called the Fast Retransmit algorithm.[1]

Fast Recovery algorithm is invoked when duplicate ACKs are being received, the TCP sender knew explicitly that data is flowing to receiver. So there is no congestion. Rather than start at a window of one segment as in Slow Start mode, the sender resumes transmission with a larger window, incrementing as if in Congestion Avoidance mode [2]. This allows for higher throughput under the condition of only moderate congestion.

Different new algorithms had been developed using idea of Fast Retransmit and Fast Recovery such as Reno and new Reno. Most of New method developed for congestion control are based on idea additive increment multiplicative decrement (AIMD) algorithm. Being a window-based algorithm, TCP controls the send rate by maintaining a window size variable W, which limits the number of unacknowledged packets in the network from a single user. This window size is adjusted by the AIMD algorithm in the following manner: W is increased by α/W(α = 1 for standard setting) for each ACK, and thus is increased by a constant a/β per round trip time (RTT) if all the packets are acknowledged within an RTT, where b is the number of packets acknowledged by each ACK (b = 1 for original TCP, and b = 2 for delayed ACK [3]). On the other hand, W is decreased by a fixed proportion βW(β =1/2 for standard setting) once some packets are detected to be lost in the last RTT. With help of this algorithm, senders probe the network for spare bandwidth by cautiously increasing their send rates, and sharply reduce their send rates when congestion is detected. Along with other features like slow start, fast recovery, and fast retransmission, TCP achieves congestion control successfully in the current low speed networks. However, the current TCP can perform poorly in networks with high bandwidth-delay product (BDP) paths, since the AIMD algorithm, being very conservative, is not designed for large window size flows. First, it takes too long time for a large window size user to recover after packet loss is detected and the bandwidth is not effectively utilized [4].

Several alternatives to current versions of TCP have been proposed for implementation in high-speed networks. Some require the modification to router algorithms also, like XCP and some modify the sender side only, like HSTCP Scalable TCP, TCP Vegas, and Compound TCP [5]. Although each of these has shown advantages over standard TCP in some aspects, none of them have yet provided convincing evidence that they are overwhelmingly better than standard TCP and are suitable for general deployment.

In this paper, we introduce the TCP-Illinois algorithm, which uses packet loss information as the primary congestion signal to determine the direction of window size change (whether window size should be increased or decreased), and uses queueing delay information as the secondary congestion signal to adjust the pace of window size change (the amount of window size increment or decrement). We then show that how TCP Illinois can be configure in Linux in order to have maximum throughput for receiver by downloading file and using wire shark for analyzing packets.

II. THE TCP-ILLINOIS PROTOCOL

Since we know that TCP Illnois use idea of AIMD algorithm, where decrease and increase parameters are based upon estimation of buffer size and packet queuing delay.

To achieve a better throughput in network we need to know Whether congestion is imminent or not. And the only congestion indicating information is queuing delay.

The key idea is the following: when the average queueing delay da is small, the sender assumes that the congestion is not imminent and sets a large a and small b; when da is large, the sender assumes that the congestion is imminent and sets a small a and large b. As a result, a= f1(da) and b= f2(da), where f1(·) is decreasing and f2(·) is increasing.

Any combination of increasing f1(·) and decreasing f2(·)

Since we know that TCP-Illinois is a special form of AIMD algorithms in which we have two functions of f1(·) and f2(·).

In the congestion avoidance phase, the sender measures RTT T for each acknowledgement, and average the RTT measurements over the last W acknowledgements (one RTT interval) to derive the average RTT Ta. The sender records the maximum and minimum (average) RTT. ever seen as Tmax and Tmin, respectively, and computes the maximum (average) queueing delay dm =Tmax−Tmin and the current average queueing delay da = Ta−Tmin.

The sender picks the following parameters: 0 < amin ≤ 1≤ amax, 0< bmin ≤ bmax ≤1/2,Wthresh >0, 0≤ h1 <1, 0 ≤ h2 ≤ h3 ≤ 1. The sender sets di = hidm (i= 1,2,3), computes ki (i=1,2,3,4) and computes aand b.

W ←W + a/W for each ACK.

W ←W − bW, if in the last RTT there is packet loss

detected through triple duplicate ACK.

Once there is a timeout, the sender sets the slow start threshold to be W/2, enters slow start phase, and resets a= 1 and b= 1/2, and a and b values are unchanged until one RTT after the slow start phase ends.

When no queueing delay is detected, the rate of additive increase (AI) is fixed at 10 packets per RTT; as the estimated queueing delay rises the AI rate is gradually reduced to 0.3 packets per RTT when the estimated queueing delay is maximal when network buffers are estimated to be full.

III. EXPERIMENTAL SETUP

These experiment of tuning Illinois congestion control algorithm were performed in Linux kernel 2,6,4,5.

During these experiments we download a file of size 100 MB is downloaded from ...........

As file is downloaded different graphs are obtain and valuable information of Link Delay Slow Start, Link Bandwidth and window size. Throughput Graph give all over performance of Link. On our first Downloading file we did not change any parameters.

Then we change our parameters by increasing our Receiver Buffer Size. And also Sender Window. Such That

### References

- Van Jacobson. Modified TCP Congestion Control Avoidance

Algorithm. end-2-end-interest mailing list, April 30, 1990.

- M. Allman, V. Paxson, and W. Stevens. TCP Congestion Control, ,RFC 2581.

- W. Stevens. TCP/IP Illustrated, Vol.1 The Protocols. Addison-Wesley,

- S. Floyd. Highspeed TCP for large congestion windows. Internet

draft, draft-floyd-tcp-highspeed-01.txt, December 2003,

- J. U. Duncombe, "Infrared navigation—Part I: An assessment of feasibility (Periodical style)," IEEE Trans. Electron Devices, vol. ED-11, pp. 34-39, Jan. 1959.

- Circuits and Systems Theory, New York, 1994, pp. 8-16.

- G. R. Faulhaber, "Design of service systems with priority reservation," in Conf. Rec. 1995 IEEE Int. Conf. Communications, pp. 3-8.

- N. Kawasaki, "Parametric study of thermal and chemical nonequilibrium nozzle flow," M.S. thesis, Dept. Electron. Eng., Osaka Univ., Osaka, Japan, 1993.

- J. P. Wilkinson, "Nonlinear resonant circuit devices (Patent style)," U.S. Patent 3 624 12, July 16, 1990.

- IEEE Criteria for Class IE Electric Systems (Standards style), IEEE Standard 308, 1969.