# Telecommunication services are using Internet as single network for voice

### I. Introduction

The Internet these days is undergoing a rapid change from simple point-to-point best-effort communication toward a multiservice network that supports a number of multimedia applications and services with prospectively greater bandwidth need.

The development of increasingly high bandwidth links has created possibilities for Internet Service Providers to go for a tactic of bandwidth over provisioning in the networks. On the other hand, this technique presently applies only to the core network and the need from rapidly increasing end-user IP traffic over the Internet as a whole still cannot be met [5].

The calculation results published in [4] show that bottlenecks of the Internet backbone are not only seen at inter-domain links between autonomous systems, but also within separate domains. With this knowledge, it still is necessary for Internet service providers to do effective resource optimization both intra and inter-domain levels, so as to remove these bottlenecks. Internet traffic engineering is the strategy of doing this job.

Two main problems that have shortly got notice in traffic engineering techniques are QoS and robustness [5]. First, a lot of the recent multimedia applications and services not only have bandwidth requirements, but also require other QoS assurances, like end-to-end delay, jitter or packet loss likelihood. These QoS requirements put new challenges on Internet service providers. Therefore the end-to-end QoS requirements should be fulfilled by traffic engineering mechanisms. Second, due the fact that network node and link failure are still common things on the Internet, traffic engineering mechanisms considers how to reduce the impact of failures on network performance and resource utilization.

To the best of our knowledge, most of the work done so far in the field of IP traffic engineering is on the optimization of network utilization under different network conditions like heavy load, etc. Very little work has been done in addressing the issue of end-to-end QoS assurance. Even researchers who have addressed the end-to-end QoS have presented enhancement and optimization techniques focusing on division of bandwidth resources among multiple competing DiffServ traffic classes.

As more and more delay-, jitter- and loss-sensitive Internet applications are developed to meet the sudden shift of voice, video and mission critical data services from legacy Public Switched Telephone Network (PSTN), Asynchronous Transfer Mode (ATM), and Frame Relay Networks to the world of IP (Internet). The development of new, and optimization of existing QoS assurances models, is the order of the day. MPLS has emerged as a single protocol which provides platform to comply QoS assurances. MPLS traffic engineering and DiffServ, when combined together, enable researchers to achieve bandwidth assurance models. But these models do not completely provide such QoS assurances.

Therefore, it is the right time to devise QoS assurance models which also satisfy the needs of delay-, jitter- and loss-sensitive Internet services along with services with high bandwidth requirements. This can be achieved using MPLS DiffServ Traffic Engineering. Some of the work already done addressing QoS is presented in [1, 2 and 3].

Moreover, as internet is growing at a great pace, the need to optimize the Internet traffic will remain a research catching issue in the predictable near future. This issue has not and will not be solved merely by bandwidth over provisioning. Congestion avoidance and throughput optimization models need also be worked out

### II. RESEARCH POBLEM

Quality of Service (QoS) assurance for IP traffic has been research focus for the last many years. Researchers have worked on many different aspects of QoS. Although substantial successes have been achieved in many aspects, there are still more to be done due to the everyday changing nature of IP traffic.

Internet has to handle more packet loss sensitive IP traffic, real-time video transmission in the form of video conferencing and web streaming are increasing parts of IP traffic; just like voice, which has been shifted from traditional Public Switched Telephone Network (PSTN) to IP networks by placing voice gateways and soft switches. Mission critical data traffic needs to be transmitted in real time between different hosts and systems across the IP network. Packet loss should be minimal during transmission from source to destination.

### III. RELATED WORK

Recent research work done on different aspects of Intra-Domain IP/ MPLS Traffic Engineering is Briefly Overviewed as follows

A generalized MPLS routing optimization can be devised as a multi-priority flow problem [6], and so that it can be solved using linear programming to produce an optimal solution for routing mechanisms that allow arbitrary traffic splitting. However, this method is frequently considered as impractical, particularly in a large-scale network, as the number of LSPs needed is would be enormous due to random traffic division. To get a more scalable traffic engineering solution, traffic division has to be limited in scope. An early MPLS-based traffic engineering method used simple constraint-based routing (CBR) [7] without coordination between individual traffic trunks [8]. One of such CBR algorithm is as follows. As an LSP being set for a particular traffic trunk, the links which do not fulfill the constraints are removed from the topology database. Then, shortest path routing (SPR) is then performed on the remaining network topology, and the shortest path is assigned to the LSP. These steps are repeated until all trunks are assigned to LSPs. This routing algorithm is called Constrained Shortest Path First (CSPF) routing. Some optimizations have also been proposed to add new capabilities like, Widest Shortest Path (WSP) and Shortest Widest Path (SWP) [9, 10]. These two algorithms somewhat optimize the bandwidth availability at congested links. Application of WSP/SWP, increases the chances of network traffic to find a feasible path and also congested links are avoided by sparing bandwidth for upcoming needs, rest of traffic is benefited from this routing technique. There are many MPLS-based traffic engineering techniques have been presented to reduce the maximum link utilization. In [11] traffic engineering has been evaluated by using single and multiple paths.

With the development of differentiated services (DiffServ), DiffServ-based traffic engineering has become a research area for supporting QoS differentiation. DiffServ-MPLS-based traffic engineering has now been supported by many Vendor routers, CSPF being the basic routing algorithm. More complex DiffServ aware/equivalent MPLS-based traffic engineering schemes have also been proposed [12-14]. In [13] a general outline for intra-domain QoS assurance by MPLS-based traffic engineering in DiffServ networks.

Online MPLS-based traffic engineering can be categorized into two distinct categories: dynamically adjusting the traffic division ratio among pre-constructed static LSPs, and computing dynamic LSPs in real time for each new traffic trunk demand. MATE [15] is a typical example of the first category, and its basic procedure is to adaptively send incoming traffic onto multiple pre-constructed LSPs as per network core traffic statistics. In this traffic engineering model, routing optimization is not directly addressed, and optimization is gained by online sending adaptation. CSPF, WSP, and SWP algorithms are the basic routing methods that can be applied to online MPLS-based TE strategies.

Dynamic Online Routing Algorithm (DORA) [16] through the online traffic engineering method is performed in two stages; stage one is performed whenever there is any topology changes in the network. And second stage path is performed whenever there is a request for LSP setup. In the first stage a Path Potential Value (PPV) is assigned to each link for each source to destination node pairs. PPV is the parameter which shows the number of times a link can be used for future path setup request. The higher PPV value indicates the higher are the chances for a link to be utilized for multiple future paths, so to avoid this link to be allocated for future path requests. Finally, a conventional Dijkstra's shortest path algorithm is applied based on the set of defined link weights.

Simple Minimum Interference Routing Algorithm (SMIRA) [17] resolves the issue of LSP interference, setting up LSPs using CSPF without taking the location of ingress/egress nodes pairs into consideration. It is expected that congestions may occur in a few links that are used by multiple LSPs. So SMIRA, and before that MIRA, solved this problem by avoiding critical links while setting up of LSP, and spare these critical links for future traffic that will use critical link as the only path for Ingress/Egress pairs. This algorithm first distinguishes critical links for individual ingress/egress pairs by calculating the maxflow value. After that, weight is calculated for each ingress/egress pair, as a rising function criticality of the link. Finally, CSPF algorithms are applied to the network topology containing only feasible links that can support the bandwidth demand of the incoming traffic.

Online MPLS-based traffic engineering has also been studied in DiffServ environments for QoS support, a typical example being traffic engineering automated manager (TEAM). The Traffic Engineering Tool (TET) in the TEAM framework is responsible for LSP preemption and construction.

Survivable online traffic engineering in MPLS networks has also been considered. Similar to MIRA, this scheme constructs LSPs dynamically by applying the shortest path algorithm to the dedicated link weight metric that reflects the specific traffic engineering requirement. This type of dynamic link metric is based on a Lost Flow in Link (LFL) function that is used to assign working routes with local restoration. In LFL the metric of a particular link reflects the change in the objective function if an incremental demand has been (re)routed through or even near that particular link [5].

### IV. A PROPOSED SOLUTION/ network setup

Different ways have been introduced over time to address each of the above problems. DiffServ was introduced to classify IP traffic into multiple classes on the bases of their QoS requirements. MPLS traffic engineering has been used to gain the knowledge of network state and utilize this control the traffic admission and routing in the IP network. If we use DiffServ and MPLS traffic engineering together, QoS assurance can be enhanced for multimedia IP traffic.

We have setup a network topology of seven routing nodes in NS2. We have used two source nodes to generate traffic and these two nodes are connected to MPLS domain edge router-1 with 100mbps DropTail links. Core routers are connected by DiffServ enabled links of varying bandwidth. We have used five nodes as DiffServ MPLS TE enabled. Destination node is connected to DiffServ MPLS TE enabled core by 10mbps DropTail link.

After enabling MPLS on core nodes, we have established LDP peering sessions among in a full mesh manner to enable Traffic Engineering. To classify IP traffic into multiple FEC (forwarding equal lance classes) having different QoS parameters configured between the edge and core links. DiffServ and FEC are responsible for categorizing the traffic.

CBR (constant bit rate) traffic generating applications were attached to both source nodes; to use UDP at the transport layer we attached UDP agents with CBR applications and source nodes. Then source nodes and destination node applications connected to generate traffic and receive traffic respectively.

### V. Research Methodology

Our work is based on the development of QoS enhancement model using DiffServ and MPLS TE and then testing with the help of NS2 simulation.

In our work after setting up the network topology and configuring certain QoS parameters in DiffServ and MPLS TE, we generated CBR traffic over the UDP transport layer and routed to destination the DiffServ and MPLS enabled core. Following but not limited to scenarios have been deployed and tested for reducing packet loss for QoS sensitive traffic.

- DiffServ we used to admit and classify traffic at the Edge 1 router connected to two traffic source nodes. When traffic from source-2 was also injected to the network, we observed packet drops for low priority FECs, depicted in below figure.

- MPLS TE used to carry differentiated traffic in the second scenario over the under utilized link to reduce packet loss.

- MPLS TE again used to route the traffic to better path as soon it got available to further reduce packet loss observed in scenario 2.

Observations and results are discussed in following section.

### VI. RESULTS AND DISCUSSION

The results obtained from our simulation shows the general trend of reducing over all packet loss for high priority traffic.

When we injected traffic more than what a simple DiffServ network without MPLS traffic engineering, packet drops was observed as shown in first table below. We can see that high priority traffic has experienced less packet loss than low priority traffic classes 20 to 22. Code points have been assigned to different traffic classes at the edge of network and traffic is handle based on these code points, lower the code point number the higher the priority of traffic flow.

Table-1 Packets Statistics DiffServ

| CP | TotPkts | TxPkts | Ldrops | edrops |
| --- | --- | --- | --- | --- |
| All | 690 | 514 | 69 | 7 |
| 10 | 36 | 36 | 0 | 0 |
| 11 | 117 | 117 | 0 | 0 |
| 12 | 193 | 190 | 0 | 3 |
| 20 | 104 | 80 | 24 | 0 |
| 21 | 94 | 75 | 19 | 0 |
| 22 | 46 | 16 | 26 | 4 |

In our 2nd network scenario where we used DiffServ along with MPLS TE packet loss has been greatly reduced for flows CP 20 and 21, where as all the packets are dropped for flow having least priority. Results are shown in Table-2 below.

Table-2 Packets Statistics MPLS TE-1

| CP | TotPkts | TxPkts | Ldrops | edrops |
| --- | --- | --- | --- | --- |
| All | 639 | 558 | 73 | 8 |
| 10 | 51 | 51 | 0 | 0 |
| 11 | 104 | 104 | 0 | 0 |
| 12 | 109 | 109 | 0 | 0 |
| 20 | 124 | 124 | 0 | 0 |
| 21 | 140 | 140 | 0 | 0 |
| 22 | 111 | 30 | 73 | 8 |

In our 3rd network scenario where we also used DiffServ and MPLS TE but in this case we have utilized even better path after getting information about the available network resources. So, here we don't observe any pack dropped for all traffic classes.

Table-3 Packets Statistics MPLS TE-2

| CP | TotPkts | TxPkts | Ldrops | edrops |
| --- | --- | --- | --- | --- |
| All | 845 | 845 | 0 | 0 |
| 10 | 43 | 43 | 0 | 0 |
| 11 | 127 | 127 | 0 | 0 |
| 12 | 181 | 181 | 0 | 0 |
| 20 | 145 | 145 | 0 | 0 |
| 21 | 148 | 148 | 0 | 0 |
| 22 | 201 | 201 | 0 | 0 |

### VII. CONCLUSION AND FUTURE WORK

Increasing dependency of communication services on the internet packet based backbone requires QoS guarantees. Using internet (IP/MPLS) network infrastructure for voice, video and data services provide tremendous benefits in terms of cost and global presence. There are many challenges for the researchers to ensure QoS guarantees. In out study, we have deployed DiffServ and MPLS TE together to reduce the over all packet drops to ensure QoS. In future our aim is to extend our work to ensure QoS for delay and jitter sensitive traffic.

### REFERECNCES

[1] D. Zhang, Ionescu “QoS Performance Analysis in Deployment of DiffServ-aware MPLS Traffic Engineering,” Eighth ACIS International Conference, Volume 3,pages 963-967, July 30 2007-Aug. 1 2007

[2] Z. Li, Z. Zhang, L. Wang “A novel QoS routing scheme for MPLS traffic engineering,” Communication Technology Proceedings, 2003. ICCT 2003. International Conference, Volume 1,9-11 April 2003

[3] T. Kim, J. Yoo, H. Jung, H. Lee, S. Jin “Signaling for traffic engineering with QoS guarantee in IP environment,” Advanced Communication Technology, 2005, ICACT 2005. The 7th International Conference

[4] N. Hu, L. Li, Z.M. Mao, P. Steenkiste, J. Wang “Locating Internet Bottlenecks: Algorithms, Measurements and Implications,” Proc ACM SIGOMM, 2004, pp.41-54

[5] N. Wang, K. Ho, G. Pavlou, M. Howarth “An Overview of Routing Optimization for Internet Traffic Engineering” IEEE Communications Surveys 1st Quarter 2008, Volume 10, No.1

[6] D. Mitra, K. G. Ramakrishnan “A Case Study of Multiservice, Multipriority Traffic Engineering Design for Data Networks,”Proc. IEEE GLOBECOM, 1999, pp. 1077-83.

[7] O. Younis, S. Fahmy “Constraint-Based Routing in the Internet: Basic Principles and Recent Research,” IEEE Commun. Surveys & Tutorials, 3rd qtr., 2003, pp. 2-13.

[8] X. Xiao, A. Hannan, B. Bailey, L.M. Ni “Traffic Engineering with MPLS in the Internet,” IEEE Network, vol. 14, no. 12, Mar./Apr. 2000, pp. 28-33

[9] Z. Wang, J. Crowcroft “Quality of Service Routing for Supporting Multimedia Applications,” IEEE JSAC, vol. 14, no. 7, Sept. 1996, pp. 1228-34.

[10] R.A. Guerin, A. Orda, D. Williams “QoS Routing Mechanisms and OSPF Extensions,” Proc. IEEE GLOBECOM 1997, pp. 1903-08.

[11] Y. Wang, Z. Wang “Explicit Routing Algorithms for Internet Traffic Engineering,” Proc. IEEE ICCCN, 1999, pp. 582-88.

[12] F.L. Faucheur, W. Lai “Requirements for Support of Differentiated Services-aware MPLS Traffic Engineering,” IETF RFC 3564, July 2003.

[13] P. Trimintzios, T. Baugé, G. Pavlou, P. Flegkas, R. Egan “Quality of Service Provisioning through Traffic Engineering with Applicability to IP Based Production Networks,” Comp. Commun., vol. 26, no. 8, May 2003, pp. 845-60.

[14] V. Tabatabaee, B. Bhattacharjee, R.J. La, M.A. Shayman “Differentiated Traffic Engineering for QoS Provisioning,” Proc. IEEE INFOCOM, 2005, pp. 2349-59.

[15] A. Elwalid, C. Jin, S. Low, I. Widjaja “MATE: MPLS Adaptive Traffic Engineering,” Proc. IEEE INFOCOM, 2001, pp.1300-09.

[16] R. Boutaba, W. Szeto, Y. Iraqi “DORA: Efficient Routing for MPLS Traffic Engineering,” J. Network and Sys. Mgmt., vol. 10, no. 3, Sept. 2002, pp. 309-25.

[17] I. Iliadis, D. Bauer “A New Class of Online Minimum-Interference Routing Algorithms,” Proc. Second International IFIP-TC6