# The Wi-Max standards

### CHAPTER 2 LITERATURE SURVEY

The Wi-Max standards given as IEEE (802.16) delineate the physical layer and medium access layer specifications for a broad band wireless network. The physical medium is bifurcated into frames of constant length. Each frame is segmented into downlink and uplink sub frames to link up in network traffic.

The construction of the frame underlie in the physical layer. A numerous physical layers defined for various operational environments by the standards. Depending on the various carrier modulations different physical layers are defined.

- Wireless MAN-SC for a frequency 10-66 GHz band depending on single carrier modulation.

For the frequencies less than 11 GHz three alternative physical layers are defined

- Wireless MAN-SCa with a single carrier modulation

- Wireless MAN-OFDM with a orthogonal frequency division multiplexing

- Wireless MAN-OFDM with a orthogonal frequency division multiple access

The IEEE(802.16) standard endorse two duplexing techniques.

- FDD in which downlink and uplink sub frames with distinct frequencies takes place at same time.

- TDD in which downlink and uplink sub frames takes place at distinct time and with a similar frequency.

The medium access layer is divided into three sub layers, they are

- Convergence sub layer

- MAC common part sub layer

- Security sub layer

The convergence sub layer is amenable for receiving Protocol data units from a higher layer and assigning them to a reserved connection, processing and distributing to appropriate MAC Service access point.

The basic MAC functionalities provided by common part sub layer includes establishment of connection, management, generation of MAC management messages, ranging, registration, service flow management scheduling services and registration.

The wireless medium is distributed along dual modes are defines as

- PMP mode in which subscriber stations convey to each other by a Base station

- Mesh mode in which stations are configured in an ad-hoc fashion and convey each other directly.

In connection oriented communication the network packets are distributed in the ways of connection and the MAC protocol is defined as a connection oriented communication.

The connections are defined in two different ways.

- Transport connections for data transmission

- Management connections for transmitting control messages

An initial ranging phase is included in the registration phase in which management messages RNG-REQ and RNG-RSP are switch between SS and BS.On receiving RNG-REQ the BS verifies parameters such as power level.

To transmit and receive control messages these connections are then used.

A set of control messages are defined by MAC which are called as management messages and the important messages are DL-MAP, UL-MAP, DCD and UCD.

When a Base station broadcasts messages then downlink MAP and uplink MAP defines the access to the sub frames of Downlink and Uplink of current frame.

These message headers contain a set of information in which each specifying an SS of the DL or UL grant assigned to it. These are preceded by a set of DCD and UCD messages which include a set of general information about the channel and a pack of burst profiles, Each burst profile determines a set of parameters that are used to send and receive data in a given profile of down link and uplink grant. A complete set of data is carried under transport connections. There is a peer to peer relationship between a service flow and a transport connection. A service flow determines a unidirectional flow of data traffic and binds it with a set of QoS parameters.

The standard supports a huge set of QoS parameters. A service flow is created by set of special MAC management messages DSA-REQ and DSA-RSP which are exchanged between SS and BS. The standard classified a set of four scheduling services and are given as UGS (Unsolicited Grant Service), rtPS (Real-Time Polling Service), nrtPS (Non-Real-Time Polling Service) and BE (Best Effort).

Unsolicited grant service is created for a real time application with a constant size of packets. Real time polling service is created with a variable size packet on interval basis for real time applications. Real time polling service is different from UGS and is polled by the base station on interval basis allowing to send bandwidth requests. The request is accomplished based on the available bandwidth. For delay tolerat applications non real time polling service is created. Even in heavy network congestion conditions the non real time polling services is ensured with a minimum bandwidth by polling it on a regular basis. For HTTP and Email services best effort is designed and it does not guarantee a minimum bandwidth. An additional class of ertPS(extended real time polling service has introduced by the IEEE 8.2.16e amendment cascade the features of UGS and rtPS allowing unsolicited grants for variable packet size applications. A bandwidth request is accomplished by sending a bandwidth request packet.

A bandwidth request packet is sent by a special transmission which is allocated in uplink sub frame .A response is given by the BS with a grant allocated in subsequent frames. A bandwidth is requested on per connection basis but assigned on per SS basis. Then the responsibility is taken by SS to decide which connection will transmit in a defined grant. In the similar fashion BS scheduler selects packets which will be transmitted in DL sub frame. A manufacturer defines all the scheduling algorithms and this standard does not interfere in defining scheduling algorithms.