# The internet traffic

### Chapter 4

### Forward Error Correction in supporting Video Streaming over the Internet

### 3.1 Introduction

The Internet traffic suffers from heavy losses due to network congestion caused by the limited capacity of queues in the routers, when all the bits currently in transit on that link will be lost. Error control correction is used to reconstruct the lost data by either retransmission of data from the sender using ARQ or by adding redundant data using FEC. FEC is a method of error control correction, used to correct the error in data transmission by adding redundant data at the sender, receivers detect the error and reconstruct lost data from redundant data without the retransmission of lost data from the sender. Several drawbacks are attached to the use of FEC. First, FEC cannot recover all lost packets. In addition, the transmission of redundant packets increases the overall network load. Finally, the effectiveness of FEC is known to depend on the way packet drops are distributed in the data stream. FEC is more efficient when packet losses are independent. In this chapter, we will elaborate the efficiency of FEC packet level mechanisms in improving video streaming quality over a best-effort network.

This chapter is organized as follows. In section 4.2, we describe how packet losses occur in the network due to congestion, and explain the most popular queue policies. In section 4.3, we show the FEC mechanism. In section 4.4, we are going to evaluate FEC over a best-effort network and show how FEC can improve the video streaming quality. Lastly, section 4.5 summary of this chapter.

### 4.2 Packet losses

The most notable and common problem that networks are faced with is loss of packets. Packet loss is the failure of one or more transmitted packets to arrive at their destination. Packet loss has noticeable effects in all types of digital communications. Packet loss can cause severe damage of received data, broken-up images, incoherent speech or even the complete absence of a received signal. Therefore, packet loss is one of the most significant QoS performance metrics for multimedia applications.

Packet loss occurs when packets are damaged and discarded due to queue capacity of intermediate network devices being exceeded, which results in packets being dropped. This point explains one of the primary reasons for packet loss.

### 4.2.1 Congestion

Congestion in the network is the most common reason for packet loss [1] [2]; congestion refers to the loss of network performance when a network is heavily loaded. This loss of performance can be packet loss, and large delays in data transmission, which is often unacceptable.

Congestion occurs in a router when the aggregate bandwidth of incoming packets, destined for a particular output link, exceeds the link's bandwidth. An example of congestion occurring at a router is given in Figure 4.1.

There are two types of congestion: transient and persistent. Transient congestion can be managed with a buffer queue at the router. During to the congestion period the queue will grow and contain the excess packets. When the congestion period ends, the buffered data is forwarded to the appropriate output link. On the other hand, persistent congestion is said to occur when the data overflows the buffer. While transient congestion only introduces a delay in data transmission, persistent congestion results in data loss.

Congestion usually occurs at any particular router. Selected appropriate router queue policy management effects can help, in which congestion is avoided in a network and that reduces packet loss. Also the appropriate buffer size or queue limit of a router can help as well. Later in this chapter we are going to investigate the effect of router queue policy management and queue limit in the number of packet losses and show how FEC can reconstruct the lost packets, and find the correlation between these factors and FEC.

### 4.2.2 Queue Policies Mechanisms

Queue policies mechanisms refer to traffic policies techniques at a router that detect and notify traffic sources of imminent network congestion to prevent outbound buffer overflow and control queuing delay [3]. When notified of network congestion, cooperative traffic sources like TCP reduce their transmission rates to participate in the congestion control. In that case network congestion cannot be managed voluntarily by the traffic sources, Queue policies may use buffer management techniques to suppress traffic to the targeted traffic level and achieve the QoS goal.

Traditional Internet routers employ TailDrop (TD) queue management, discarding arriving packets if the buffer of the output port overflows. A new queue management policy proposed [4], called RED, was to improve the Tail Drop policy. In the following subsection we explain each policy.

### 4.2.2.1 Drop Tail

DT is a simple queue policy algorithm used by Internet routers to decide when to drop packets. In contrast to the more complex algorithms like RED, with DT all the traffic is not differentiated. Each packet is treated identically. With TD, when the queue is filled to its maximum capacity, the newly arriving packets are dropped until the queue has enough room to accept incoming traffic. The DT has two disadvantages:

- Lock-out:

- Full Queue

The solution to the full-queues problem is for routers to drop packets before a queue becomes full, so that end nodes can respond to congestion before buffers overflow. We call such a proactive approach, by dropping packets before buffers overflow, active queue management allows routers to control when and how many packets to drop. The next section introduces RED, an active queue management mechanism that solves both problems listed above.

### 4.2.2.2 Random Early Detection

RED [4] is the most studied active queue policy mechanism on the Internet. RED solves the full queue drop packets by using the average queue size as the indication of emerging congestion. The RED algorithm drops arriving packets probabilistically. The probability of drop increases as the estimated average queue size grows. If the queue has been mostly empty in the recent past, RED will not tend to drop packets unless the queue overflows. On the other hand, if the queue has recently been relatively full, indicating persistent congestion, newly arriving packets are more likely to be dropped.

The RED algorithm consists of two main parts: [3].

- Estimation of the average queue size RED estimates the average queue size, either in the forwarding path using a simple exponentially weighted moving average.

- For the decision to drop an incoming packet, RED decides whether or not to drop an incoming packet. It is RED's particular algorithm for dropping that results in performance improvement for responsive flows. There are two RED parameters, minth (minimum threshold) and maxth (maximum threshold).

RED effectively controls the average queue size while still accommodating bursts of packets without loss. RED's use of randomness breaks up synchronized processes that could lead to lock-out phenomena.

### 4.3 FEC Mechanism

FEC has been proposed to recover packets losses in real time applications audio and video based on the redundant information. A number of forward error correction techniques have been developed to repair losses of data during transmission [5] [6] [7] [8]. FEC enables the receiver to correct losses without dealing with the sender.

FEC sends original and redundant data as a block of FEC (n, k), where k is the number of data packets in a FEC block and n is the number of all the packets in the FEC block. We can calculate the encoding rate using formula 1.

R is the encoding rate of block. Codes that introduce less redundancy have higher code rates, and transmit more information per code bit.

### 4.3.1 FEC Approaches

There are two approaches of FEC design to recover data packets from losses, media dependent or media-specific and media independent. Figure 4.2 shows the way to use the media-dependant or media-specific FEC. Figure 4.3 shows the media-independent FEC.

Media dependent FEC works against packet loss by transmitting each packet more than one time. When a packet is lost, one of its extra packets is able to restore it as shown in figure 4.2. The first packet transmitted of audio or video packet is the main encoding because it has the best quality. Duplicates of this packet is the minor encoding because the sender is able to decide if the quality or bandwidth of this packet should be the same or lower than the main encoding packet.

Media- independent FEC does not need to know what is inside the contents of the stream. Block or algebraic codes are transmitted to help repair what was lost. There are k data packets in a codeword and n-k extra check packets are transmitted for n packets that need to be sent over the Internet.

### 4.3.2 FEC Codes

Error correction data generate the bits from either parity coding, or R-S recovery technique is used to assist checking for entire packets lost. There are two block coding schemes that are used across the equivalent bits in blocks of packets. Media-independent FEC has two types, block codes and convolutional codes.

FEC Codes are commonly divided into two classes, block codes and convolutional codes. Block codes are based on finite field arithmetic and abstract algebra. They can be used to either detect or correct errors. Block codes consist of a block of K information bits producing a block of n coded bits. By encoded rules, n-k redundant bits are added to the k information bits to form the n coded bits. Generally, these codes are referred to as (N, K) block codes. Some of the regularly used block codes are Hamming codes [9], BCH codes [9], and R- S codes [10].

Convolutional codes are developed with a mathematical structure and are mainly used for real time error correction. Convolutional codes convert the entire data stream into one single codeword the encoded bits depend not only on the current k input bits, but also on past input bits. The main decoding strategy for convolutional codes is based on the widely-used Viterbi algorithm [11]. Figure 4.4 shows the FEC codes categories.

### 4.3.3 Reed-Solomon Codes

Many researchers have considered using erasure codes to recover packet losses [12] [13] . In such approaches, a video stream is first partitioned into segments; each segment is packetized into a group of m packets. A block code is then applied to the m packets to generate additional redundant packets resulting in an n-packet block, where n = m + l. With such a code, the receiver can recover the original m packets if a sufficient number of packets in the block are received. The most commonly studied erasure codes are RS codes [14], which have good erasure correcting properties and are widely used in practice [12] [13].

The block-based error correcting codes comes with a wide range of applications in digital communications. R-S codes are non-binary cyclic, The R-S decoder processes each block to correct errors and repair the original data. The number of errors that can be corrected depends on the characteristics of the R-S code. A R-So code is specified as RS (N,K).

A R-S decoder can correct up to T symbols that contain errors in a codeword. We can compute T by using the following formula:

N is the number of all the packets in the FEC block (block size). This can be computed using the following formula.

M - bit symbols

K is the number of data packets in a FEC block, and can be computed using the following formula:

### 4.4 Evaluation of the Current FEC Mechanism

The main purpose of this chapter is to examine the current FEC mechanism then propose an improved FEC mechanism. In order to study the effects of the Media-independent FEC packet level mechanism in improving video streaming quality, we conducted two simulation experiments. The first experiment studied the FEC with the Drop Tail queue policy. The second experiment studied the FEC with the RED queue policy.

### 4.4.1 Experiment 1 (FEC with Drop Tail)

Most packet losses in the current Internet are due to congestion caused by the limited queue size and queue policy in the router. In this experiment, we studied the Media-independent FEC packet level mechanism with Drop Tail for improving video streaming quality when the losses occur due to congestion with different queue sizes and different amounts of flow; packet losses due to congestion have been studied in [1] [15] [16] [2] [17]. FEC for packet recovery states that the added redundancies increases the network load and this makes the performance bad in a state where congestion is an important factor. To observe how FEC can improve the video streaming quality in the presence of packet loss due to congestion losses, the experiment was run to start the simulations for different scenarios and conditions to validate our results.

### 4.4.1.1 Experiment Design

To study FEC, we conducted a simulation for single bottleneck topology (dumbbell) as show in Figure 4.5. We used the dumbbell topology because it is the most suitable topology for our research [18] . 80% or more of Internet traffic today consists of TCP traffic; we used competing TCP traffic flow to increase the packet losses. The TCP sources connected to R1 with a bandwidth of 10Mbps and 5ms delay, the FTP traffic attached to TCP sources. The FEC sources connected to R1 with a bandwidth of 10Mbps and delay was generated randomly using uniform distribution to achieve the heterogeneous environment of Internet, We used the Constant Bit Rate (CBR) model in ns-2 for video traffic because it closely represents the behavior of real video data, and attached it to FEC and Non-FEC sources.

R1 was connected with R2 with a bandwidth of 5Mbps and a 20ms delay link. These configurations cause congestion and loss at R1 so we can identify the efficiency of the FEC to recover packet losses based on received packets at the receiver. The router in this experiment used the Drop Tail queue policy management, which implements FIFO scheduling and drop-on-overflow buffer management that most Internet routers use because of ease of implementation [19]. Different queue sizes were used at 20, 40, 60, 80 and 100 packets to give the chance of dropping packets when the congestion is accrued and study the FEC with different queue sizes. TCP and FEC receivers are connected to R2 with a bandwidth of 10Mbps and 5ms delay link. This topology is similar to other topologies used by other works [20] [16]. The experiment was run for 100 seconds; the first 20 seconds was ignored due to instability of the simulation in warming up. The reason of running the simulation for 100s was to let the simulation run until it reaches the steady state. And simulations were run for 30 times using a random number generator. The results were presented with a 95% confidence interval. We used an FEC block length of 255, which is a popular FEC code that has been used for both hardware as well as software implementations [21].

### 4.4.1.2 Experiment Results and Discussion

We discussed the simulation results of our experiments; after we analyze the trace file, we presented our results in tables and graphs. We explained each scenario and discussed its results.

### 4.4.1.2.1 Scenario 1: Single Sender

We present the results of simulation experiment in Tables 4.2 and 4.3. Table 4.2 shows the results of a single sender using FEC with DropTail and Table 4.3 shows the results of a single sender without using FEC with DropTail.

Figure 4.6 shows the amount of packet loss for various queue sizes with and without using FEC. From the figure, we can observe that the amount of packet loss with FEC is more than without FEC; the reason is that with FEC we sent redundant packets, these redundant packets increased the sending packet that caused congestion at the router, so the amount of packet loss increases. But still we can reconstruct the lost packets if the lost packets are less than the redundant packets. For example, with the queue size equal to 60 the amount of packet loss with FEC is 156 and the number of redundant packets equals 450, so we can still reconstruct all the lost packets. But without FEC the amount of packet loss is 134; these packets can't be reconstructed cause a bad quality. Also, we can observe that when the queue size increased the packet loss decreased. This is because when the queue size is large it allows for more packets to wait in the queue before the router before starts dropping any packets.

Figure 4.7 shows the packet loss ratio before and after using FEC. We can observe that PLR after FEC is less than before FEC. When queue size is increased the PLR is decreased too. This is because when queue size is large the received packet increased and the PLR is deceased according to PLR formula.

So with FEC the PLR is less, so provides good quality compared to non-FEC.

Figure 4.8 shows the throughput at the receiver with various queue sizes with and without using FEC. We can observe that using FEC produced more throughput than non-FEC. This is because of the added redundant data with the FEC block. As we mentioned the FEC used redundant packets to reconstruct lost packets at the receiver. As the queue size is increased the received packets increase. Large queue sizes provide more throughput and good quality.

Figure 4.9 shows the utilization of bandwidth with various queue sizes with and without using FEC. We observed that using FEC required more bandwidth; extra bandwidth used for the redundant packets when the network does not lose packets, i.e. when queue size is 60 the lost packets is 156 and redundant packets is 450, so 156 lost packets will reconstruct from 450 redundant packets. That means 294 useless packets were sent through the network and these packets required bandwidth to transfer. When the queue size is increased the bandwidth is increased. Because when the queue size increased the lost packets decreased, so receiving packets increased.

Figure 4.10 shows the end-to-end delay with various queue sizes with and without using FEC. We can observe that using FEC increased the end-to-end delay; this is because of the redundant packets. We can see that when queue size increased the delay increased. This because the packets stay a long time till they start forward from the router to the network. Next section we discuss scenario 2.

### 4.4.1.2.2 Scenario 2: Multi-sender

We present the results of the simulation experiment in Tables 4.4 and 4.5, where Table 4.4 shows the results of a multi-sender using FEC with DropTail and Table 4.5 shows the results of a multi-sender without using FEC with DropTail.

Figure 4.11 shows the amount of packet loss for various queue sizes with and without using FEC. We can observe from the figure, the FEC has more loss packets and when the queue size is increased the packet loss decreases. The reason we mentioned in Scenario 1. We see that the number of loss packets increased because the number of senders increased.

Figure 4.12 shows the packet loss ratio before and after using FEC. As we see the FEC has less PLR, because with FEC more packets are received at the receiver.

Figure 4.13 shows the throughput at the receiver with various queue sizes with and without using FEC. We can observe that using FEC produced more throughput than non-FEC. We mentioned the reason in Scenario 1. We can see that more throughputs were produced due to the increased number of senders.

Figure 4.14 shows the utilization of bandwidth with various queue sizes with and without using FEC. We observe that using FEC required more bandwidth. We explained the reason in Scenario 1. The higher amount of bandwidth refers to a higher number of senders.

Figure 4.15 shows the end-to-end delay with various queue sizes with and without using FEC. We can observe that using FEC increased the end-to-end delay. Delay here was increased due to an increased number of senders.

### 4.4.1.3 Conclusion

FEC is useful in improving the video quality with various sizes of the droptail queue policy. The simulation results from Experiment Scenario 1 and 2 showed that FEC can improve the video quality by reconstructing loss packets from redundant packets at the receiver, so these increased the receiver throughput. But the results show that FEC is worse from a network perspective, where it required more bandwidth and increased the end-to-end delay due to redundant packets. The results showed also fixed number of redundant packets worse to network if loss less than redundant and worse to quality if loss greater that redundant.

### 4.4.2 Experiment 2 (Random Early Detection)

In this experiment we studied the FEC packet level mechanism with the RED queue policy in improving video streaming quality when the losses occurred due to congestion at the bottleneck router with different queue sizes. We used the same topology and the same configurations that were used in Experiment 1, we just changed the queue policy from DT to RED. The Table 4.6 shows the RED parameters. These parameters were selected based on "RED: discussions of setting parameters" by Sally Floyd[1].

### 4.4.2.1 Experiment Results and Discussion

We discussed the simulation results of our experiments; after we analyzed the trace file, we presented our results in tables and graphs. We explained each scenario and discussed its results.

### 3.4.2.1.1 Scenario 1: Single Sender

We present the results of the simulation experiment in Tables 4.8 and 4.9. Where Table 4.8 shows the results of a single sender using FEC with RED and Table 4.9 shows the results of a single sender without using FEC with RED.

Figure 4.16 shows the amount of packet loss for various queue sizes with and without using FEC. From the figure, we can observe the amount of packet loss with FEC is more than without FEC, the reason is that with FEC we sent redundant packets; these redundant packets increased the sending packets that caused congestion at the router, so the amount of packet loss is increased. We can observe also when the queue size increased the packet loss decreased. But the packet loss does not decrease a lot as the queue size increases. This is because the RED depends not only on the queue size to drop packets. Packets are dropped before the queue is filled.

Figure 4.17 shows the packet loss ratio before and after using FEC. As we see the FEC has less PLR, because with FEC more packets are received at the receiver.

Figure 4.18 shows the throughput at the receiver with various queue size with and without using FEC. We can observe that using FEC produced more throughput than using non-FEC. We mentioned the reason in Experiment 1.

Figure 4.19 shows the utilization of bandwidth with various queue sizes with and without using FEC. We observed that using FEC required more bandwidth. We explained the reason in Experiment 1.

Figure 4.20 shows the end-to-end delay with various queue sizes with and without using FEC. We can observe that using FEC increased the end-to-end delay.

### 4.4.2.1.2 Scenario 2: Multi-sender

We present the results of the simulation experiment in Tables 4.10 and 4.11. Table 4.10 shows the results of a multi-sender using FEC with RED and Table 4.11 shows the results of a multi-sender without using FEC with RED.

The results of this simulation scenario are almost similar to Scenario 1. The difference is the increase in the value due to the increased number of senders. Therefore we do not discuss these results.

### 4.4.2.3 Conclusion

Again the results show, FEC is useful in improving the video quality with various sizes of the RED queue policy. The simulation results from Scenarios 1 and 2 shows that FEC can improve video quality by reconstructing loss packets from redundant packets at the receiver; these increased the throughput at receiver. But the results show that FEC is worse from a network perspective, where it requires more bandwidth and increases the end-to-end delay. The results showed also fixed number of redundant packets worse to network if loss less than redundant and worse to quality if loss greater that redundant.

### 4.5 Comparison between FEC/TD and FEC/RED

The results of Experiments 1 and 2 have shown that FEC can improve the video quality. Here we show how FEC worked with DT and RED for both scenarios: single sender and multi-sender.

### 4.5.1 Single sender

Figure 4.21 shows the packet loss with DT and RED. We can observe that when queue size increased the DT performed better than RED. As we mentioned, the DT just depends on the queue size parameter to drop the packet, while in RED there are four other parameters than queue size used to drop the packet.

Figure 3.22 shows the throughput with DT and RED. From the figure we can observe that the DT produced more throughput than RED with an increase in queue size. This is because the large DT queue size has less packet loss.

Figure 3.23 shows the bandwidth usage with DT and RED. From the figure we can observe that the DT requires more bandwidth than RED with an increased queue size. This because the large DT queue size has less packet loss so more packets would be transferred.

Figure 3.24 shows the end-to-end delay with DT and RED. From the figure we can observe that the DT produced delay more than RED with the increased queue size.

We can observe that the RED performed better than DT from a network perspective, since the RED required less bandwidth and delay with various queue sizes, while DT performed better than RED from the quality perspective, since the DT had less packet loss and more throughput with various queue sizes.

### 3.5.2 Multi-sender

Figure 4.25 shows the packet loss with DT and RED, Figure 4.26 shows throughput with DT and RED, Figure 4.27 Bandwidth with DT and RED and Figure 4.28 the end-to-end delay with DT and RED. All senders were sending the same packet size and the same number of packets.

These results do not show much difference between the DT and RED. Using an end-to-end delay metric, we showed that RED was more efficient than DT for single and multi-sender. Using the throughput metric, we showed that DT is more efficient than RED.

### 3.5 Summary of Chapter

In this chapter, we have examined the current FEC mechanism with the most popular queue policy use in today Internet routers, DT and RED, conducted using a set of simulation experimental suites. Our simulation results showed that FEC can improve the video quality by reconstructed packet losses caused by congestion at a bottleneck router. The results also showed that FEC require more bandwidth and increased end-to-end delay due to redundant packets. So in the next chapter we will develop a enhancement for FEC that requires less bandwidth and delay.

In addition, the results showed when we have a single sender the RED can perform better than DT from a network perspective, since the RED required less bandwidth and delay with an increase in queue size, while DT performed better than RED from the quality perspective, since the DT had less packet loss and more throughputs with an increased queue size. With multi-sender the results do not show much difference between the DT and the RED queuing policy.

- http://www.icir.org/floyd/REDparameters.txt