# The introduction of delay

### Abstract:

This article discuss about the introduction of delay in source quenching messages in internet protocol. In this concept a delay "D" will be introduced to the datagrams which are been sent to the same destination host. various topics like source quench , the effect of source quench in datagrams and how the introduced delay can affect the transfer of datagrams are been explained .

### Introduction

A source quench message is sent to source host by the gateway when it does not have enough memory space to queue the datagram which it needed to route to destination host. A source quench message is a ICMP which request the host to slow down the speed at which it is transferring the traffic to the destination.

### Packet format - source quench message[1]

- Type must be set to 4.

- Code must be set to 0.

- The additional data is used by the sender to match the reply with the associated request.

The IP header plus the first 8 bytes of the original datagram's data is returned to the sender. This data is used by the host to match the message to the appropriate process. If a higher level protocol uses port numbers, they are considered to be in the first 64 data bits of the original datagram's data. This message is not generated in response to a datagram destined for a multicast address.

Even though the ICMP is a part of IP layer, the handling of the messages is processed by the Transport or application layer. The message is reported to these layers and they implement a mechanism to respond to the messages.

### The SQuID Concept

Consider the IP module at the datagram source is sending queue of datagrams with the attribute "D". D is the introduced Delay time between sending datagrams from the queue to the network. i.e the time it waits to send another datagram after it sends one datagram. The default value is set to zero .the value of D will be increased when a source quench is received and the value decreases when the time goes out .

### How it is implemented?

The IP would maintain a list of D values for destination host in its cache and it won't keep the destinations which has the default value.

Suppose the IP wants to send a datagram, it would search the cache if the destination is noted , If it is not, then it assumes D value is zero, and it sends the datagram at once.If the destination is listed, the IP must wait D time indicated before sending that particular datagram. It could look at a datagram addressed to a different destination, and possibly send it in the mean time.

When the IP receives a source quench, it checks to see if the destination in the datagram that caused the source quench is on the list. If so, it adds K to the D value. If not, it appends the destination to the list with the D value set to "I".

### The implementation has some practical problems,

- The IP can send one SQ for every N datagrams they discard so the SQ messages will not make the congestion problem much worse .this results in that any of the sources of the N datagrams may get the SQ not necessarily the one causing the most traffic. However if a host continues to send datagrams at a high rate it has a high probability of receiving a SQ message sooner or later.

- The IP or ICMP specification does not have a well defined event to indicate receipt of SQ to higher level protocols. Therefore many TCP implementations do not get notified about SQ events and thus do not react to SQ.

- TCP is not the only source of IP datagrams either. Other protocols should also respond to SQ events in some appropriate way. TCP and other protocols at that level should do something about a source quench. Also implementation of SQ processing at one level of protocol should not interfere with the behaviour of higher level protocols.

- Protocols using IP which are trying to transfer large amounts of data the data flow is most typically very bursty. Such protocol uses NETBLT which is a rate based protocol which has parameters for burst size and burst rate. The burst allows the source to send more number of datagram one at time and it increases efficient scheduling.

- The network must be kept busy for accepting data to maximize effective throughput in spite of a potentially large network round trip delay. To send a datagram then wait for an acknowledgment is a simple but not efficient protocol on a large wide area network.

- The efficiencies at the source node by generating many datagrams will not be same intermediate IP node. Since each datagram is potentially from a different node they must all be treated individually.

Datagrams received in a burst may also overload the queue of an intermediate node losing datagrams and causing SQs to be generated. If the limit of the queue is near the maximum level then all the datagram would be lost. Hence a datagram must be set with a greater delay at intermediate level than the source nodes

The above said problems can be rectified if the gateways can send SQs to us to tell us how we are doing. Because the loss of a single datagram affects data flow so much it would be much better for the source IP node if it got a warning before datagrams were discarded.

### Conclusion

The following things are concluded from the report,

- Inorder to get the best throughput the value of introduced delay must be accurate, though it is tedious to determine.

- The values of SQ Keep (SQK) and SQ Low Water (SQLW) queue level percentages should given a low value to reduce queue sizes and thus the through net delay. The limit of SQK and SQLW must be based upon the percentage of time, the queue is empty.

- Window closing algorithms reduce the average inter-datagram delay and the burst size but do not affect the minimum inter-datagram spacing by TCP.

To conclude, The SQuID algorithm fulfils the requirements and it could be installed in one location and implemented successfully.

### Bibliography

- ICMP_Source_Quench. (2008, july 30). Retrieved dec 20, 2009, from Wikipedia: http://en.wikipedia.org

- protocol/icmp. (n.d.). Retrieved jan 02, 2010, from networksorcery: http://www.networksorcery.com

- W.Postel, & Prue, J. (1987, july). /CIE/RFC/Orig/rfc1016.txt. Retrieved dec 27th, 2009, from freesoft website: http://www.freesoft.org