# The rapid growth

### Abstract

The rapid growth in digital communication techniques and the consecutive developments in the field of computer networks have made the world very smart but not smart enough against sneakers. The threat for the private communication posed by the loopholes in the computer networks has become a grave challenge to the designer of any secret communication system. After the popular defeat of many cryptographic algorithms by many brute-force and pre-computed dictionary attacks by unknown faces, the domain of steganography started providing a stealthy, yet, unsuspicious means of communication, along with its simplicity and reliability. In this paper as an optimistic effort a random walk embedding stego system has been proposed without stego-key. The proposed stego system scans the image, pixel by pixel along a complex path, not row by row, and hides the k bit of the data in each pixel visited in the order defined by a space-filling curve, such as the Hilbert curve, the Moore curve and magic numbers traversing path. Such curves visit each point of a square area in Hilbert curve or rectangle area using Moore curve exactly once. The effectiveness of the proposed stego system has been estimated by computing eight different metrics namely number of bit errors, bit error rate, Mean Square Error (MSE), Peak Signal to Noise Ratio (PSNR), universal image quality index , Mean Structural Similarity Index (MSSIM), relative entropy and time taken, and also illustrates how security has been enhanced using this algorithm.

Index Terms - Hilbert space filling curve, Information Hiding, Magic numbers, Moore curve, Steganography.

### 1. Introduction

Internet is an embarrassing open book which reveals how the world is on its way to become a "global village" in which everybody wants to know everything about everyone. This www. medium of communication invigorates everyone to exploit it for effective, efficient and cost effective information sharing. But at the same time, it has beckoned the spoilers to foul play a lot to destroy or steal the original or secluded information. This results in lack of information security which could sabotage the website and hence makes the internet more corruptive.

The insecure trend of information sharing has conflagrated many scientists and technologists to develop different encoding and information hiding techniques (Bender et al., 1996; Katzenbeisser and Petitcolas, 2000; Petitcolas et al., 1999) [ 1, 9, 14]. But, hackers are equivalent to or sometimes better than the constructive technologists in creating hacking tools. Hence secret information sharing through encoding techniques has become a cake walk for the eaves droppers. In order to balance any such critical or criminal attacks on original codes, an innovative and hard to hack tool namely steganography has emerged as stalwart method against any type of interlopers.

Steganography (Bender et al., 1996) [1] makes use of innocent looking digital media as cover to indiscernibly carry secret information to an intended recipient, but it is definitely different from cryptography. Cryptography (Bruice Schneier., 2007) [2] usually scrambles the information into an unintelligent form whereas steganography tries to hide the data in the cover object. In steganography the information bearing cover object is called stego cover. The stego cover can be many kinds of digital media such as text, image, audio, and video. In the present work an image has been selected as cover object because of the widespread use in internet and capability of storing large amount of data and significantly digital images (Morkel et al., 2005) [12] are considered good cover carriers because of their insensitivity to the human visual system.

There have been many embedding schemes namely LSB embedding (Chan and Cheng., 2004) [4], pixel value differencing (Wang., 2008; Young-Ran Park., 2005)[5, 20], transform domain technique (Johnson and Jajodia., 1998) [8], spread spectrum technique (Marvel et al., 1999) [11], statistics of the cover (Niels Provos and Peter Honeyman., 2003) [13], reversible embedding scheme(Kieu and Chang., 2009; Wang et al., 2009; Wu et al., 2009) [10, 17, 19], etc., proposed in the existing steganographic methods of secret communication. In these schemes, majority of the time, authors have adopted raster scan (Bender et al., 1996; Chan and Cheng., 2004; Young-Ran Park., 2005) [1, 4, 20] for data embedding and extracting processes. From the literature (PhilSallee., 2003) [15] it is obvious that, if random scan is employed instead of raster scan in secret data embedding, the effectiveness can be improved significantly.

In the current process of information hiding an interesting and novel data embedding scheme has been proposed and implemented successfully. Instead of adapting the usual raster scan for data embedding and extracting from the pixels of an image, embedding based on Hilbert, Moore (Hans Sagan., 1994; Westfeld., 2005)[7, 18] space filling curves and magic numbers traversing path has been identified as an innovative and effective technique. The flow of space filling curve will provide the embedding path for stego process which will definitely be a nightmare for hackers. The level of confidentiality of this proposed scheme has also been tested with eight different metrics which follows in the next section.

### 2. Implementation of Random Steganography

The limitations of least significant bit embedding, based on random selection of pixels of the cover image can easily be overcome by the present innovative scheme. In general, random embedding scheme require a specific key with variable size to retrieve the embedded secret data at the receiving end. In order to overcome this drawback, the concept of space filling curve (SFC) has been adapted for embedding the secret data in image where Hilbert and Moore SFC method can be used. Furthermore a random walk defined by the magic numbers has also been considered for k-bit embedding.

SFC is a one dimensional curve which traverses through each and every point within a two dimensional space or image. SFC scans a pixel array which has a size of M x N pixels and while scanning, it will not retain the same direction but will turn around to embrace all the pixels at least and at most once. Hence the unpredictable traversing path of SFC through the image has been chosen to hide the secret message in the cover. In this scheme, both the transmitter and receiver can adapt a particular SFC so that there is no need to communicate the key. In the similar line a common magic number generator available with two ends will provide a complicated traversing path for k-bit embedding which does not require any key.

Before considering the entire cover image for secret bit embedding, block of 8 x 8 pixels has been taken to implement Hilbert SFC, Moore SFC and Magic number traversing path based stego technique by adapting a common traversing path for both the sender and receiver. After performing this process for a single 8 x 8 block, it has been extended to the full image by considering it as multiple of 8x8 blocks to cover up the entire 28X28 pixels.

### 3. Experimental Results

Ten digital images which have been selected for implementing the Hilbert SFC, Moore SFC and Magic number traversing path based stego method are shown in Figures 4a, 4b, 4c, 4d, 4e, 4f, 4g, 4h, 4i and 4k. Each cover image has been divided into multiple blocks of 8x8 pixels. The encrypted secret data has been hidden in each pixel of 8x8 block by adapting k-bit LSB technique and in the same way the secret message has been embedded in all the 8 x 8 block pixels of the cover image. In the current implementation, k=1, 2, 3 and 4 bits LSB embedding [6] have been accomplished to obtain the final stego cover. Figures 5a, 5b, 5c, 5d, 5e, 5f, 5g, 5h, 5i and 5j show the stego covers for the k=4 bit embedding. Eight different metrics have been used to evaluate the quality of the stego covers. The computed metric values for ten images employing Hilbert SFC, Moore SFC and magic number traversing path are given in Table I, II and III respectively.

From this implementation, it is observed that the number of bit error value increases with increase in the number of k-bit embedding for the entire three random traversing path. In order to evaluate the disorderliness of the stego cover, relative entropy has also been computed. For k=3, 2, 1 bit embedding, relative entropy is found to be approaching zero which suggests that the proposed stego technique will be efficient and effective up to k=3 bits. Since relative entropy has considerably increased for k= 4 bit, it is not advisable to use the same for the current stego process.

From the estimated values of MSE one can note that it increases with increase in the number of k-bit embedding and this trend is the result of significant depth of distortion on each pixel due to increasing number of bit embedding. Same type of variations has been observed for all the ten stego covers.

Computed values of PSNR prove that, it is better for lower k bit embedding than the higher k bit case. It is a known fact that the PSNR value should be greater than 30 dB for a better stego cover and the present calculated result substantiates the same. In the present case, it is significant that even for the k=4 bit case this value is around 33 dB which confirms the effectiveness of the proposed random traversing path based stego technique.

In addition to the PSNR pixel quality estimation, the authors have estimated two types of image quality index based on statistics measures namely universal image quality index [21] and MSSIM. But in the present implementation, the estimated universal quality index is always found to be closer to 1 for k=1 to 4 bit embedding. Hence the latter method has been adapted to evaluate the quality index for all the k-bit cases. From the computed values it has been observed that the MSSIM value decreases with increase in k-bit embedding which validates the deteriorating quality of stego cover. The estimated SNR values confirm the fact that k=1 and 2 bits embedding cases are much better than the k= 3 and 4 bit cases to be adapted.

All the estimating parameters of the ten stego covers have been performed using Intel Core2 Duo CPU processor @ 1.60 GHz, 1GB RAM. From the time taken by this processor for estimating all parameters for k bit embedding, it is obvious that k=1 bit case takes much lesser time than the other cases.

### 4. Conclusion

The present stego system employs several security techniques to protect the clandestine information from being abused. As an initial protection, prior to embedding, the secret information has been scrambled through DES. During the embedding process, the cover image is divided into several blocks in which user has many options to select the size of the basic block. As 30 dB is fixed as the threshold PSNR value for human visual system, the present results possess excellent imperceptibility without noticeable degradation and the same is well supported by the estimated PSNR value for all the ten stego covers. Since the scrambled message has been hidden imperceptibly in the cover image through k-bit embedding in a specific random traversing scheme, the effectiveness of stego process has increased appreciably and toughness to crack the secrecy against any serious threat is also improved significantly. In general, all the estimated parameters show the same trend for all the ten images towards Hilbert SFC, Moore SFC and magic number traversing path based embedding cases.

### References

- Bender, W., Gruhl, D., Morimoto, N., Lu, A., 1996. Techniques for data hiding. IBM Systems Journal 35 (3-4), 313-336.

- Bruice Schneier., 2007 Applied Cryptography Protocols, Algorithm and Source Code in C. Second ed., Wiley India ed.

- Cachin C., 1998. An information theoretic model for steganography, in Proceedings of the international workshop on information hiding Springer LNCS 1525, 306-318

- Chan, C.K., Cheng, L.M., 2004. Hiding data in images by simple LSB substitution. Pattern Recognition 37, 469-474.

- Chung-Ming Wang., Nan-I Wu., Chwei-Shyong Tsai., Min-Shiang Hwang., 2008 A high quality steganographic method with pixel-value differencing and modulus function The Journal of Systems and Software 81, 150-158

- Cosman, P.C.Gray, R.M.Olshen, R.A., 1994. Evaluating quality of compressed medical images: SNR, subjectiverating, and diagnostic accuracy Proc. of the IEEE Vol 82(6) 919-932

- Hans Sagan., 1994. Space-Filling Curves, Springer-Verlag, New York, ISBN: 0-387-94265-3.

- Johnson NF., Jajodia S., 1998. Steganalysis of images created using currentsteganography software David Aucsmith(Ed) Information Hiding LNCS 1525, 273-289

- Katzenbeisser, S., Petitcolas, F.A.P., 2000. Information Hiding Techniques for Steganography and Digital Watermarking. Artech House Inc.

- Kieu, T.D., Chang, C.-C. A high stego-image quality steganographic scheme with reversibility and high payload using multiple embedding strategy. J. Syst. Software (2009), doi:10.1016/j.jss.2009.05.028

- Marvel, L.M., Boncelet Jr., Retter, C.T., 1999. Spread spectrum image steganography, IEEE Trans. Image Process. 8 (8) 1075-1083.

- Morkel, T., Eloff, JHP., Olivier, MS., 2005, "An Overview of Image Steganography," in HS Venter, JHP Eloff, L Labuschagne and MM Eloff (eds),Proc. of ISSA

- Niels Provos., Peter Honeyman., 2003. Hide and Seek: An Introduction to Steganography, IEEE Security and Privacy, 1(3) 32-44.

- Petitcolas, F.A.P., Anderson, R.J., Kuhn, M.G., 1999. Information hiding-a survey. Proceedings of IEEE 87 (7), 1062-1078.

- PhilSallee., 2003. Model-Based Steganography T.Kalker et al( Eds): IWDW LNCS 2939 154-167

- Proakis John G., Digital Communications, 4th ed., New York, McGraw-Hill, 2001.

- Wang, Z.-H., et al. A reversible information hiding scheme using left-right and up-down chinese character representation. J. Syst. Software (2009), doi:10.1016/j.jss.2009.04.045

- Westfeld A., 2005. Space filling curves in steganalysis in E.J Delp III & P.W. Wong(Eds), Security, steganography and watermarking of multimedia contents VII SPIE 5681, 28-37

- Wu, H-C., Lee, C-C., Tsai, C-S., Chu, Y-P., Chen, H-R., A High Capacity Reversible Data Hiding Scheme with Edge Prediction and Difference Expansion, The Journal of Systems and Software (2009), doi: 10.1016/j.jss.2009.06.056

- Young-Ran Park., Hyun-Ho Kang., Sang-Uk Shin., and Ki-Ryong Kwon., 2005 An Image Steganography Using Pixel Characteristics Y. Hao et al. (Eds.): CIS 2005, Part II, Springer-Verlag Berlin Heidelberg LNAI 3802, 581- 588.

- Zhou Wang, Alan Conrad Bovik., 2002. A universal image quality index, IEEE Signal Processing Letters 9, 81-84.

- Zhou Wang, Alan Conrad Bovik, Hamid Rahim Sheikh, Eero P. Simoncelli., 2004 Image Quality Assessment: From Error Visibility to Structural Similarity, IEEE Transactions on Image Processing, 13(4) 600-612.