# The scalable video coding standard

### I. INTRODUCTION

Advancements in the infrastructures of networks, storage capacity and data processing power, gave the opportunity to multimedia for blooming. Apart from this, the big steps of technology in the field of motion picture and the fast spread of handheld devices, such as smart phones, PDAs and portable video players, forced the Telecommunication Standardization Sector (ITU-T) of the International Telecommunication Union (ITU) in cooperation with the Joint Technical Committee of the International Organization for Standardization (JTC1/ISO) and the International Electrotechnical Commission (IEC) to create a new extension of the H.264/ Advanced Video Coding (AVC) standard [1]. The new extension of the AVC protocol was needed to provide greater scalability in terms of frame size and video quality. For applications with video signal of a fixed spatial and temporal format, traditional systems of digital transmission are used. These systems are based on H.222 if the applications include terrestrial, cable or satellite TV; while video conference services are based on H.320 protocol of the MPEG-2 [2]. According to [1] and [2], for video conference; the above format is CIF, while for broadcasting (TV) is SDTV or HDTV [5]. Modern applications that involve the Internet; such as multimedia playback in networks (streaming live or stored video and real-time interaction), are most of times based on Real-time Transport Protocol (RTP)/ Internet Protocol (IP) [1], [2]. The key element of an RTP/IP is that provides a dynamic range of quality variations, according to the current available throughput and the capabilities of the end user's device. Due to the generalization of the subject of this paper, the reader is expected to have an experience in digital video encoding (interfaces & processing). The books of [2] and [5] can provide such information to the reader.

### II. SVC TECHNICAL ANALYSIS

According to [1] and [3], MPEG-4 / SVC extension supports spatial, temporal and quality scalability. "Scalability" as a term refers to a framework, where from a united encoded video stream can result to a representation of the video in different quality, resolution and temporal frame rate. Furthermore a scalable digital video enables the removal of some parts of the original bit stream in a way that the sub stream that results, forms a valid stream - for the decoder- similar to the former (regarding the length) but with reduced quality and adaptive resolution and frame rate. The above types of video scalability can be combined for a final representation with spatio-temporal changes. The importance of scalability can be understood with an example. A video encoded once, with the maximum of bit rate and resolution can be delivered as a single scalable stream of data, to clients with different resources. This means that a user with a cellular phone can obtain the same video with another user of a high-end PC. Each user decodes only some part of the SVC encoded video. Consequently, this method can be very useful to restricted throughput scenarios while passively avoids network congestion and improves error robustness of the video delivery; which means that packet loss or drop are unlikely to happen. In the chapters below, a brief description of the AVC standard and the three types of scalability takes place.

### A. H264/AVC key elements

It is important for the reader to be informed at some basic elements of the H.264/AVC standard in order to deeply understand the SVC protocol. Advanced Video Coding protocol includes the NAL (Network Abstraction Layer) and VCL (Video Coding Layer). VCL is in a way the encoder of the source and NAL the modulator. This means that the data are coded from the VCL and given to NAL to appropriate format the data and provide them a header in order to be rate-distortion improved and error-resilient for the transport layer or the storage medium. The coded data of the digital video are organized in NAL units (packets counted in a number of bytes) and then are classified in VCL NAL and non-VCL NAL units. The former contains the encoded data of the video, in other words the information; while the latter includes additional information such as the header data and enhancement information such as timing information and other features for enhanced usability of the VCL NAL units [4]. Schwarz and Wien [3], refer to one decoded picture as an access unit of a set of NAL units and a coded video sequence as a set of successive units with a number of properties. This video sequence represents part of a stream of bits that can independently be decoded. Note that due to the fact that SVC is an extension of H.264/AVC, it includes all the elements of AVC (fig. 1). This means that the former uses tools of the latter, tools such as transform coding, entropy coding, intra prediction, deblocking filter and the NAL unit technique for packet creation described above [1], [4].

### B. SPATIAL SCALABILITY

The frames of the n spatial layers are encoded with the use of motion compensation and intra prediction parameters. A switching method of interlayer prediction of intra, motion and residual; is used to enhance the efficiency of the layer coding [1], [7]. With the Scalable Video Coding, each of the n layers can be decoded from a single loop of motion compensation prediction and deblocking. This means that the encoder of Figure 1 somehow manages these operations through a loop, and automatically understands and maps the target layer to the output pictures/frames. As in the older versions MPEG-4 Visual and MPEG-2, SVC extension has spatial scalability with random resolution ratios, which means that the original image (frame) can be reconstructed to arbitrary ratios depending on its enhancement layer and reference layer. In order to have spatial scalability of resolution, the video should initially be down sampled to the resolutions required; depending on the application service. According to [6], the scalable resolution ratio between the frame's width and height is not needed to be a factor of two (2). In addition to the needless dyadic resolution, the configurations of 1080x720p are achieved very easily. Encoding and decoding of the resolution-scaled frames start from the base layer Advanced Video compatible encoder (Figure 1), beginning from the lower and heading to the higher "desired" resolution. As the encoder "moves" from the lowest to the highest resolution, three (3) key components are used for the up sampling. These components involve the inter-layer prediction (described above) and are [6]:

1. Up sampled intra-coded macro blocks.

2. Motion and mode information (stretched or aligned, depending on the frame size ratios)

3. Up sampled symmetric signal for inter-coded macro blocks.

Note that the lower layer prediction from the base - layer AVC encoder is not essentially been used because each one of the spatial layers have the ability to identically and independently be encoded. An illustration of spatial scalable coding with prediction fixation for two (2) resolutions can be seen in Figure 2 and for a multilayer structure with the same characteristics in Figure 3. Before continuing to the Temporal Scalability the three (3) prediction modes of the spatial scalable encoder are being presented, in order for the reader to have a complete aspect of the Spatial Scalability enhancement of SVC.

### i) Inter-Layer Motion Prediction

According to [1] and [7], for the prediction of Inter-Layer motion in spatial enhancement, a new macroblock is introduced; the reference layer skip mode. This mode is needed to specify that the predicted data are outcome from the reference layer and that only the enhanced part of the remaining signal is encoded. The macroblock partitioning according to [7] is "determined by up-sampling and realigns the partitioning of the reference layer region that aliases the same frame as the macroblock to be coded". This happens when the outcome prediction mode, specifies inter-frame coding. The example of a factor of two (2) spatial scalability, given in [7] makes things clearer: Each macroblock of refinement layer corresponds to a submacroblock of 8x8 in the reference layer and the partitioning of the enhancement layer macroblock derives by scaling the 8x8 block of the dyadic base layer; vertically and horizontally. Finally SVC has the ability to switch between the usual motion predictor and the inter-layer predictor, while signaling the choice with a flag (cursor), transmitted on a macroblock partition.

### ii) Inter-Layer Residual Prediction

When this type of prediction is used, a flag (cursor) is been transmitted on a macroblock and if true, the appropriate remaining signal of the reference layer is initially been up-sampled and then used as a signal point that only the corresponding difference signal is encoded. This up-sampling is performed at a transform block basis, in order to avoid distortion from the filtering of the transform block ends [7].

### iii) Inter-Layer Intra Prediction

This prediction mode is the only that was already been supported in the previous H.262/MPEG-2, H.263 and MPEG-4 Visual standards. The mode operation begins with the macroblock encoding, using the layer skip mode (described in i). The outcome prediction mode specifies intra-frame coding. The prediction signal in this mode, occurs from up-sampling of the reconstructed intra signal of the reference layer [1]. Furthermore it must be highlighted that according to [7], the complexity of the spatial scalable encoder is significantly smaller in SVC than the ones used for single-layer H.262, H.263 and MPEG-4 Visual.

### REFERENCES:

[1] Overview of the Scalable Video Coding Extension of the H.264/AVC Standard

[2] Fundamentals of Multimedia

[3] Standards in a nutshell

[4] ADVANCED VIDEO CODING FOR GENERIC AUDIOVISUAL SERVICES

[5] Video Demystified book

[6] Video subgroup - overview of Scalable Video Coding Jens-Rainer Ohm

[7] Performance analysis of the SVC