# The wireless communication

### I. INTRODUCTION

Today wireless communication is very popular among the mobile users than ever before. This is due to the growth in the number of laptops and wireless data communication devices, such as wireless LANs and wireless modems. There are two different approaches used for wireless communication between two nodes.

The first approach is to let the existing cellular network infrastructure carry data as well as voice. In cellular networks, communications between two mobile nodes completely rely on the wired backbone and the fixed base stations.

The second approach is to form an ad-hoc network among all users wanting to communicate with each other. It is also called MANETs (Mobile Ad-hoc Networks) [3], [4]. MANETs is a network with mobile nodes without pre-configured infrastructure for transferring data packet between two nodes. In MANETs nodes can move free in any direction and organize themselves arbitrarily. That's why the network topology changes rapidly and an unpredictable manner.

MANETs are formed with a set of wireless nodes without any existing infrastructure or centralized administrative support. In MANETs, medium of the communication is broadcast. Nodes have limited resources such as short-term power supply, memory, communication range, low processing and limited bandwidth. Due to the limited transmission range of the nodes, multiple hope counts may be needed for a node to send data to any other node in the network. Every node wishing to participate in MANETs must be willing to forward packets for other nodes. Thus each node in MANETs acts as a host and router and takes part in discovery and maintenance of routes to other nodes in the network. The advantages of such a network are rapid deployment, robustness, flexibility and inherent support for mobility.

MANETs are also capable of handling topology changes and malfunctions in nodes. Due to their quick and economically less demanding deployment, Applications of such networks are vehicle-to-vehicle communication ,military deployment [17],wireless sensor network, wireless mess network, distributed computing, conferences, emergency operations, exhibitions, virtual classrooms and operations in environments where construction of infrastructure is difficult or expensive [18]. [dsdv,dsr,olsr]

A representative routing protocol is chosen from each category of MANETs routing protocols namely Destination-Sequenced Distance-Vector (DSDV) protocol [8], [9], Ad hoc On Demand Distance Vector (AODV) protocol[10], [11], [15], and Temporally-Ordered Routing Algorithm (TORA) [12], [13].

The aim of the thesis is to evaluate the proposed MANETs routing protocols based on performance by using different scenarios in terms of throughput, end to end delay, packet delivery ratio and convergence time to uncover in which situations these types of MANETs routing protocols have their strengths and weaknesses.

The evaluation of these MANETs routing protocols is based on the following research questions:

- Which routing protocol provides a better performance in MANETs?

- What factors influence the performance of these routing protocols?

- Address the major differences in the routing protocols under study.

The evaluation of MANETs routing protocols will be done by theoretical and simulation [1], [2]. The simulation environment will be based on Network Simulator 2 (NS 2) from Berkeley [2].

The achievements after completing the master thesis should be; general understanding of ad -hoc networks, generate a simulation environment for different performance metrics, implement and analyze the MANETs routing protocols theoretically and through simulation and recommend the routing protocols for specific network scenarios.

### A. Method

### II. CLASSIFICATION OF ROUTING PROTOCOLS FOR MANETs

In MANETS nodes are free to move in any direction. When a node wants to communicate with another that is outside its transmission range, an intermediate node acts as a router to forward packets from source to destination. Due to this node mobility, changes in network topology occur frequently. So we need a routing protocol that can easily adapt changes in network topology.

Internet Engineering Task Force (IETF) [4] has a mobile ad hoc networking (MANET) working group to develop IP-based protocols in ad hoc networks. A number of routing protocols have been proposed for MANETs, which are derived from either distance-vector [5] or link state [6] based classical routing algorithms. Routing protocols for MANETs can be classified [7] into three main categories: Proactive or table-driven Routing Protocols, Reactive or on-demand Routing Protocols and Hybrid Routing Protocols.

### A. Proactive Routing Protocols

Proactive routing protocols, also called table-driven protocols, attempt to maintain routing table of the entire network topology. They exchange routing information to maintain routes from each node to every other node in the ad hoc network, including nodes to which no packets are sent. They react to topology changes by propagating updates throughout the network in order to maintain a consistent network topology. In proactive routing protocols, a node must periodically send control messages to maintain correct routing information even though the node may not be transmitting any kind of data traffic to each other. This large amount of data control messages may cause wastage of network bandwidth. The main advantage of proactive routing protocols is that nodes can quickly get routing information and start a session. Example includes the Destination-Sequenced Distance Vector (DSDV) protocol [-].

### B. Reactive Routing Protocols

Reactive protocols, also called on-demand protocols, create the routes to the destination on demand. When a source node needs to transmit data to a destination node, it invokes the route discovery mechanisms to find the path to the destination. Once a route to the destination is searched or all possible routes toward the destination node have been examined, the routing process is completed. Once a connection is established, source and destination nodes can transmit and receive data. The connection is maintained until either the destination node becomes inaccessible from the source or until the route is no longer desired. They discover the routes by flooding a route request packets through all over the network. Reactive routing protocols do not need to search for and maintain routes on which there is no data traffic, so that they reduce the routing overhead, save memory, network bandwidth and battery power. This feature is very useful where there are limited resources. On-Demand routing protocols can be classified into two categories: source routing and hop-by-hop routing.

In source routing, each packet's header has the complete path information from source to destination. Therefore, each intermediate node forwards these packets according to the information in the header of each packet. Source routing does not perform well in large networks. Due to the following reason. In large network the number of intermediate nodes in each route grows. Due to this reason probability of route failure is high and the amount of overhead carried in each header of each data packet will grow.

In hop-by-hop routing each data packet only carries the destination address and the next hop address. Therefore, each intermediate node in the route to the destination uses its routing information to forward each data packet towards the destination. The advantage of this strategy is that each node can update its routing table when they get new information about network topology and hence forward the data packets over better routes. The disadvantage of this strategy is that each intermediate node must have to store and maintain routing information for each active route and each node use beaconing messages to aware from the neighbors in the network topology. Example includes the Ad hoc On Demand Distance Vector (AODV) protocol [ -].

### C. Hybrid Routing Protocols:

These routing protocols have the best properties of both proactive and reactive and routing protocol. They are used to obtain a better balance between the adaptability to varying network conditions and the routing overhead. These protocols use different kind of routing strategies in different regions or times in the same network topology. These protocols may benefit for cluster network of nodes within the same network and applying different routing mechanism within and outside the cluster network. These protocols can adapt the frequency and size of the routing updates according to the network condition.

### III. OVERVIEW OF DSDV, AODV & TORA

### A. Destination Sequenced Distance-Vector (DSDV) Protocol:

DSDV [8], [9] is a proactive or table driven, distance vector protocol routing protocol proposed for mobile ad hoc networks. It is based on the idea of the classical Bellman-Ford Routing Algorithm with certain basic improvements made include freedom from loops in routing tables, more dynamic and less convergence time. Each node in the MANET maintains a routing table that contains a list of all available destination nodes within the network along with hop counts, their metric; next hop address and a sequence number assigned by the destination node. Routing table of each node contains the shortest distance and the first node on the shortest path to every other node in the network. The sequence numbers are used to distinguish new routes from old routes to avoid the formation of loops and to counter the count-to-infinity problem. To maintain consistency in routing table information, the routing table updates are broadcast between neighbors at regular interval or when there is a significant change occure in the network topology.

This exchange of routing updates creates overhead in the network. To overcome this problem, routing updates can be sent via two methods: a "full dump" or an "incremental update". In "full dump" the entire routing table is sent to directly connected neighbors and provides quick convergence when the network is first boot up. Whereas "incremental updates" carrying only information about changes from the full dump. These updates are stored in the Network Protocol Data Unit (NPDU), and thus decreasing the amount of traffic significantly. Incremental updates can be big in the frequent changes network, so the use of full dump updates will be more frequent. Updates are tagged by the sequence numbers. Nodes update their routing table by using the most recent sequence number of the updates. If two updates have the same sequence number then hop count factor is used for routing decision. The following are the limitation of the DSDV:

- To maintain routing table for large network is difficult. This would lead to network overhead and consumes more bandwidth of the network.

- To determine a time delay for the advertisement of routes is difficult [9].

- Multipath routing is not supported by DSDV.

- bandwidth wastage due to the unnecessary routing advertisement even if there is no change occurs in the network [16].

### B. Ad hoc On Demand Distance Vector (AODV) protocol:

AODV [10], [11], [15] is a reactive ad hoc routing protocol based on distance vector. It request and establishes a route to a destination only on demand and requires hosts to maintain only active routes. Those nodes that are not belonging to active routing path towards the destination node do not need to maintain routing information to the destination in the routing table. Thus AODV minimize the number of control messages sent between the nodes. It enables multi-hop routing between each communication nodes wants to establish and maintain an ad-hoc network.

Each entry records the next hop to that destination and a sequence number generated by the destination which indicates the freshness of the routing information. In addition, each entry also records the addresses of active neighbors through which packets for the given destination are received. Routes, which are not in use for long time, are deleted from the table. Therefore, once the corresponding link of this entry is down, the upstream hosts using this link can be notified immediately. AODV reduce the need for system wide broadcasts as much as possible by using a "monotonically increasing number" for the destination sequence number. This number prevents old routing information being used, which the essential is caused for the routing loop problem in the traditional distance vector algorithm. The result of which is that AODV is a loop-free, highly situational responsive and bandwidth efficient routing protocol. AODV has capability of both unicast and multicast routing and avoid Bellman Ford "count to infinity" [19] problem.

The main advantage of AODV is that routes are obtained on demand and destination sequence numbers are used to find the latest route to the destination.

The disadvantages of AODV are that multiple Route Reply (RREP) packets in response to a single Route Request (RREQ) packet can cause overhead; continues hello message leads to unnecessary bandwidth consumption; if the source sequence number is very old and the intermediate nodes have a higher but not the latest destination sequence number then intermediate nodes lead to inconsistent routes; it requires symmetric link to fulfill the needs of bidirectional transmission; whenever the routing is invalid ,a routing request procedure is required immediately; if a routing is out of time the route is deleted from the routing table even if it is a valid route .

AODV uses different kind of messages to discover and maintain routes. AODV builds routes using a ROUTE REQUEST / ROUTE REPLY queries. When a source node desires a route towards destination for which it does not have a route or route has expired, it broadcasts a ROUTE REQUEST (RREQ) packet across the network, including the last known sequence number for that destination. Each node receive the ROUTE REQUEST (RREQ) update their information for the source node and creates a reverse route for itself back to source node in the routing table. The RREQ contains the source node's IP address, current sequence number, broadcast ID, and the most recent sequence number for the destination of which the source node is aware.

When the ROUTE REQUEST (RREQ) reaches a node with a route to Destination, that node generates a ROUTE REPLY (RREP) that contains the number of hops necessary to reach Destination and the recent sequence number for Destination. Each node that participates in unicast REPLY back toward the source node creates a forward route towards Destination. After establishing the route, source begins to forward data to the destination. In the future, if source receive a sequence number with a smaller hop count towards the destination, it store and use the better route. As long as the data packets travel the source to the destination, the route is consider active. When source stops sending data, the link is deleted from the routing table of intermediate node. If a link break occurs while the route is active, the node prorogate a ROUTE ERROR (RERR) message to the source node to inform the source node that the route to destination is unreachable.

### C. Temporally-Ordered Routing Algorithm (TORA):

TORA [12], [13]is a highly adaptive distributed routing algorithm based on the concept of "link reversal". It is a source initiated protocol .It quickly discover and establish multiple routes to any source/ destination pair only when desired using a query-reply process with less routing overhead. It ensures all routes are loop free. Control messages are localized to a very small set of nodes and minimize reaction to topological changes. Each node needs information about its neighboring node only. Three basic functions of TORA are route discovery, route maintenance and route deletion.

When a source wants to establish a route to destination, it broadcast a QRY message containing the destination address to its neighbor. The search is accomplished via flooding QRY message throughout the network. The destination node or intermediate node which has a route to destination, will reply with an UPD message listing its height with respect to destination. The significance of the heights is that during routing process, a node may send routing information to a lower node. The node which receives a UPD packet sets its height to a value one greater than the height of the neighbor from which the UPD was received. By doing this, a set of sequential directed links has created from the sender of the QRY messages to the node that first broadcast the UPD message.

When a node discovers that a route towards destination is no more valid, it reset the value of height so that it is a local maximum with respect to its neighbors and transmits an update packet. Route maintenance is performed only for those nodes that have a non null height and these nodes are not used for computation. When a node lost its last downstream connection, it initiates link failure. The numbers of nodes that are participating in the failure of the network reaction are less. No reaction is initiated to link activation .When a node detects a network partition, it generates a CLR message that resets routing state and removes invalid routes from the network.

The effect of route erasure at a node is to set its height to null.

TORA is layered on top of IMEP (Internet MANET Encapsulation Protocol) [14] that has three main functionalities:Control message encapsulation, to reduce overhead, IMEP attempts to aggregate many TORA and IMEP control messages together into a single packet before transmission; provide reliable, in-order delivery of all routing control messages from a node to each of its neighbors; and neighboring links connectivity management. For link-status sensing and maintaining a list of neighbor nodes, each IMEP node periodically transmits a BEACON message, which is answered by each node hearing it with a HELLO messages.

### IV. Experimental Design

This section will be about the experimental design of the final project, in these section requirements for experiment, topological design and simulation scenarios will be discussed.

- Requirements for Experimental Design

- Experimental Topology

### V. Results and Analysis

- Throughput.

- End to end delay.

- Packet delivery ratio.

- Convergence time.

### VI. Conclusion and Future Work

### A. Conclusion

This section will contain conclusion of all the studies and experiments.

### B. Future Work

The future study and work about this final thesis will be described here.

### VII. Acknowledgment

This will be acknowledgment note for the teacher and friends who help to accomplish the project.

### VIII. References

- Marc Greis. "Tutorial for the Network Simulator ns". http://www.isi.edu/nsnam/ns/index.html (as of January 14, 2008)

- The NS Manual (Oct. 2, 2006), http://www.isi.edu/nsnam/ns.

- M. Frodigh, P. Johansson, and P. Larsson. "Wireless ad hoc networking: the art of networking without a network," Ericsson Review, No.4, 2000, pp. 248-263.

- IETF Working Group: Mobile Adhoc Networks (manet). http://www.ietf.org/html.charters/manet-charter.html.

- G.S. Malkin and M.E. Steenstrup, Distance-vector routing, in: Routing in Communications Networks, ed. M.E. Steenstrup (Prentice Hall, 1995) chapter 3, pp. 83-98.

- J. Moy, Link-state routing, in: Routing in Communications Networks, ed. M.E. Steenstrup (Prentice Hall, 1995) chapter 5, pp. 135-157.

- Dimitri Bertsekas and Robert Gallager, "Data Networks - 2nd ed". Prentice Hall, New Jersey, ISBN 0-13-200916-1. (classification of adhoc)

- C.E. Perkins and P. Bhagwat, Highly dynamic destination sequenced distance vector routing (DSDV) for mobile computers, in: Proc. Of ACM SIGCOMM'94, London, UK (August-September 1994) pp. 234-244.

- Guoyou He. "Destination-sequenced distance vector (DSDV) protocol". Technical report, Helsinki University of Technology, Finland.

- C. Perkins, "Ad hoc On-Demand Distance Vector (AODV) Routing ", RFC-3561, July 2003.

- C. E. Perkins and E. M. Royer, "Ad Hoc On-Demand Distance Vector Routing," Proceedings of IEEE Workshop on Mobile Computing Systems and Applications 1999, February 1999, pp. 90-100.

- V. Park and M. S. Corson, "A Highly Adaptive Distributed Routing Algorithm for Mobile Wireless Networks", Proc. IEEE INFOCOM '97, Kobe, Japan (1997).

- Vincent D. Park and M. Scott Corson. Temporally-Ordered Routing Algorithm (TORA) version 1: Functional specification. Internet-Draft, draft-ietf-manet-tora-spec-00.txt, November 1997.

- M. Scott Corson and Vincent D. Park. "An Internet MANET Encapsulation Protocol (IMEP) Specification". Internet-Draft, draft-ietf-manetimep-spec-00.txt, November 1997. Work in progress.(IMEP)

- I. Broustis, G. Jakllari, T. Repantis, and M. Molle. "A Performance Comparison of Routing Protocols for Large-Scale Wireless Mobile Ad Hoc Networks". Technical Report, University of California, Riverside.

- Danny D. Patel. "Energy in ad-hoc networking for the pico radio". University of California Technical report.

- A. Vahdat, D. Becker. "Epidemic Routing for Partially-Connected Ad Hoc Networks". Technical Report, Duke University, 2000.

- H. Wu, R. Fujimoto, and G. Riley. "Analytical models for data dissemination in vehicle-to-vehicle networks," In IEEE, VTC 2004 Fall.

- Martha Steenstrup, "Routing in communication networks". New Jersey, Prentice Hall. ISBN 0-13-010752-2.