# VBLAST architecture

This chapter deals with aspects of the VBLAST architecture. Section 3.1 introduces the VBLAST architecture and its operation. The detection method, nulling, interference cancellation and optimal ordering are discussed in sections 3.2 and 3.3. The decoding algorithm is given in section 3.6, and an exact unreported complexity analysis of the decoding algorithm is done in section 3.7. This is one of the contributions of this thesis. Section 3.8 shows VBLAST decoding using the QR decomposition. The benefits of forward and backward sweeps are considered in section 3.9, including ordering for optimal detection in section 3.10. Calculation of complexity is given in section 3.11. The chapter ends with some simulation results showing the performance of the original VBLAST and QR methods.

### 3.1 Introduction

To achieve the high capacities promised by using a MIMO scheme, Foschini et al [11] proposed an architecture known as Bell Labs Space Time, BLAST for short. The original BLAST system used a diagonally dispersed coding structure, the implementation of which was technically involved. Instead, a modified version known as Vertical Bell Labs Space Time, or VBLAST for short was proposed and prototyped in the laboratory [12]. A simplified block diagram of the VBLAST system is depicted in Fig. 3.1. A single data stream is demultiplexed into t substreams, and each substream is then encoded into constellation symbols and fed to its respective transmitter. Each transmitter is an ordinary QAM transmitter, and the symbols are taken from a QAM constellation. The encoding process is simply a bit to symbol mapping for each substream, and all substreams are mapped independently. The total transmit power is equally divided

among the t transmitters. The r receivers are conventional QAM receivers operating independently in the same frequency band. Each receiver receives signals from all the transmitters. The channel matrix H is assumed quasistationary, meaning it remains constant during the transmission of a whole data block. For this reason, decoding a whole stream is decoding each symbol of that stream. The next section discusses the detection of the individual symbols.

### 3.2 Detection Process

The detection process of the VBLAST system involves is the estimation of x given y and H in

The t elements of the transmit vector x are constellation symbols which are assumed to be uncorrelated. We also assume that the channel matrix H is full rank. It is shown later that the second assumption is very crucial to the operation of the VBLAST system. The receiver knows the received vector y and has an estimation of H. The detection process is then a multiuser detection type process. The process involves two steps [13]:  Slicing (and then decoding) a symbol while nulling the others  Cancelling the effect of each new decoded symbol from the rest

### 3.2.1 Nulling

Denoting the ith column of H as hi the received vector can be written as here xi is the transmitted symbol from the ith transmit antenna. Nulling is performed by linearly weighting the received symbols to satisfy the zero forcing (ZF) or minimum mean squared error (MMSE) performance criterion. The zero forcing nulling vector wi is chosen such that where ()T indicates transpose. Then, the decision statistic for the ith symbol is A soft or hard decision now can be made on di to estimate the the transmitted symbol where Q(.) is the soft/hard decision function.

### 3.2.2 Interference Cancellation

The effect of symbols already detected can be subtracted from the symbols yet to be detected. This improves the overall performance when the order of detection is chosen carefully. Denoting the received vector y by y1, if the nulling vector is w1, then the decision statistic for the 'first' symbol is If x1 = Q(d1) is the estimated x1 after the decision (soft or hard), then the interference due to x1 on the other symbols can be subtracted by taking assuming  x1 = x1, i.e, the decision taken was correct. The next symbol is then detected by finding w2 and then making a decision on wT 2 y2 and so on. The performance of this successive cancellation and detection scheme depends on the decision taken on each stage, as any wrong decision is propagated through all the later stages.

### 3.3 Optimal Detection Order

To minimize error propagation the 'strongest' symbols are detected first. This is known to be the optimal detection order.

A simple 'optimal' ordering is based on the postdetection SNR of each sub- stream. The SNR for the ith detected symbol of vector y is given by [13] where _2 is the noise power and E{} denotes the expectation. As ||wT corresponding hi have higher 2-norm. So the SNR in (3.2.7) for the ith substream is proportional to the norm of the ith column of H. Thus, the optimal detection order is in decreasing order of the 2-norm of the columns of H.

3.4 Computing the ZF Nulling Vector The vector wi in (3.2.3) is unique and is the ith row of the pseudoinverse of H [13] where <>i denotes the ith row and + denotes the pseudoinverse.

With the successive cancellation and decoding, is chosen as the ith row of pseudoinverse of H whose 1 to i - 1 columns are set to zero. This is due to the fact that at the ith stage the vector wi has to be orthogonal only to hj for j = i to t. With optimal ordering, if {k1, k2,    kt} denotes the optimal order, at the kith stage the ZF nulling vector wki is where Hki-1 denotes the matrix obtained from H by zeroing the columns k1,

3.5 Computing the MMSE Nulling Vector Using the MMSE criterion, the nulling vector is the ith row of the matrix where is the SNR [14]. For successive decoding and optimal ordering based on G, the matrix G should be computed on each step from the partially zeroed H as in (3.4.2).

The MMSE criterion always results in better SNR and thus a better performance. But the disadvantages are that the SNR has to be known at the receiver and a matrix inverse need to be computed.