# Wireless mesh network

### Abstract—

In recent years, the wireless mesh network gain momentum as a new broadband internet access technology, where most of the traffic is towards the gateway asthe user needs to access the internet and other wired resources. However, increased network capacity is still open; one way to increase the network capacity is to equipped each mesh router with multi-radio and turn each interface into a non-overlapping channel. These additional interfaces can create multiple concurrent linksbetween adjacent nodes. In this paper, we propose a channel reservation scheme for common traffic in WMN, which reserves one of these links for common traffic support, while the remaining channels can simultaneously beused to support other traffics such aslocal traffic.

Our scheme aims to reduce the interference for common traffic, support full duplex transmission as well as enable multi-flow transmission simultaneously. Simulation results show that this proposed scheme can greatly improves performance of multi-radio multi-channel wireless mesh networks.

### I. Introduction

Recently, wireless Mesh Network technology has gained a lot of attention and became popular in wireless technology and industry field owing to their low cost, rapid development and offer broadband wireless access to the internet in places where wired infrastructure is not available or worthy to deploy [1].

WMNs are composed of mesh routers which collect and relay the traffic generated by mesh client.

Mesh routers are usually stationary and equipped with multi-radio. Mesh clients are typically mobile and relay on mesh routers to deliver data to the intended destination. One or more mesh router may have gateways functionally and provide connectivity to other networks such as internet access figure 1[20].

In WMN, the most of traffic is generated by mesh client toward the gateway or from gateway to mesh client, this kind of traffic is called internet traffic which is the common WMN traffic as the user needs to access the wired resources.

Previous study was shown that the WMN backbone inherits some scalability problem in terms of throughput, delay and packet delivery ratio due to interferences [15] [16] [17] [18].

WMNs capacity is reduced by interference from simultaneous transmission. There are two types of interference affect the throughput of WMN:

Intra-flow interference is caused by medium access contention between different links along the flows, and inter-flow interference between different flows[21]. The main reasons are as follows:

- Half duplex of the radio.

- Broadcast nature of wireless medium.

Several approaches have been proposed to improve the WMNs capacity, one approach is that each mesh router uses single radio interface that is dynamically switching to wireless channel with different frequency band to communicate with different node, and however this Approach increases the routing overhead due to switching delay.

The more practical approach is use multiple radio interfaces are dedicated to non-over lapping channel.

The IEEE 802.11 b/g and IEEE 802.11 a standard define 3 and 12 non-overlapping frequency channel, which greatly increases WMN capacity due to avoid transmission completion and collision in the same channel and to eliminate the interference [3] [4].

One of the most important design questions for multi-radio multi-channel is how to bind each radio interface to channel. In a way that keeps the network connectivity.

However, most of the previous researches focus on how to answer the above question without consideration the unique properties of WMN such as:

- Mesh router is fixed and no mobility is considered on the routing algorithm works in backbone where the link between mesh routers is stable.

- The inter-flow or intra-flow traffic must pass through the backbone nodes to reach their destination and the backbone works as relay nodes. Thus improving the backbone performance will increase the WMNs performance.

- Availability of multi-link between adjacent mesh router, make the mesh router can support multi-flow transmission simultaneous.

According to above unique characteristic WMN, we propose reservation (allocation) channel for common traffic based on AODV reactive routing discovery process.

Our propose algorithm will increase the WMN backbone capacity, supported full duplex transmission for common traffic and also support inter- flow and intra flow traffic.

The remainder of the paper is organized as follows: section 2 discusses relevant related work. The AODV-MRCR protocol is explained in section 3. In section 4 we provide details of our simulation environment. Simulation results and their analysis are presented in section 5 with concluding remarks in selection 6.

### II. Related work

Several routing protocols have been proposed to join routing protocols with channel assignment. Deves [5] proposed first multi-radio multi-channel metric, which increases the diversity between channels to reduce the intra-flow interference. The protocol has proposed identical channel assignmenti.e. assign channel 1 to interface 1 and channel 2 to interface 2 and so on. Such approach clearly preserves network connectively but does not reduce interference.

The Hyacinth architecture [4] proposed distributed channel assignment based on spanning tree topology where the gateway is the root of the spanning tree. The protocol dedicates one interface channel for communicate with its parent node on the tree and other interfaces are configured as child for communication with its child nodes.

A node can only switch one of it child interfaces while theparent Interface is associated with a unique child of its parent. One drawback of this protocol is that it considers only the common traffic where data is transmitted from source to gateway and vice versa.

MCR [6] proposed to overcome Hyacinth's problem by considering local traffic as well as internet traffic. MCR classified the node interfaces into two kinds:

- Fixed Interface.

- Switchable Interface.

The protocol uses fixed channel as a common channel for communication between neighbours and the remaining considered as switchable interfaces.

Whena node wants to communicate with others, it looks in its table to find the destination's fixed channel and switches one of the interfaces to that channel.

To exchange fixed channels between neighbours, MCR uses a hello message to carry the fixed channel information. However, this protocol may not work well in a multi-flow transmission because of high switching interfaces and it does not utilize all non-overlapping channels as the static channel assignment uses.

In [7], the authors proposed the local channel assignment (LCA) algorithm which adopts tree-based routing protocol for common traffic similar to Hyacinth.

LCA algorithm solved Hyacinth conflict interface-channel assignment which is caused when a parent switches to the least load channel that may be in use by one of its children, the interface-channel assignment problem may cause recursive channel switching and delay.

LCA solved the above problem by dividing the non-overlapping channel into groups and made each parent interface belong to one group which differ from its child interface group.

Both protocols discussed earlier assign channels from node to node and every node in WMN assigns fixed channels which makes it different from our approach. In our scheme, channel assignment is based on data flow. That is to say that a channel is only assigned to a node if and only if it has data to send or forward to the gateway.

In [8] [9], algorithms to minimize the network interference have been proposed. [8] Uses genetic approach to find the largest number that makes whole network connectivity, while minimizing network interference.

The algorithm proposed in [9] is interference-aware, as it visits the links in decreasing order of the number of links falling in the interference range and selects the least used channel in that range. Assuming the knowledge of the set of connection requests to be routed, both an optimal algorithm based on solving a Linear Programming (LP) and a simple heuristic are proposed to route such requests given the link bandwidth availability determined by the computed channel assignment. The algorithm considers minimum-interference channel assignments that preserve k-connectivity.

However, such approaches only focus on minimizing network interference which may decrease the network connectivity, in constructing our approach based on eliminating the interference for common traffic on WMNs while keeping the network connectivity.

As we focus on AODV routing protocol several approaches has been proposed to improve AODV in WMNs [10] [11] [12] [13].

AODV-ST [10] is hybrid routing protocol has been designed with the aim of providing Internet access to Mesh clients with the help of one or more gateways.

AODV-ST uses proactive strategy to discover routes between the mesh router and gateways, and reactive strategy to find routes between mesh routers.

AODV-MR [11] has been proposed to improve AODV to work in multi-radio WMNs. AODV-MR assumes that each node has at least one common channel with neighbours.

AODV-MR broadcast the Router Request Message (RREQ) on all interfaces. The first RREQ message received by destination or intermediate node is selected and all duplicate RREQ s are discarded.

In addition AODV-MR increases the network capacity because it causes lower degree of interference and contention time because of distributed the traffic across multiple non-overlapping channels. However, it does not utilize the all non-overlapping channel and the path selection may select less capacity link or instable path.

AODV-HM [12] is a node-aware routing protocol that can successfully differentiate between backbone nodes and client nodes.

In [13] proposes CA-AODV to assign channel within k hop in ad hoc network, thus allowing concurrent transmission on the neighbouring links along the path and effectively reducing the intra-flow interference.

However, such approach may not work well in WMNs where the most of the traffic toward the gateways and must pass through mesh router.

III. MULTI-RADIO AD-HOC ON-DEMAND DISTANCE VECTOR ROUTING PROTOCOL WITH CHANNEL RESERVATION SCHEMA (AODV-MRCR)

A. AODV-MR

AODV routing protocol is a reactive distance vector routing that has been optimized for mobile ad hoc [2]. When a source node has data to transmit, it checks the route table for destination entry. In case the route is not known, it generates and broadcasts route request packetsto its neighbours.

Each RREQ packet has a unique ID used as identifier and the sequence number indicates the freshness of control packet.

When the intermediate receives RREQ packet that it has not seen before, or does not have fresh route to destination, a reverse path to destination is created and rebroadcast after incrementing the hop count. As RREQ is received at the destination orintermediate node with fresh rout to destination, rout-reply packet is generated and unicast to source of RREQ using the reverse path.

Each route reply packet contains destination sequence number and destination address router life time together with hop count and control flags. Each intermediate node will receive the RREP packet. The nodes receiving the RREP for the first time increment their hop count, establish a forward path to source and unicast the RREP to next hop using reverse route. However, the difference between AODV and AODV-MRis that AODV-MRbroadcasts RREQ packet on all nodeinterfaces. Thusthe intermediate nodewithone or moreinterfaces which operates on the common channel will receive many copies of the RREQ Packet.

The first route request received at intermediate node is selected and all subsequence route requests arediscarded. For receiving RREQ, a reverse path is established with the recommend interface.

The entire document should be in Times New Roman or

The setup of the forward path in AODV-MR [11] is similar to AODV [2], where the destination generates the RREP packet whenever it receives an RREQ packet and unicast to next hop using reverse path entry.

### B. Our Proposal Routing (AODV-MRCR)

AODV-MRCR is multi-radio on demand distance vector routingprotocol proposed to reserve a unique list of channels for common traffic in WMN. Our protocol is an extension of the AODV-MRwhich aims to improve AODV to work in multi-radio WMN environment.

The protocol tries toutilize the availability of multi-link between neighbours, by reserving one of them to transmit the common traffic while the remaining links be used to transmit other traffics, See the following figure.

All title and author details must be in single-column format and must be centered.

Figure 3: Multi-radio Mesh Network and logical topology

The scheme is implemented by using on-demand routing protocol discovery to distributea channel reservation list for everynode alongthe path from source to destination.

When a node has data to transmit, and it does not have a fresh route to destination, it broadcasts RREQ in all its interfaces similar to AODV-MR.

The neighbouringnodes and destination with common channels will receive many copies of RREQ and a reverse path will be create for first RREQ receivedand discard all subsequence.

At the gateways, for every RREQ received, a list of channelis select and the number of channels on each list is based on the number of hops between source and destination, see figure 4.

By using better distribution channels along the path, both the inter-flow and intra-flow interferences will be eliminated, as there is only one link using the selected channel within its interference range as shown in figure 5.

From theabove figure,only three channels are required to be select for eachlist.

During router replay phase, channel information is carried in the unicast RREP message. Two fields are added to RREP packet, which point to channel information, namely, recommend channel, which refers to channel use to communicate with next hop along the path and channel list which contains a list of reserved channels for the flow.

Before the gateway sends a unicast RREP to the source of RREQ it selects one channel from the list and attaches it to the RREP packet.

For each intermediate node that received the RREP builds the forward path to the destination with channel recommend information and select one channel from the list according to following information.

Figure 6: AODV-MRCR Route routing Table fieldsThe intermediate nodes modify the recommend channel in the router table for a reverse path and modify the RREP's recommend channel to the selected channel and send to next hop using a reverse path as follows:

Figure 7: RREP Processing in AODV-MRCR at Intermediate Node

IV. SIMULATION ENVIROMENT

The efficient of AODV-MRCR in comparison to AODV-MR[11] was evaluated using ns-2[14].

A mesh network converge on area 1000 x 1000m was established using random distribution mesh router.

Each mesh router was equipped with four wireless interfaces which statically turned to non-overlapping channel using same channel allocation schema.

Concurrent UDP flows are established between randomly select source and gateway.

The performance metrics are obtain by average the results from over thirty simulation runs for every experiment. The common parameters for all the simulation are listed on table 1.

TABLE 1: SIMULATION PARAMETERS

| Simulation Time | 250 seconds |
| --- | --- |
| Simulation area | 1000m × 1000m |
| Propagation Model | Two-ray Ground Reflection |
| Transmission range | 250 m |
| Traffic type | CBR(UDP) |
| Packet Size | 512 bytes |
| Packet rates | 20 packet/second |
| Number of nodes | 100 |
| Number of radios | 4 |
| Number of connection | 10,20,30,40,50 |

A. Communication Model:

IEEE 802.11 Distribution Coordination Function (DCF) [19] is used at Mac layer with channel switching delay 80 millisecond [16]. All packets are transmitted using the un-slotted Carrier sense multiple access protocol with collision avoidance (CSMA/CA).

B. Performance Metrics:

The simulations provide the following three performance metrics:

- Packet Delivery Ratio: The ratio between the number of data packets successfully received by destination nodes and the total number of data packets sent by source nodes.

- Aggregate Goodput: The total number of application layer data bits successfully transmitted in the network per second.

- Packet Loss: The number of packets that were lost due to unavailable or incorrect routes, MAC layer collisions or through the saturation of interface queues.

- End-to-end delay of data packets: This is define as the delay between the time at which the data packet originated at source and the time it reaches the destination, and includes all possible delays caused by queuing for transmission at node, buffering the packet for detour, retransmission delays. This metric represents the quality of routing protocol.

### V. SIMULATION RESULTS

To evaluate our protocol, we conducted two different scenarios. Our results come from average of thirty experiments for each scenario.

In the first scenario we check the effective of packet size on our protocol. We varied the packet size from 128 to 1440 with 20 packets per second. The number of flow injection from mesh router to gateways fixed to 50 simultaneous flows with 20 packet/second data rate.

The experiment results depicted in figure 8 shown that AODV-MR achieve poor network performance in term of throughput, packet loss, and delay. This is because of AODV-MR does not consider channel used for each flow in the area which may leads to uses same channel for many flow which caused interference between simultaneous transmission flows.

In figure 8(a) shows that our protocol reduces the packet loss over the AODV-MR protocol because of large packet size need long transmission time, thus the property of collision happen between simultaneous transmission become high.

In construct, our protocol achieve better performance over the AODV-MR, this due to our protocol assign unique list of channel for each flow by using our reservation schema which reduces the interferences between simultaneous transmission flows. The lower packet losses incurred by our protocol enable it to achieve significantly higher packet delivery ratio (figure 8(c).

In second scenario, we study the behaviour of our protocol on low and high traffic load. We varied the traffic load in the network by increasing the number of simultaneous connection between mesh router and gateways from 10 to 50 connections, with increment of 10 connections. The packet size for each connection was fixed to 512 byte with 20 packet/second data rate.

Our results (figure 9) show that at lower traffic load such as 10 or 20, the performance of AODV-MRCR is comparable to that of the AODV-MR. This due to AODV-MR can utilize the four channels to create channel diversity along the path which minimize the number of link on same channel within the path.

However, as load is increased, the packet loss incurred by AODV-MR increases significantly, thereby decreasing the goodput of network as in figure 9(b).

In construct, our protocol (AODV-MRCR) assign unique list of channel to every flow during routing establishing stage. This leads to divide the active area from single collision domain to many collision domains as number of flow increase.

We see an improvement performance of former under increase traffic loads Relative to AODV-MR.

Figure 8(c) and 9(c) show average end-to-end delay varying with number of traffic flows and the packet size respectively. As both flows and packet size increase. Our protocol achieves better average end-to-end delay than AODV-MR. This because of our reservation schema allow the AODV-MRCR protocol to assign different non-overlapping channel per each node for common traffic which leads to reduce the contention time at MAC layer, as well as allows the node to receive and send simultaneous.

### VI. CONCLUSIONS:

In this paper, we propose a channel reservation scheme for common traffic in WMN, which utilize multiple links between multi-homed nodes in infrastructure wireless mesh network. The proposed protocol reserves one of these links for common traffic support, while the remaining links can simultaneously beused to support other traffics such aslocal traffic.

AODV-MRCR reduces the interference for common traffic, support full duplex transmission as well as enable multi-flow transmission simultaneously.

Simulation results show that AODV-MRCR can improve throughput and reduce packet loss as well as reduces end-to-end delay of the network.