# There has been a radical growth in the Asian economies

As seen over the past decade, there has been a radical growth in the Asian economies, which has led to a growth in the construction industry in the Asian developing countries. The massive need in Infrastructure, Residential, commercial and Industrial sector is going to see further growth in years to come. The construction industry in India is worth over US Dollar 51 billion and accounts for more than 20 per cent of GDP. (The Hindu, 2010) As major construction activities are happening such as skyscrapers, residential building, office buildings, luxurious hotels, airports and shopping malls, in which Elevators play an integral part as it gives swift access to the higher floors. Since last few years due to global warming, construction industry is going green for their upcoming projects. As GOING GREEN is a campaign all over the world, companies are trying to get themselves the title of a “Green Company” as the consumers are becoming more conscious about the environment. Recent study by National Geographic has shown that Indian and Chinese consumers are best at making green choices compared to other countries. (AHN, 2010) Thus Companies are adopting environmental friendly approach for their products. One such company whose aim is to continue to grow strategically and profitably in a green way is ThyssenKrupp Elevator. Innovation, quality products, services and lasting customer relationships are hallmarks of ThyssenKrupp Elevator. (ThyssenKrupp Elevator, 2009)

ThyssenKrupp Elevator which is one of the world’s leading Elevator Company. Their current environmental policy is to offer energy efficient drives and control systems for their elevators. As a conscientious corporate citizen, ThyssenKrupp Elevator’s sustainability objective is to help contribute to Green Building Council’s LEED (Leadership in Energy and Environmental Design) certification for building by proper project analysis and product recommendations. ThyssenKrupp Elevator is also looking towards the future and is working diligently to develop products and services, which reduce energy consumption and encourage the use of reduced environmental impact materials. (The McGraw-Hill Companies, 2010)

Having studied their current product line I would suggest that they incorporate the following changes in their product lines.

Introduce energy regenerative Inverter (drives) for their elevators.

Introduce PMS (Permanent magnetic synchronous) gearless motor.

Introduce LED lighting for their cabins.

ThyssenKrupp elevator uses energy efficient drives for controlling the motor speed, use of regenerative type of drives for motor control would further improve the efficiency as in this case we not only save on the consumption of power but we also generate power and feed it back to the main grid or use it for lighting in the other lifts or for building lighting and heating.

The working of the regenerative drive in elevator is similar to a Hybrid car, where it recharges its battery while braking. The working of the regenerative drive in elevator can be explained in the following manner; the elevator car is linked to a counterweight via a pulley system which is the traction machine. When an ascending cabin is full of passengers, the system uses electricity to run the traction motor that pulls up the cabin. When the car is full and descending it needs to break, so that it does not free fall. When a fully loaded elevator is descending or a lightly loaded car is ascending, the counterweight at the top of the shaft/ elevator-well has potential energy which is released as it moves down. This potential energy is converted to kinetic energy and helps turn the traction motor causing it to act as a energy generator with the help of the regenerative drive. In this way the traction motor works in motoring mood as well as generator mood. Thus a Regenerative drives reduce elevator energy use by up to 75 percent compared to non- regenerative drives. The advantage of regenerative drive is not only energy efficiency but the regenerated electricity is fed back to the building's power grid to be reused for things such as lighting and heating. (Jin-seo.C, 2008)

Traction machine is an important part of elevator which consumes lot of energy. The motor is coupled to the gear box which in turn moves the cabin up and down. This machine needs lubrication, oiling and greasing is required for reducing the frictional losses. This machine consumes lot of energy which is explained in the bar chart below. I would recommend ThyssenKrupp Elevator to use PMS Gearless machine which is a permanent magnetic synchronous motor which doesn’t require any lubrication as the working is completely based on permanent magnet, no oiling greasing for maintenance and it creates less noise. In Comparison to geared machine PMS gearless machine is energy efficient as shown below in the bar chart. Gearless machine when attached with regenerative drive, the average energy consumption will be 1540Kwh/year whereas for geared machine without energy regeneration drive the average energy consumption will be 5000kwh/year as per the data attached below for different traction motors. The Average energy Consumption bar chart shown below is calculated based on: an elevator speed of 1.0 m/s (0.63 for hydraulic), a load of 630kg (8 persons) and 200,000 starts/year. (Kone, 2010)

Source: KONE elevator eco- efficiency

http://www.otis.com/site/in/OT_DL_CommonImages/Ba4_Geared.jpg

PMS gearless Motor

260GD Permanent Magnet Gearless Motor

Source: Otis Elevator

Surprisingly it is not only the traction motor which consumes energy it is observed that the Elevator cabin lighting can consume up to 40% (equal to 1100 kWh) of the elevator’s energy consumption. I would recommend ThyssenKrupp Elevator to use long-lasting LED light in their elevator cabin which is eco-efficient compared to Halogen bulbs. LED lights are optimized for maximum efficiency and natural colour saturation. LED lights last up to 10 times longer than traditional halogen bulbs and use up to 80% less energy. (Kone, 2010)

In one of the article in Korea Times it was mentioned that if LED lights in the cabin, gearless traction machine and regenerative drives are used for all the 340000 elevators operating in Korea it can save 1.7 billion kilowatt hours of electricity or 200 billion won. It was also mentioned that this saving is equivalent to 10 million barrels of gas and 260000 tons of carbon dioxide emission. So the product is not only better for the environment but also eliminates costs. (Jin-seo.C, 2008)

Production of this new regenerative drives, gearless machines and energy efficient LED lights for the cabin can be taken up in their existing plants worldwide. Manufacturing of this product may be costly in the initial years, but as the quantities increase and the new technologies are introduced in the production it would become cost effective because of the economy of scale. According to ACEEE (American council for energy efficient economy) the incremental cost of regenerative drive is roughly $10000/per elevator. This additional cost can be covered by reduced energy expenses in the long run. (Harvey.S, 2005)

The existing distribution network of ThyssenKrupp elevator can be used to reach the product safely and on time to the project sites. The elevator has to be delivered to site by truck or container load. The material is unloaded and stored safely in the storage space provided by the client at job site. (Jobber.D, 2001)

Elevator is an engineered system once installed the core elements such as cabins, shaft/ elevator-well will be used for life of the building in many case around 50 years. However during their service life some components can be changed or upgraded to latest technology on a 20 to 30 years renovation cycle. (Harvey.S, 2005)

Marketing and promotion of this green product can be done through their existing marketing and sales team. Direct sales force in different regions around the countries can market this product by giving presentations to Architects, consultants, Construction Engineers, Property Developers, Builders and also to existing clients in order to educate them about energy efficiency and regeneration of energy from elevators for their upcoming projects and suggest them that the new product will be economical in terms of energy consumption compared to conventional elevators. (Jobber.D, 2001) Apart from this modernisation sales team can target old residential apartments, office Building, Hotels, Hospitals and Government offices where conventional elevators are being used which are in bad shape, which consumes a lot of energy, money and needs replacement. By modernising elevator with this new energy regeneration drive one can reduce the overall elevator energy consumption by up to 75 percent compared to systems with non-regenerative drives. Modernisation sales team can also market this green product where competitors have installed conventional elevator which doesn’t regenerate energy, by doing this ThyssenKrupp elevator can increase its market share.

The existing marketing team will be motivated with the new product line in their portfolio. Their moral would be high thus achieving higher sales numbers for the company which in turn would result into higher profitability.

ThyssenKrupp Elevator can publish eco friendly product Brochures for which can be made out of recyclable paper, it can also market their green product in elevator magazines which are circulated around the world. The company should opt for GREEN MARKETING by taking e-Marketing route for this new product in India as highest number of searches for green marketing has originated in India than any other country. (Google Trends) This will spread awareness about the new eco friendly product to new customers.

The plan of selling energy regenerative elevators will not only provide financial gains to ThyssenKrupp Elevator but will also be named as a Green Technology Elevator company. Energy regeneration in elevators is an innovative technology no other company in Indian market has come up with this kind of product so ThyssenKrupp Elevator will have an edge over the existing competitors and will also have a first mover advantage. So I believe that it is a great opportunity for ThyssenKrupp elevator India to add this green product into their existing product range and sell them profitably in a Green way.