### What is Modulation?

Modulation is the process of transforming a message signal to make it easier to work with. It usually involves varying one waveform in relation to another waveform. In telecommunications, modulation is used to convey a message, or a musician may modulate the tone from a musical instrument by varying its volume, timing and pitch. In radio communications for instance, electrical signals are best received when the transmitter and receiver are tuned to resonance. Therefore keeping the frequency content of the message signal as close as possible to the resonant frequency of the two is ideal. Often a high-frequency sinusoid waveform is used as carrier signal to convey a lower frequency signal. The three key parameters of a sine wave are its amplitude ("volume"), its phase ("timing") and its frequency ("pitch"), all of which can be modified in accordance with a low frequency information signal to obtain the modulated signal.

A device that performs modulation is known as a modulator and a device that performs the inverse operation of modulation is known as a demodulator (sometimes detector or demod). A device that can do both operations is a modem (short for "Modulator-Demodulator").[1]

## Digital modulation methods

In digital modulation, an analog carrier signal is modulated by a digital bit stream. Digital modulation methods can be considered as digital-to-analog conversion, and the corresponding demodulation or detection as

analog-to-digital conversion. The changes in the carrier signal are chosen from a finite number of M alternative symbols (the modulation alphabet).

A simple example: A telephone line is designed for transferring audible sounds, for example tones, and not digital bits (zeros and ones). Computers may however communicate over a telephone line by means of modems, which are representing the digital bits by tones, called symbols. If there are four alternative symbols (corresponding to a musical instrument that can generate four different tones, one at a time), the first symbol may represent the bit sequence 00, the second 01, the third 10 and the fourth 11. If the modem plays a melody consisting of 1000 tones per second, the symbol rate is 1000 symbols/second, or baud. Since each tone represents a message consisting of two digital bits in this example, the bit rate is twice the symbol rate, i.e. 2000 bits per second.[2]

According to one definition of digital signal, the modulated signal is a digital signal, and according to another definition, the modulation is a form of digital-to-analog conversion. Most textbooks would consider digital modulation schemes as a form of digital transmission, synonymous to data transmission; very few would consider it as analog transmission.