# Fire safe design

Fire safe Design is at the centre of all good construction, discuss the implications in terms of material selection for a commercial building.

Following on from the devastating collapse of the world trade centre there has been an even greater demand placed on architects to design buildings to delay and prevent fire by incorporating materials that do not react together during high temperatures.

Commercial buildings now need to be designed to incorporate efficient, cost effective passive and automatic fire protection systems; this is done by carefully selecting materials. When deciding on materials the designer will need to look at what material will contain , control and possibly extinguish a fire in the early stages t prevent fire spread and in particular for a commercial building to allow time delays for people to evacuate. The designer needs to ensure the materials are not combustible and understand how the materials react with heat; they also need to adhere to building regulations/Fire (Schedule 1, part b). Although the designer needs to meet fire ratings of materials, he also needs to balance safety with sustainability by trying to use green products.

Non structural elements such as walls and ceilings are linked to the structural integrity of a building therefore when selecting material fire safe design is key, as if they collapse it opens up more area which creates additional air and fuel for a fire to grow. The designer needs to understand the thermal expansion of a material and the important relationship they have during fires.

One of the key elements of a building is the actual structure which needs to maintain its integrity and stability during a fire, majority of commercial buildings are made from steel, brick or concrete structures. Steel is non combustible and it is said to withstand temperate of up to 550�c before it would begin to loose strength, with an average temperature for a standard fire being 1000�C it is crucial that the steel is reinforced to prevent it losing its integrity and stability. In designing the building it is imperative to take this factor into account when planning fire safety design. To protect or strengthen steel from fire there are several ways that one can achieve this, the first being to remove steel form the direct course of fire, by casing it within another material such as boards that are fire resistant, this will increase the fire rating time to 4 hours as oppose to approximately 30 minutes if left unprotected. It is vital that the designers looks at the materials and how they interact with each other, for example a sprayed material on steel being used in conjunction with a board material, since water from the spray could have an impact on the fire properties of the board the designers would have to look at how this would effect the properties of the board. Another method used to protect steel is to use hollow steel and fill with water to allow the steel to cool, and finally the last method I will mention is to coat the steel with intumescent coating which is a decorative spray paint that is applied to the steel to provide fire resistance. The collapse of any structure is also dependent on several other factors including loads, the diagram below shows the failure rate temperature is less according to loads placed on the steel. (http://www.corusconstruction.com)

Concrete is another material used, it is not chemically active and has poor thermal conductivity, it also doesn't contribute to the fire load, which creates a slow rate of heat transfer, again this is dependent on how the material is used, the thickness of the concrete as this plays a large part in keeping the heat transference within an acceptable limit. During high temperatures concrete can break, up which can lead to a loss of protection to the steel used and also reduce the thickness of the concrete, this is why it is vital to ensure the correct aggregate is used. Concrete has many attributes in fire design , those being it helps contain the fire within the buildings boundaries, if used in walls and roofs it prevents the fire jumping across to other buildings, and most importantly it can save lives. For concrete to be so effective in a fire it is dependant on the thickness of the concrete, the type of build, i.e. solid walls or hollow with services running through, it is also dependant on the quality of the cement used, however even though concrete will start to decrease at temperatures of 200�c, it does not begin to spall until it reaches 900/1000�c which is the temperature for a fire in full flow. One should stress that as with all materials the strength is dependant on the growth of the fire and other factoring materials that could increase temperatures, i.e. chemicals and gases that will interact with other materials and cause greater damage.

Timbers, although not commonly used do form part of structures and are seen in larger quantities in floors, stairs, panels and doors. Timbers ignite quite quickly and emit a high level of smoke with carbon monoxide, which are deadly. Timbers are more sensitive to fire and will spread easily, also any paints applied would also contribute to the growth of a fire and the designer needs to question this if using within the design of a building, whilst timbers can be treated to reduce the speed in which they diminish under fire conditions the designer needs to also be aware that they will burn and contribute the same amounts of heat and fumes if they sustain a high enough temperature. The designer would also have to look at how timers are joined to other structural elements, given that they allow fire to spread across them, however once timer is charred this creates a protective coating around the timber to reduce rapid deterioration and gives a more steady flow rate.

There are many more materials that one could analyse for their effectiveness under fire conditions, in this essay we have looked at the three main materials used in commercial buildings, a simple chart below shows the effectiveness of each material without any protection in place when coming into contact with fire.

To conclude, designers within the construction industry be they architects, fire design engineers or quantity surveyors need to ensure they have knowledge of the materials they hope to incorporate into the design, they need to know how they react with each other, such as concrete protecting steel, whilst also ensuring they understand their limitations with regard to fire within the building. Fire protection within buildings and the actual materials can be costly and it is something fundamental that the designer needs to look at, as although costly to the design it could also be costly to the developer or owner of the building should there be a fire and inadequate protection has been put in place, it would also be a breach of building regulations which would come with a hefty fine and possible imprisonment.

Although fire design and material selection is key, this is also dependant on materials being readily available and also being cost effective and sustainable, with more emphasis being placed on the environment designers need to look at alternative materials that do not place such a high cost on the environment, designers need to look at the use of alternative materials and alternative technologies to enhance fire design.

The research conducted has shown that poor section of materials could be detrimental to the building in the event of fire, but one also has to look to the overall design and how the structure and its elements are joined together to ensure safety , as designing steel beams encased in concrete alone is not enough to prevent fire spread, one has to look at floor design and how they are joined to the structure and also other materials present such as plastics, it is also important to take into account the building use and the materials the occupants will bring into the building. Even though materials and their fire resistance have played a large part in design for some time, the activities if the last decades in the way of terrorist attacks have led to even more emphasis being placed on materials selection and is stability during fires.

- Bjorhovde, R., Engstrom, MF., Griffis, LG., Kloiber, LA., and Malley,JO., (2001) Structural Steel Selection Considerations A Guide for Students, Educators, Designers, and Builders

- Read, REH., and Morris, WA., (1993) Aspects of Fire Precautions in Buildings

- Morris, WA., Read, REH., and Cooke, GME., (1988) Guidelines for the Construction of Fire Resisting Structural Elements

- Berge, B. (2000) The Ecology of Building Materials. UK: Reed Educational & Professional Publishing Ltd

- Dunkeld, M (2009) Construction Technology 2, Steel in Fire.

- James, D. (2009) Material Science, Fire Safety.

- http://www.bre.co.uk

- http://www.planningportal.gov.uk

- Wilkins, R. (2009) Personal Tour and Interview (Corus Steel Mill Scunthorpe) 30 November