# System of electrical transmission

PSTN (Public Switched Telephone Network)

History of RTC

In 1854, French inventor Charles Bourseul was the first to devise a system of electrical transmission of speech. In 1877, the American Alexander Graham Bell built the first telephone capable of transmitting the human voice, while maintaining its quality and timbre.

In France, a large telecommunications development plan was implemented during the 1970s, leading to rapid equipment.

Pending the installation of automatic across the French territory (which is effective at the end of the 1970s), telephone exchanges and home to many qualified personnel. The most famous figures in this microcosm are the "telephone ladies", so called because this category of staff was recruited exclusively among unmarried girls, whose education and morals are beyond reproach. She generally lost their jobs when they married

Research conducted at the National Center for the Study of Telecommunications (CNET) and allowed the establishment of the first central fully electronic world. France Telecom decided to open its digital network subscriber integrated services (ISDN), marketed under the name of ISDN. This network can improve some services such as fax or interconnection of computers.

What is it?

The public telephone network (PSTN Public Switched Telephone Network or PSTN simply) mainly for the transfer of voice. Transport data is authorized in France since 1964. Using the principle of the switching circuits, it connects two subscribers through a dedicated link for the entire exchange.

There are two main parts in this network:

The capillary network or distribution, it is the connection from the subscriber's premises to an entry point of the network. This part of the network is analog.

The transit network, for its part, makes the transport of communications between the nodes of transit hubs / switches). This portion of the network is now digital.

Scanning has several advantages. Since this is only 0 and 1, the signal quality is maintained, regardless of the distance between the transducers (analog to digital and digital analog). This is not the case of analogue communications where the signal is polluted handling.

Overall management of the network identifies three functions:

- Distribution, it essentially comprises the subscriber connection or local loop (pair twisted wire) connecting the installation of the subscriber transmission to the center of attachment. This line provides the voice (voice frequency from 300 to 3400 Hz), numbering (10 Hz ottoman pulse dialing-in and dial-697-1633 Hz frequency dialing) and general signaling (loop current, frequencies above voice)

- Switching is the essential function of the network, it is to connect two subscribers, maintain liaison throughout the exchange and release resources at the end of it. This is the network that determines the parameters of taxation and charges the cost of the call to the caller transmission, this is the part support telecommunication network, this function is performed either through wired copper (being disappearance), fiber optic or microwave links.

Today, the network is almost fully digitized, the only connection is analog subscriber.

Operation of the RTC

The RTC is organized into three sub-sections:

- Switching: central part of the network. It allows for the linking between subscribers.

- Transmission: all techniques used to connect the switches together. All switches and switches between the transmission media is called transmission network or transmission system.

- Distribution: organization technique implemented to connect subscribers to the nearest switch (switch attachment). All devices for this connection is the distribution system.

Switched telephone network has a hierarchical organization at three levels. It is divided into zones corresponding to a level of concentration.

Can be distinguished:

Autonomy of Routing Area (BIA), the area, the lowest in the hierarchy has one or more of Routing Switches Autonomy (CAA), which themselves serve Switches Premises (CL). Local switches are only single line concentrators which are connected end-subscribers. The BIA (Zone Routing of Autonomy) is a star network, it is the service network;

Secondary Area Transit (ZTS), this area includes switches Transit Secondary (CTS). There are no subscribers connected to CTS (Secondary Transit Switches). They provide the CAA when mixing circuits (switch Autonomy of routing) can not reach the addressee directly CAA (imperfectly meshed network);

Transit area Main (ZTP), this area provides the switching of long distance connections. Each ZTP (Main Area Transit) includes a switch Main Transit (CTP), one of the main transit switches (CTP) switch is connected to international transit.

Next the supports is carried multiplexing techniques:

Time Division Multiplexing (PCM and PDH multiplex (Plesiochronous Digital Hierarchy) transmission in digital connectivity for digital

- 2 Mb / s: 30 voice channels.

- 8 Mb / s: 120 voice channels.

- 34 Mb / s: 480 voice channels.

- 140 Mb / s: 1920 telephone channels.

- 565 Mb / s: 7680 telephone channels.

It now favors the optical fiber (as highway information) as the transmission medium with the use of multiplex SDH (Synchronous Digital Hierarchy).

II - Scan signal

SIGNS SEMAPHORE

- Until the 1970s, the telephone system was analog. Since that time, the RTC s is scanned (RTC64) and scanning is now complete up to the local loop subscriber BLA (Subscriber Loop). It is also the same for signaling.

- Signage is all the dialogues that take place in the control plane functions between various users and control switches involved in a call.

There are two kinds of dialogue thus signaling:

- signaling link or signaling link associated circuit.

- signaling not associated with circuit.

Associated signaling circuit is implemented when a transmission means is taken adjacent. It is a question of a signaling section by section (Link by Link). So they are dialogues between adjacent control functions with the aim s to allocate a transmission channel or circuit.

- Not associated signaling Supplements For Service (CS) (Toll Free Numbers ...) and does not imply circuit. It is a question of a transaction in the control plan.

- Before 1970-80, signaling between exchanges was through transmission of specific tones closer and closer, each channel (DTMF, 2 frequencies from 5, MF R1 SOCOTEL, CCITT No. 5).

Signaling borrow the same circuit as the voice and was therefore in the band. The settling time of the communication was very long (> 3s!).

- Currently, the telephone network uses digital transmission techniques PCM channels.

- With the development of new services (call transfer ...), it was critical to separate the signal transmission and transit signaling that a specific network: OOB signaling channel semaphore.

The channel signaling or signaling semaphore can:

- implement digital transmission techniques (MIC).

- reduce the waiting post numbering.

- exchange control messages during the conversation.

- expand the range of possible messages therefore introduce Complements Service or comfort services.

- serve as platforms for intelligent networks (IN Intelligent Network).

- serve as the backbone Digital Network ISDN Integrated Services.

- better control fraudulent use.

The telephone network is made up of two communication channels:

- A transmission channel (user information)

- A signaling channel said control channel.

The control channel carries signaling related to a plurality of circuits. It can be used to exchange messages between management and supervisory switches.

The signaling network is a transmission network using the full packet switching.

RECOMMENDATION Q.700

System channel signaling is defined by ITU Recommendation Q.700. It is also called:

- SS7 Signalling Semaphore 7.

- CCITT 7.

- CCS7 (Common Channel Signalling System number 7).

- Its objective is the definition of a standard international signal optimized for digital networks and future services.

- It is suitable for working on circuits 64 kb / s. SS7 data traffic is quite low.

- Semaphore channel at 64 kb / s circuits typically 2000 can control simultaneously.

- The channel signaling does not support the routing function (spring software call processing switches).

- A set of standard messages are an application signaling SS7 signaling.

There are applications associated signaling circuit:

- TUP (Telephon User Part) signaling analogue PSTN.

- ISUP (ISDN User Part): Digital ISDN signaling.

There are applications not associated signaling circuit:

- MAP (Mobile Application Part): GSM signaling between MSC and VLR / HLR.

- INAP (Intelligent Network Application Part) signaling IN.

THE BENEFITS OF SIGNALLING SS7

- Ability to transfer signaling pure regardless of the establishment of a circuit.

- Reducing delays in transfer of signaling through the digital transmission (rule 3).

- Possibility to book tours for a call only when the called party is actually reachable (pre-test).

DISADVANTAGES OF THE SIGNAL SS7

- Complexity to designate the physical circuit which the signaling message is attached (logical view).

- Rupture of a semaphore channel makes it impossible to establish a set of communications.

- PS: Semaphore Point: These are telephone exchanges that generate and interpret signaling messages.

- PTS: Transfer Points Semaphore which are used when two telephone exchanges are not interconnected by a signaling link. PTS stores the signaling messages, analyzes their headers for routing and forwards (Store & Forward) as a standard router.

SS7 SIGNALING

- It is to logically separate the aspect of signaling information transmission aspect users (typically voice over a telephone network).

- The transmission network carries only the information user, the network semaphore signaling.

- But the two networks can potentially share the same physical transmission media.

- MTP (Message Transfer Part) or the Sub-Transfer System Messages (MTP) offers a transfer of signaling messages between a PS network. It includes 3 levels (physical, link and network).

INTERNET AND RTC

ENSEIR

INTRODUCTION

- The growing need for Internet connectivity is the problem of access teams and individual users to sites connected to the Internet.

- This type of access is not treated at global operators today in regional networks.

- Security measures are implemented to maintain the anonymity of the caller.

SLIP

Very simple protocol.

IP packets are sent to the PSTN with a byte separation END:

- END code 0xC0.

- if END in the data: ESC ESC_END (0x0D, 0xDC).

- if ESC data: ESC ESC_ESC (0x0D, 0xDD).

- No error detection.

- No negotiation (IP address, packet size, protocol carried).

- No security.

CSLIP

Similar to SLIP with compression of IP headers + TCP (40 bytes) called Van Jacobson (RFC 1144).

PPP (RFC 1661)

Point to Point Protocol

Standard method for transporting different protocol datagrams over point to point links.

PPP components:

- A method for encapsulating datagrams (PPP packet).

- Encapsulating the PPP packet in an HDLC frame simplified.

- Control protocol data link.

- Establish, configure, and test the link.

- A family of Network Control Protocols: establishing, configuring different network-layer protocols.

ENSEIRB

A DIGITAL NETWORK INTEGRATION SERVICES ISDN NARROWBAND

INTRODUCTION

ISDN is an acronym for Digital Network Integrated Services (translation of ISDN: Integrated Services Digital Network).

ISDN is defined as follows by the ITU-T:

"A Network Integrated Services Digital Network is generally developed from a digitized telephone network that allows digital connectivity from end to end providing a wide range of services, voice or otherwise, to which users have access by a set limited-purpose interfaces. "

- ISDN is a network of technically advanced.

- With the supporting infrastructure of the existing PSTN, ISDN achieves higher speeds.

- Narrow Band ISDN (ISDN Narrow) migrates to broadband ISDN Broadband (Broadband ISDN).

HISTORY

- Appearance in the late 70s.

- Natural evolution of the Public Switched Telephone Network (PSTN) traditional. The first public ISDN network in the world was launched in Britain in late 1987.

- Today, 100% of the French telephone exchanges are digital.

- t its marketing (to 1995), ISDN ISDN was called by France Telecom.

- Scanning the switching means that the electromagnetic switches are replaced with electronic switches to the time switch technology.

- Switching time: sequential exploration of N input channels. Development of a multiplexed frame comprising N time intervals (IT) of k bits.

- In ISDN PBXs for every IT has 8 bits and is repeated every 125? S, 8000 times per second (64000 b / s)

BENEFITS

- Separation of signaling and data transport.

- Signaling much richer.

- Decoupling of speed (signal / data).

- Availability signaling system during the transfer phase.

- Integration easier and more consistent new services.

- Call waiting, call forwarding.

- Presentation incoming calls.

- Mini messages ...

- Higher speeds and guaranteed (64kb / s between two ISDN subscribers) for data transfer (fax, Internet ...).

- Possibility of establishing virtual circuits in the data transport channels (B channels).

- Connection time between two ISDN adapters low.

- New signage with the subscriber: Protocol D.

- New signaling network: CCITT No. 7.

- New transmission between the subscriber and the switch.

Single network:

- Telephony.

- Fax G3 and G4.

- Data transmission.

- Sound.

- Images (H.261).

Network with national coverage.

Interfaces:

- R interface (Rated) provides an interface between non-ISDN equipment users and non-compatible ISDN adapter (TA: Terminal Adapter).

- S interface (Subscriber) separates the user network functions of terminal.

- T interface (Terminal): between the equipment and network provider equipment user. Provides a standardized interface between the hardware, the transmission and reception, validation and synchronization information to the network and to the part of the terminal concerned.

- U interface (User).

The connection of the telephone set of ISDN subscriber does not directly on the distribution line of the public exchange. The operator places the subscriber in a box TNR (Digital Network Termination).

The role of TNR does the level 1 of the OSI model. It provides:

- conversion functions into four two son son.

- Management access terminals on the line S0.

- the remote power supply of terminals and in particular telephone sets.

- protection of the site of the subscriber against overloads (especially lightning).

- The TNR itself may be self-powered by the telephone connecting.

- It can also be powered locally. In this case, a backup battery ensures minimal service to ensure a minimum telephone service.

- The telephones can not communicate directly among themselves (internal communication). To remedy this, you need to have a switch (TNA).

ISDN BASIC ACCESS 2B + D

- Goodput 144 kb / s for a flow rate of 192 kb / s.

- A frame of 48 bits every 250? S with 36 bits of data.

- 2 B channels at 64 kb / s for speech, data, text and images.

- 1 D channel at 16 kb / s for signaling, messaging and access to Transpac TPC (packet switching in the D channel).

- Standard user access side is called S0. It speaks of S0 for basic access.

- The standardized access network side is called T0.

Simplest topology to the user:

- passive bus network with a maximum of 8 outlets.

- ISDN RJ45 (ISO 8877).

ISDN PRIMARY ACCESS 30B + D

- Rate 1984 kb / s link to 2048 kb / s (E1).

- Connecting PABX, computers, servers.

- U.S.: 23B + D on a link at 1544 kb / s (T1).

- Standardized access user side: S2

- Standardized access network side: T2

Other three channels (hypercanaux) defined by the CCITT, mainly for video conferencing (H.261) H0: 384 kb / s, H11: 1536 kb / s, H12: 1920 kb / s.

Hypercanal is a concatenation of B channels and imposes a system of resynchronization reception due to different transfer times on each channel B.

Should be distinguish interfaces:

- User / Network (UNI).

- Network / Network (NNI).

- We begin by looking at the interface U / R is the only equipment must meet to connect to ISDN. The interface R / R must be respected by the operator.

- At the interface U / R, there are traffic and ISDN signaling.

- Signaling is in the band because it shares the same medium as traffic.

Traffic at the interface U / R: no normalization. We can use the channel B (or hypercanal) so crude or establish a protocol for there reliability and multiplexing:

- X.25: LAP-B and PLP (Packet Layer Protocol).

- PPP.

Signaling interface U / R:

- link level: LAP-D.

- network level: protocol D.

- This signal is to be seen as an extension to the user signaling R / R.

- ISDN uses circuit switching (such as the PSTN) with possibility of interworking with the packet switched network TPC.

ISDN: LEVEL 1

S0: transmitting a frame of 48 bits corresponding to two sub-frames comprising:

- 1 byte of the channel B1.

- 1 byte of the channel B2.

- 1 bit D-channel

- The transmission is full duplex at a rate of 192 kb / s 144 kb / s of throughput. The difference is the control bits of the frame.

- Using a bipolar RZ code base.

- B channels are established after establishing communication signaling. There is no contention access.

- The D-channel is shared by all devices connected to the ITA. There is a risk of contention.

The access method used is CSMA / CA:

equipment D listens to the channel before transmitting to see if it is free (at least the time of issue of 8-bit D).

The access method used is CSMA / CA:

- in the control bits of the sub-frame, there is a bit of echo corresponding to the value of D received by the bit and returned to TNR equipment.

- if the bit of the echo received by a device does not match the bit that it has issued, there is contention. The equipment stops transmitting.

- we define a dominant bit (0) and a recessive bit (1) so that it makes a wired-OR bus at the ITA (open collector or open drain).

- The equipment with the most consecutive 0's in the address field of the LAP-D frame gains access to the channel D.

- A station already issued in the D channel must wait a silence greater then (9 bits or more) to give a chance to other equipment.

Access S2: transmitting a frame of 256 bits in 125? S including:

- 30 bytes of channel B.

- 1 byte for the Lock Screen (IT 0). A Multi Frame Lock is implemented in two consecutive frames.

- 1 byte D channel (IT 16).

- The transmission is full duplex at a rate of 2048 kb / s 1920 kb / s throughput.

- Using a code base bipolar HDB3 high density.

ISDN LEVEL 2: LAP-D

- Recommendation I.411 CCITT (ITU-T).

- D LAP (Link Acess Protocol on D channel) defines a protocol frame exchange between peer entities U / R and R / R.

- It uses the service level 1, that is to say the D channel

LAP-D functions:

- envelope near HDLC LAP-B.

- error detection FCS (Frame Checking Sequence).

- flow control.

Other functions LAP-D:

- timing control frames.

- multiplexing several communications channel D.

Extension of the common channel signaling (SS7) to terminals.

LAP-D protocol for exchanging information in two modes:

- connected mode requiring the management of a data link connection can implement control functions of the sequencing of good frames, the flow control, detection and correction of transmission errors. In this case, the frames are numbered.

- the offline mode does not require the prior establishment of a data link to exchange information does not provide the control functions between entities sequence level 2: Use unnumbered frames (UI).

A frame LAP-D is at least one flag separated.

We apply the principle of transparency in the frame: a 0 is inserted between the 5th and 6th consecutive one issue deleted reception that a given byte $ 7E is not seen as a flag in reception.

There are the four classical fields of a frame LAP-B:

address, control, data (network) and CRC (FCS).

TEI is the identifier of the equipment using the D channel C 'is a single 7-bit value so rating:

- Manual: configure switches from 0 to 63.

- automatic power equipment supplied by TNR: 64 to 126.

- The value 127 is reserved during the phase of automatic assignment by TNR in power.

- SAPI identifies which the entity LAP-D is carried out at the request of the network level. It is the concept of SAP OSI!

There are 3 phases of operation of the data link:

- establishing the connection.

- data transfer (numbered frames).

- release of the connection.

For this purpose, different types of frames LAP-D are defined by the value of the command field:

- information frame, I frame (numbered).

- supervisory frame, frame S.

- frame unnumbered frame U (unnumbered).

With the SAPI TEI can unambiguously identify the entity level 3 affected by the information exchange level 2 and level 2 service implemented.

SAPI + TEI DLCI = Data Link Control (Id). We find this DLCI in the frame used in Frame Relay.

I frames:

The I frames are used to perform the transfer of information.

They contain information provided by the entity level 3 using the services of level 2. These frames contain further information relating to the control frame transmission:

- N (S) sequence number issue.

- N (R) sequence number received.

Information frames are still orders and can require a reply using the P bit (Poll) set to 1.

S frames:

S frames can provide supervisory functions of the data link and particularly management frames:

- sequencing.

- flow control.

- retransmission.

- suspending the transmission of frames.

S frames can be commands or responses.

U frames:

- U frames allow to implement the exchange of information frames without having to establish the data link in advance.

- The exchange of such information frame is therefore less secure (no timing control or flow).

- Unnumbered frames are used for the establishment and release of the data link as well as the management of sequencing errors or protocol.

CRC:

- The CRC field is calculated from all the data of the frame (excluding flags).

- It is calculated on 16 bits (generator polynomial of degree 16).

One finds as LAP-B for the sequence numbers at each end:

- N (S) Issue: number of the last transmitted frame.

- N (R) for reception: number of the next frame to be received.

Pays (N (R) -1) frames already received.

Differences between LAP-B and LAP-D:

- address field 2 bytes for LAP-D against 1 byte for LAP-B.

- modulo 8 for LAP-B against 128 for LAP-D.

- line maintenance for LAP-D does not exist for LAP-B.

Is sent (network) all the T203 (10 s) a RR frame to force the ISDN equipment to respond (P bit = 1). C is a logical way to physically see if the device is still connected to the ITA.

ISDN LEVEL 3: PROTOCOL

- ISDN signaling is the most significant aspect of ISDN. This allows you to exchange messages very rich. Beside the basic service that is the establishment of a communication, in addition a large number of additional services.

- The integration of telecommunications services through the implementation of ISDN based on the functional richness level 3 protocol D.

- The level 3 of Protocol D has as main function the call control to enable the implementation of circuit-switched connections or packet-switched.

The various functions performed by a network layer protocol manager D:

- dialogue with the level peer network.

- resource management communication.

- control of the compatibility of the information exchanged with the peer entity.

- verification services implemented and consistency of designation information (address, EI ...).

- implementation of timers and logical entities own management calls.

- processing service primitives exchanged level 2 with the binding moiety directly below.

Can be distinguished:

- call control circuit switched.

- the user to user signaling (UUS).

- call control packet.

- control Additions Service (CS).

- secure transfer small volumes of information.

Main signaling messages:

ESTABLISHMENT. Initialization call. Issued to request the establishment of a call. It is the most important message and more complex.

APPEAL PENDING. Confirmation of receipt of a message.

Institution indicating that the resources necessary for the establishment of the call are under reservation.

- ALERT. Alert the user is being asked (ringtone).

- LOGIN. The called user accepts the call.

- ACKNOWLEDGEMENT OF CONNECTION. Confirms the inclusion of the connection and is the completion of the call setup phase.

Main signaling messages:

- I

- NFORMATION. Contains additional information that may affect the operation of the service (taxation).

- STATE. Sets the state of the call, the user side or network side.

- DISCONNECT. Initiates release of the call.

- RELEASE. Confirmation of the release of the disconnect message.

- END OF RELEASE. Completion of the release phase. The resources reserved for the communication are released.

- The ISDN address identifies the ITA in its entirety.

- Subaddress identifies equipment of the ITA.

- Signaling protocol D in the band at the interface U / R (UNI) is transformed into its equivalent in-band interface R / R via the SS7 network.

OOB signaling is ISUP signaling.

ISDN PROVISIONAL CONCLUSION

- ISDN has enabled the integration of all telecommunications services that are accessible by a single dose (in fact 2: S0 and S2). It is joined in the standard "socket" that allows you to connect any convenient electrical device on the network EDF.

- A network data transmission independent conveying signaling (SS7) has been developed. This network can carry ISDN signaling but also that of PSTN, GSM ... This factorization can calmly see any technological change.

- ISDN reveals its technological limits now facing new multimedia teleservices video, Internet. We tried with limited success testing video transmission access n.64kb S2 / s (H.261 standard), but the transfer mode offered by ISDN type STM (Synchronous Transfer Mode) with a constant flow ( remember 8 bits every 125? s!).

- Current multimedia services are asynchronous rather variable rates, which is incompatible with ISDN. You need to have a new type of network that supports asynchronous transfer mode type ATM (Asynchronous Transfer Mode). Bandwidth should be as large (> Mb / s).

- ISDN BE must evolve to support these new types of teleservices and offer higher data rates.

- BE ISDN (N-ISDN) ISDN evolves naturally to LB (B-ISDN) capitalizing knowledge and existing infrastructure (SS7).

- BE ISDN ADSL is currently challenged by supporting new multimedia services by offering a higher BP (8 Mb / s) at a lower cost. The high cost of ISDN (BE) has always been a hindrance.

A DIGITAL NETWORK INTEGRATION SERVICES BROADBAND ISDN

NEW TELECOM SERVICES

New telecommunications services are multimedia-type mixing different data streams video, audio ... :

- VOD (Video on Demand VoD).

- Internet access.

They are mainly characterized by the following:

- Bandwidth hungry.

- Generate variable rates over time (data bursts, silence).

So we now Broadband services in competition with existing services Narrowband!

Based on the following characteristics:

- constant or variable.

- synchronization between the sending application and the receiving application.

- connection mode.

INADEQUACY CURRENT PROTOCOLS

Limiting the flow of current networks mainly due to the crossing time of the network mainly due to the processing time in the different nodes of the network and not because of the flow lines. A bond to 100 Mb / s with a transfer time of 10 ms corresponds to 106 bits being transmitted. Protocols (eg X.25) implemented to ensure a certain quality of service over unreliable media (copper or wireless) generate a large number of redundant operations from one layer to the other severely penalizing the flow effective: flow control on each link and at each level (X.25 LAP-B and PLP) Increased flow can result only relief intermediate treatments authorized the use of more intensive the optical fiber.

The relief protocols in the network is made possible by the quality of existing transmission media: BER of an optical fiber is less than 10-11, which is much better than using a 16-bit CRC !

The broadband involves:

- To carry over to the end members of the tasks of detecting errors produced: no control (CRC) on the data in the network. The network is transparent to the data.

- Reduce operations layers by performing the routing level 2. Level 3 functions are lowered to level 2.

- Make optimistic assumptions about the behavior of the network by not performing flow control between the nodes where the risk of increased congestion!

- Removing intermediate acknowledgments, these being achieved by the end members. Reduction of processing time.

- simplifying protocols leads to decrease the size of the headers and this contributes to improved performance.

The information contained in the headers should allow:

Simplified error checking which allows the detection of single errors in the header when routing, but no recovery is performed. Packets (cells) are lost erroneous.

Reporting the state of congestion to the end members. If it persists, packets (cells) will simply be eliminated.

ATM

- Was selected transfer mode ATM for Broadband.

- Known as ATM cell relay (Asynchronous Tranfer mode) uses a technique of rapid switching of fixed-sized cells.

- The MTA implements specific mechanisms to ensure isochronous transfers (emulation for voice, video ...).

- An adaptation layer to a class of service implementation to implement the service constraints (and QoS).

AND ISDN ATM

- Known as B-ISDN (B-ISDN), this type of network allows video on demand, use the map of multimedia mail, distribution of CD quality music.

- ISDN (LB-) implements ATM.

SERVICES FOR ATM

There are 4 types of services dedicated to ATM:

- For telephone service, all connections must be established before the transmission starts. This means that the network requires a connection-oriented service. The voice does not require very wide bandwidth. The voice is subject to changes in flow in the network, we will implement techniques to have an exchange CBR.

- Services comprising data are more flexible. They may be connected or not. They are not too sensitive to variations in transmission delays. The data can be used high or low Bandwidth.

There are 4 types of services dedicated to ATM:

- By digital video requires a large against Bandwidth and compression methods depend for success still transmit at a rate as constant as possible.

- Videoconferencing is a connection-oriented service. It is very sensitive to variations in the data transmission. Depending on the compression method used, this application can now transmit at a variable rate data transmission.

There are 4 classes of ATM services:

- Class A: RTC emulation, video: CBR.

- Class B: audio: VBR.

- Class C: data transfer mode.

- Class D: Connectionless Data transfer: emulation for LAN access (gateway to the Internet).

Found a layer for each class of adaptation to the application AAL (ATM Adaptation Layer).

ATM incorporates the principles of the ISO reference model but several changes are needed in the fact that it must take into account the transport of video image and voice.

The ATM model has 4 layers:

- Physical delivery of cells in the medium.

- ATM cell switching.

- AAL: adaptation layers above ATM.

- Application: Applying Broadband.

In addition to these four layers, the ATM model has three levels:

- The user plane: data transfer.

- The control plane: signaling.

- The management plan: monitoring (Operation And Maintenance, OAM): performance management, fault detection, system protection, information failures and performance, fault location. This is new in the world of telecommunications.

These three types of data using the same vehicle: the ATM cell (fixed packet size).

THE MODEL AND ISDN ATM

- The same modeling of the ITA for the B-ISDN for ISDN-BE: functional groups and interfaces.

- We also find the same types of topology ITA!

ISDN: FINAL CONCLUSION

- ISDN LB is the natural evolution of ISDN to withstand BE LB new services and offer higher data rates.

- ISDN LB enjoys the experience of ISDN BE capitalizing knowledge and existing infrastructure (SS7).

- ISDN LB is mainly used by operators in the network with SDH multiplex (motorways information!).

ISDN LB slow to come up to the individual:

- operators must take new cables up to the individual (Fo. ..) and this is unfortunately the most expensive!

- There are no consensus was to define a single access interface U / R in accordance with the concept of a single dose of ISDN BE, which spreads even more trouble.

ISDN LB is currently challenged by ADSL Broadband services tailored to flow below some Mb / s can be seen as a pre ATM technology (such as Frame Relay) ...