# Sewage sludge

#### Introduction

Sludge is the solid by-product of sewage treatment. It can contain excessive levels of organic, inorganic and xenobiotic compounds as well as pathogens. Due to the potentially disastrous effects its direct disposal can have on an ecosystem, it is often processed before it is released back into the environment and many regulations are set to govern what must be removed from the sludge and what may remain after the treatment. Sludge processing involves sludge stabilization, conditioning, and dewatering and the main purposes are to reduce the quantity of the organic solids, inorganic particulates, and eliminate disease causing bacteria.

Sludge stabilization is intended to convert as much of the organic materials into gases as possible through the use of either aerobic or anaerobic bacteria - often called sludge digestion. Often a strong base, such as lime, is then added to the sludge to raise the pH of the mixture to levels which inhibit the survival of micro-organisms, pathogenic or otherwise (Wether and Ogada, 1999). Heat treatment of the sludge may also be used which coagulates the solids, releases water, and sterilizes the sludge which effectively kills all the micro-organisms present in the sludge as well. The effect of moisture content on the sludge volume is also important - the more water that can be removed, the less of the sludge there is to be disposed. This is done by thickening and drying the sludge via presses, vacuum filters, or centrifugation techniques. The extent of the dewatering will depend on the final disposal mechanism; higher water content may be necessary with water disposal to ensure spreading and a water content of zero may be required for combustion or transport.

Below is a chart illustrating the amounts of various inorganic and organic compounds that are present in sewage sludge after treatment in wastewater plants servicing Los Angeles in 1981. The types of organic and inorganic compounds shown above are typically present in most sewage sludge found around the world.

#### Marine Disposal

The discharge of sewage sludge into oceans and lakes is of particular environmental concern as well. Near shore disposal is typically done through pipelines with the exit point being the coastal region of ocean or a lake. Deep-sea disposal is done by barges which carry and then release the sludge in a designated area large distances away coastal cities to reduce the potential impact on its residents. Since the transport of the environmental contaminants such as pathogenic organisms, trace metals, or xenobiotic compounds are typically associated with the movement of particulate material in sewage sludge, the method used for disposal will greatly influence the initial dilution and dispersion of the waste (NRC, 1984). When materials are disposed in the deep ocean, once the particulates settle, their movements are typically limited to very deep sites. In shallow waters, movement can easily occur across system boundaries due to bottom currents or turbidity currents (NRC, 1989). The surface currents can easily distribute the pollutants from the sewage sludge over great distances and often into estuaries, which can be very problematic due to their role as a breeding ground for numerous species. Fluxes of waste into groundwater can also occur and the recovery of the waste to prevent contamination of drinking water can be tedious and very costly. While some remediation and biodegradation of the waste materials via benthic metabolism is possible, the method of disposal, the organic materials and pollutants present in the sludge, and also the dynamics of the body of water will all have an effect on its success (Duedall et al, 1983).

Waste disposal into water systems will often change the dynamics of the natural communities present in the area. In open-ocean systems, the species under impact have large ranges and usually good dispersal capabilities relative to the area under impact. In coastal areas and in lake systems, the addition of the sewage sludge may have stronger effects. The stability of a community is often dependent on the diversity of the species and often when excess nutrient is added, some species may respond more effectively and displace others. In areas of sludge dumping, shifts have been seen in the structure of animal communities where pollution tolerant species dominate the population (Kennish, 1999). Especially in nutrient-limited lake systems, the addition of a nutrient can cause dramatic shifts in species numbers. Phosphorus, which is present in sewage sludge, is often the limiting nutrient in lakes and coastal areas for algal cell growth so often when excess phosphorus is added, large algal blooms can be observed. This increase in biomass can deplete the dissolved oxygen concentrations, especially near the lake floor, and kill off many of the bottom dwelling organisms which reduces diversity. Hypoxia can also occur in coastal sea waters where stratification hinders the oxygenation of the water near the ocean floor - when nutrients are added, the marine microorganisms increase their metabolism of the substrates which effectively reduces the concentrations of dissolved oxygen that reach the ocean floor (Boesch and Rabalias, 1991).

Although many toxic chemicals are removed in the sludge-forming process, many toxic chemicals will persist and will be discharged into the environment along with the sewage sludge. These toxic chemicals will often enter the marine food chain and can induce specific biological changes or result in bioaccumulation of the chemicals within the organism (Swanson et al, 2004). Of specific concern is the uptake and transfer of metals, xenobiotic compounds, and other organic contaminants which demonstrate carcinogenic or mutagenic properties. Some marine species will store metal contaminants in their tissues, skeletal material, or extracellular matrixes. If ingested, removal may take place via excretion of the production of particulate products such as feces or eggs - the last method of excretion being the most problematic because it may interfere with the proper development of the embryos (Swanson et al, 2004). Xenobiotic compounds tend to accumulate in the sediments where they may absorbed through metabolic processes of multi-cellular organisms. In both vertebrate and invertebrate systems, including mammals, fish, and crustaceans, biotransformations of PAHs and PCBs through cytochrome P450-mediated mixed function oxygenase reactions may actually produce potentially more toxic metabolites (NRC, 1984). Some metabolites of xenobiotic compounds have been shown to be carcinogenic and mutagenic. A study by Perkins et al (1982) showed that there is a higher rate of tumor incidence in fish populations around documented sewage dump sites around the US coast.

Due to the diverse metabolic abilities of benthic organisms in the marine environment, the natural biodegradation and assimilation of many of the materials is sewage sludge is possible; however, careful monitoring and analyses of the nutrients and contaminants present in the sludge and also the dispersal and degradation characteristics of the dispersal area is necessary to ensure protection of the environment. The first step in the disposal process that can be exploited to reduce the impact on the environment is the actual mechanism by which the sludge is disposed into the water. The two main techniques currently used are pipelines and surface transport vessels. Strategies such as releasing the sludge at a lower depth and releasing in an area where there is more mixing of the waters can ensure a greater dispersal area to minimize the overloading of natural microbial and biochemical processes which can result in severe alterations in the structure and function of benthic communities (NRC, 1984). Near shore disposal sites should be avoided because the nutrients and contaminants from urban run-off (storm water and surface water) are already present in the waters and the addition of even more nutrients via sewage sludge may wreak havoc on the ecosystem. An accurate account of the species of benthic and pelagic organisms in the disposal area is also necessary to determine the types of contaminants that can be assimilated effectively. Food chain interactions of the species would also be a key piece to document because while there may be not detrimental effects on the organism that directly injects the contaminant, especially in the case of PCBs and PAHs, the organisms may store the toxins in their system only to negatively affect organism that will then consume them (Boesch et al, 1991). Some contaminants also persist much longer in the environment than others, such as organochlorines from pesticides; the sludge-forming process should be improved to allow as little of these compounds into the environment as possible.

The New York Bight Apex was a shallow waters dump site for the metropolitan city of New York and a well documented example of the disastrous effects that marine disposal may have on an ecosystem if the characteristics of the sewage and the body of water are mismatched. The site contains the largest deposit of sewage sludge in all of the United States - 125 million cubic metres dumped over the span of 64 years (NRC, 1989). The New York Bight Apex dump site was of relatively small concern to the residents of the coastal cities until the early 20th century when the population and the sewage of the city of New York began to increase. With help from the Gulf Stream current, waste materials began to wash up on recreational beaches which resulted in unbearable odours from the decay and outbreaks of illnesses in humans who went swimming or consumed raw shellfish (Swanson et al, 2004). This led to intense public pressure to investigate the dump site and monitor its affects on the ecosystem and the waters surrounding New York.

Much of the sewage sludge, due to dispersion and ocean currents, settled in an area North East of the release site called the Christiaenson Basin. Chemical and biological analysis of the area showed decreased levels of oxygen concentration due to the decomposition of the organic materials and an increased concentration of xenobiotic compounds. The phytoplankton productivity of the waters in and around the dump site were measured to substantially exceed that in the waters further away (Kennish, 1999). During the summer of 1979, dissolved oxygen levels near the bottom of the basin were reduced to levels near zero due to the decomposition, and also the increased stratification of the water column due to a particularly warm winter and an intense algal bloom which led to even more organic input. This resulted in large die-offs and near elimination of various bottom dwelling organisms including the commercial surf clam and mobile epibenthic organisms (Boesch et al, 1991). The number of species in the benthic community was also reduced due to the excess growth of pollutant tolerant worms that were able to take advantage of the new environment. High levels of PCBs, PAHs, and pesticides were found in the sediment and in the benthic fishes near the sludge disposal site. High prevalence of fin rot disease, a bacterial infection that destroys the fins of fish, were found in samples of at least 22 species of fish collected in the 1970s (Mahoney et al, 1973). While bacteria are responsible for the degradation of the fins, the disease also results in skin haemorrhages and even blindness; it is possible toxic chemicals may be the root of the illness although this has not been formally established (Kennish, 1999). At the height of the pollution in the New York Apex, an outbreak of shell disease in deep sea red crabs and lobsters were reported by commercial fisherman working in regions near the dump site. While a direct causation link has not been made between sewage sludge and shell disease (as there were other factors impacting the ecosystem in the New York Harbour during that time), the disease has not been ruled out as at least a partial result of the sewage (Swanson et al, 2004).

Many countries around the world have now banned ocean and marine dumping as a disposal mechanism for sewage sludge due the detrimental environment impacts that result when it's done incorrectly. In Canada, however, ocean dumping is still an approved but tightly regulated practice. Environment Canada grants permits for marine disposal following a detailed assessment to ensure that the ecosystem and marine and human health are protected (Environment Canada, 2009). All dump sites are then subjected to continuous monitoring by the Ministry to ensure compliance with the conditions of the permit. Fines will be imposed if the individuals, the municipality, or the company are found in violation of the conditions. Marine disposal of sewage sludge, when done correctly under the appropriate conditions, can be a cost effective disposal alternative with relatively minimal effects on the environment compared to combustion or land disposal.