# Spine Vertebrae Project

1. Introduction

The human spine is comprised of a complicated repeating structure of vertebrae, discs and posterior joints between adjacent vertebrae involving many ligaments and the interaction of complicated bone geometries. Injuries and degenerative diseases of the spine can lead to an alteration in the load distribution in some or all of the functional spinal units (FSU). In turn, this can lead to chronic pain and instability.

The drive to carry out this project stems from the need to be able to determine disc and facet pressures of the spinal column accurately to indicate alterations in load distributions caused by injuries and degenerative diseases. In order for this to be obtained, it is suggested that an efficient way of doing so would be to create a specimen-specific model of the spine that can be analysed under different loading conditions using finite element (FE) software. As well as providing quantitative results, the software is capable of producing a visual model showing the regions, using colour codes, to indicate highs and lows. This allows comparison of load distributions to be assessed over time and between specimens easily and quickly.

The purpose of this project would be to validate the model of the spine with experimental results. Though the original plan was to carry this out on a human spine, it has been decided that due to ethical and cost constraints of obtaining a human spine, this can be achieved using a porcine spine instead, which if validated, can be adapted to a FE model of a human spine. A porcine spine is a good alternative due to its similarity in structural and material properties in some regions.

The wide scope of the project extends far beyond the particular aims of this investigation. However, the intention is to add experience in carrying out such an investigation which can then be developed to add further to the research that currently exists on the spine which can then be used in medical care in a variety of ways, from understanding the biomechanics of the spine and the effect of degenerative diseases to implants and surgical techniques.

2. Project Objectives

The main aims of the investigation are as follows:

- Construct a finite element (FE) model of multiple functional spinal units (FSU) in the lumber and also possibly the cervical region of the spine by:

- Taking a CT scan of a porcine spine.

- Extracting 3-D surfaces from the CT scan using medical imaging software.

- Constructing a mesh of hexahedral elements projected to the bone surfaces using TrueGrid software.

- Adding ligaments, discs and boundary conditions based on muscle attachment sites and loading values from literature.

- Analyse disc and facet pressures under a variety of natural loading conditions and correlate with experiments. Analyses of the FE model will be conducted using Abaqus finite element software. Experimentation to be carried out using Instron machine to load spine into axial compression, flexion/extension, axial torsion and lateral bending. The results of each can then be analysed and an evaluation of their correlation made.

Time permitting, additional aims of the project include:

- Analyse kinematics of spine compared with model under variety of loading conditions. Use of FE element software to find displacement values of the model. Use of transmitter and sensor devices such as ‘Flock of Birds' to measure the displacement of the spine under different loading conditions in the Instron machine. The results of each can then be analysed and an evaluation of their correlation made.

- Obtain CT scan of human spine and re-mesh to construct a FE model of the entire spine.

The following sections of this report describe the progress made towards completing these objectives. Firstly, the literature research that was carried out followed by the experimental and computational parts of the project. Critical evaluation and important recommendations will be given outlining the main barriers which have been encountered and possible solutions that can be undertaken in further work.

3. Literature Research

In order to carry out this investigation successfully a fair amount of literature research is required in order to understand the requirements and the different factors involved that need to be considered as well as to benefit from the research that currently exists in carrying out the investigation. Firstly, it is vital to have a good understanding of the anatomy involved, especially that a porcine spine is to be used rather than that of a human spine additional research is required as to the comparative anatomies. The modelling process involved in generating the mesh and subsequent finite element analysis need to be understood on a theoretical basis in order to carry out an accurate analysis and to have confidence in the results obtained. Specific problems that may arise with the particular application at hand may be found in the research and taken advantage of. Lastly, the experimental procedure to be undertaken needs to be realised and the different factors involved that may affect the accuracy of the experiment identified.

3.1 Anatomy of the spine

The spinal column is vital in providing support and allowing movement, as well as protecting the spinal cord which makes up part of the central nervous system from which nerves diverge out to other parts of the body. The spine allows flexibility for standing, sitting, stretching, bending and twisting. The many functions of the spine make it vulnerable to injury. This “can occur to the bones themselves, the ligaments that connect the bones, discs that separate each vertebral bone from one another, or muscles that give movement to our spinal skeleton.”[1] Any damage to the spinal column can have very severe consequences as a result. It is estimated that in the US, 80 percent of Americans will experience low back pain at least once in their lifetime.[2]

“Humans are born with 33 separate vertebrae. By adulthood, most have only 24, due to the fusion of the vertebrae in certain parts of the spine during normal development. The lumbar spine consists of 5 vertebrae called L1 through L5. Below the lumbar spine, nine vertebrae at the base of the spine grow together. Five form the triangular bone called the sacrum.”[3]

“The vertebral column has four curves in it. The anterior sacral convex curve curves toward the belly or pelvic region. The lumbar lordosis curves toward the back. The thoracic kyphosis curves toward the front of the chest, and the cervical lordosis curves toward the back of the neck.”[4]

Due to the difficulty of obtaining a human spine, a porcine spine was to be used instead. Porcine spines are frequently used as an alternative to human specimens.[5] Research was carried out on the comparative anatomy of the porcine and human spine. Dath et al., (2007) provides a database of morphometric data of the normal porcine lumbar vertebrae and highlights the difference between porcine and human specimens.

Aultman et al. (2005): “The porcine spine appears to be a useful surrogate to the human lumbar spine in both anatomical features (Oxland et al., 1991) and biomechanical behaviour (Yingling et al., 1999). Although no study has examined the orientation of the annular fibres in pig discs, our hand-protractor measurements suggest they are similar. The similarities of a pig neck and human lumbar spine should not be surprising since a large extensor moment is required to hold up the cantilevered head of a quadruped which results in huge compressive forces on the cervical vertebrae similar to the compressive forces on the human lumbar spine from supporting the weight of the upper body and head.”[6]

Menhausen (2002) gives a detailed qualitative comparison between the anatomy of the human and porcine spines:

SegmentHumanPig

Cervical77

Thoracic1214-15 (rarely 16-17)

Lumbar56-7

Sacral 54 (rarely 5)

Coccygeal 4 (3-5)20-23

As can be seen, there is considerable variability in the vertebrae for the various anatomic regions of the pig vertebral column, especially in the thoracic and lumber region. Since the lumbar region is of particular interest, here we shall present some aspects of the anatomy of the lumber region of the porcine spine in comparison to the human.

“The lumbar lordosis present in the lumbar vertebral column of man is absent in pigs. The combined thoracic and lumbar region of the vertebral column in pigs creates a concave ventral curve in the spinal column… The sequential vertebrae of the thoracic and lumbar regions then become progressively more dorsal in relationship to the posterior surface of the pig. The lumbar vertebrae are located more parallel with and closer to the posterior (dorsal) surface of the pigs back”[7]

“The lumbar region of the vertebral column of the pig consists of 6 - 7 lumbar vertebrae. The lumbar vertebral bodies are longer in relationship to those of cervical and thoracic vertebrae. The more caudad lumbar vertebral bodies progressively increase in width and also decrease in thickness. The lumbar spinous processes are broad, consistent in height (length), and have a cranial incline. The spinous process of the last lumbar vertebrae is much narrower, shorter (length), and is anticlinal (vertical)… The transverse processes increase in length from L1 to L5 and are also much shorter on the last lumbar vertebrae. The more caudad transverse processes are oriented slightly ventrad and also have a slight craniad incline. The more cranial lumbar vertebrae have a notch in the caudal edge of the transverse processes close to where the process attaches to the vertebral body. The notch in the transverse process gradually progresses into a defined foramen in transverse processes of lumbar vertebrae located at the caudal portion of the lumbar spine.”[8]

3.2 Mesh Generation

The selected application package to generate the mesh of the spine was TrueGrid (XYZ Scientific Applications, Inc.). This software has excellent capability of creating high quality meshes to be used for finite element simulation by generating multi-block structured meshes, each composed of solid hexahedral elements. It makes use of two representations of the mesh, one computational and one physical. The physical mesh lies in physical space in which the user can model something, and the computational mesh lies in an abstract space with only integer valued points. There is a correspondence between every node in the computational mesh and the corners of the blocks of the physical mesh. The physical mesh moves to fit the real object being modelled. In contrast, the computational mesh does not move. The computational mesh serves as a convenient way of identifying regions of the mesh which are to be the object of various functions. Objects in the physical space have three coordinates named x, y, and z. Objects in the computational space have three coordinates or indices named i, j, and k.[9]

TrueGrid is powerful in creating high quality meshes of structures with complicated geometry such as that of the spine. The geometry can be imported and multiple block structured parts can be created which means that a structure can be decomposed into more manageable parts. These parts can then be projected to the surfaces required and the block interfaces merged. The projection capability in TrueGrid eliminates the need for the user to specify the bulk of the details required by other mesh generators. It is precise and capable of dealing with complicated geometries, given a mesh that crudely approximates the surface is constructed. TrueGrid interactivity allows the user to navigate the session file that is generated during a session. The command lines are easily identifiable and changes can be made from the session file. Its parametric engine allows the user to make changes to a parameter and rerun the commands that form a mesh to get a new mesh reflecting the change. The meshes can then be refined to increase the quality of the meshes and a variety of smoothing techniques can be employed in distributing the nodes. The software has the capability to output complete input files for many simulation codes, therefore reducing the need to edit the files to match the requirements for the intended software.

Teo (2007) investigates the use of heterogeneous meshing in biomechanical modelling of the human spine with the aim of developing a patient-specific biomechanical model of the human spine for the purpose of surgical training and planning. He compares three models, one of which is composed merely of tetrahedral elements, the other of tetrahedral and hexahedral elements which were manually generated and optimised, and the last of purely hexahedral elements.

He states: “For automatic mesh generation, meshes comprising entirely of tetrahedral elements (or all-tetrahedral mesh) are frequently generated as opposed to a mesh comprising of purely hexahedral elements (or all-hexahedral mesh). This is because a physical domain, as in the case of geometrically complex anatomical structures, cannot always be decomposed into an assembly of hexahedral elements. It can however be easily represented as a collection of tetrahedral elements, as these elements are geometrically more versatile. Unfortunately, tetrahedral elements do not perform well because they are constant-strain elements. Higher order tetrahedral elements or a higher mesh density, resulting in higher computational requirements, is often required to achieve satisfactory accuracy. Hexahedral elements are highly favored and these elements are characterized by high robustness, better mesh quality and require a lower element count to fill a physical domain. Because of their better mesh quality, hexahedral elements have less likelihood to be inverted compared to tetrahedral elements (inversion results in failure of FE analysis). Furthermore, the reaction of hexahedral elements to body loads corresponds more precisely to loads under actual circumstances.”[10]

In summary, “…because of the inability to mathematically represent the contours of bio-structures, automatic mesh generation of all-hexahedral mesh models are not possible, although very much favored. Available automatic mesh generation software system provides only for the development of tetrahedral patient-specific FE models and there are limitations with mesh matching algorithms. Furthermore, a bio-structure such as the spine is made up of porous cancellous bone core enclosed in a dense cortical bone shell; cortical bone has a much higher stiffness than the cancellous bone inside. It is therefore important in biomechanical modelling to consider both meshing and material assignment.”[11]

3.3Finite Element Analysis

Finite element analysis (FEA) is a computer simulation technique used in engineering analysis. The Finite Element Method (FEM) is a numerical technique for solving the field equations of a body. In the context of structural analysis, which is the aim in this project, the method is used to calculate the displacements and stresses at any (or all) locations of a structure when loading is applied. The FEM is used widely in industry, for calculating the behaviour of such structures which are too complicated to be analysed by hand. In essence the method consists of dividing the structure up into small pieces, called elements, which are sufficiently small that it is possible to calculate their individual behaviour reasonable accurately by some fairly simple analysis. The complicated structure is thus modelled as an assembly of a large number of simple pieces.[12]

Simple functions are used to describe variations of the displacements, strains and stresses over the whole volume of the single element. Thus if the boundaries of the element are displaced by forces from its neighbours, then it is possible to calculate the displacements, strains and stresses at any location within the element. Specific points on the boundaries of the element, called nodes, are identified as the locations where the elements are connected to each other. The stiffness of the element is calculated as the relationship of any forces at these nodes to the resulting displacements at the nodes. Turning to the full structure, the assembly of the large number of elements is achieved by assembling all of the element stiffnesses. This results in a large matrix equation relating the forces and displacements for the whole structure. Solution of this equation for the applied loads then gives the displacement at all of the nodes. Finally, the strains and stresses anywhere in each element can be found from its nodal displacements.[13]

There are three main phases to finite element analysis. Pre-processing, in which the finite element model is defined and environmental factors are applied to it including boundary conditions, material properties and forces/moments. This is the most vital step on behalf of the user and where error is most likely to originate. The analysis solver then generates a solution of the model. This is followed by post-processing in which the results can be visualised and evaluated.

Finite element analysis (FEA) is gaining widespread use especially during the design process for spinal devices [14] as well as for the assessment of various pathologies and surgical treatments [15]. Therefore, it is important that the FEA is able to accurately reflect the reality. Several FE models of the spine have been created and can be seen in the literature. They differ in the spinal segment and structures being investigated, mesh density as well as material definitions for the various regions.

Wilcox (2007) mentions that only limited information is available on the influence of different input parameters on the model predictions. The role of these parameters which are categorised as relating to either the geometry of the model including the FE mesh and boundary conditions, or those relating to the material properties, are investigated. Wilcox states: “In the case of the material properties, a wide range of values has been used in spinal FE models due to the large spread in experimental data available in the literature. Although many FE studies have compared the model predictions with corresponding in vitro tests, there have been only limited studies on the sensitivity of the results to the material properties used (Ng and Teo, 2004; Kumaresan et al., 1999; Liebschner et al., 2003). In the case of geometric parameters, several authors have investigated the effects of changes in the model morphology on the mechanical response of the model. A number of studies have investigated the effect of cortical wall thickness (Kopperdahl et al., 1999; Liebschner et al., 2003), although these have assumed the cortical shell to be of constant thickness around the periphery of the vertebral body. Several convergence studies have also investigated the effect of mesh density and comparisons have been made with corresponding experimental data (Villarraga et al., 1999; Crawford et al., 2003a). The outcome of these studies have indicated that the model morphology plays a significant role in the characteristic response, however a direct comparison between generic and specimen-specific models does not appear to have been made.”[16] Wilcox uses specimen-specific and generic FE models of vertebral bodies to investigate these parameters on the model predictions by direct comparison with experimental data. This was carried out using the lumbar region of the porcine spine. It was found that the greatest level of agreement between the experimental results and the FE models was with the morphologically specific models including element-specific material properties indicating that highly specific models are necessary if the FE tool is to be used effectively for spinal research and clinical practice in terms of both morphology and bone quality.[17] This justifies the means used in the investigation.

Different material properties have been assigned in the various literatures some of which are simplifications and others which are more detailed and aimed at representing each material as accurately as possible depending on the investigation.

For a basic finite element model of the cervical spine, Kumaresan et al. (1999) uses the following material properties:[18]

Schmidt et al. (2006) also gathers data from the various literatures in what seems to be the most well researched and precise material properties of the spine [20]:

The software to be used to carry out the finite element analysis in this investigation is Abaqus FEA (SIMULIA, Dassault Systemes). Abaqus is a highly sophisticated, general purpose finite element program, designed primarily to model the behaviour of solids and structures under externally applied loading. It is used here as it is especially useful for this purpose as it has a sophisticated capability to model contact between solids.

3.4 Experimental procedures

Various different experiments have been carried out on the spine that can be found in the literature. The methods and tools vary depending on what is specifically being investigated. However, some of the techniques used have become common practice and are used systematically in the literature. The relevant methods are highlighted in the experimental examination part of this report (section 4). Several experiments involved applying compression and moments to the spine from which approximate values of the loading can be taken.

O. Lundin et al. (2000), gives values of the mean ultimate force at failure specifically on the lumbar region of the porcine spine of both adolescent and adult pigs. This value must not be approached as experimentation will be repeated on the same specimen under the different loading conditions. These values are 9.4 kN (SD 0.9 kN) and 25.3 kN (0.7 kN) for the adolescent and adult pig respectively.[21]