# The effect of ultrasonic pre-irradiation treatment

This study analyses the effect of ultrasonic pre-irradiation treatment upon aqueous enzymatic extraction of essential oil from lemongrass, Cymbopogon citratus by comparing different irradiation time (0min, 5min, 10min, 15min), extraction process time (4hr, 6hr, 8hr) and conventional extraction method (steam distillation and hydrodistillation). Pectinase Ultra SP-L, a commercial enzyme were used in the aqueous enzymatic extraction of lemongrass essential oil. The essential oils extracted were then analyzed for their chemical composition by Gas Chromatography with FID detector. Results showed ultrasonic pre-irradiation time at 15 minutes gave higher yield (0.008%) of essential oil (P<0.5), and the major component were geranial (23.92%) and neral (21.14%). However, irradiation at 5 min showed geraniol (54.45%) and nerol (11.17%) were the major components due to the reduction of aldehydes geranial and neral under the anaerobic condition of the enzymatic extraction process. Sample which have been irradiated with ultrasonic treatment gave the higher yield (0.014%) after 8 hour (P<0.0005) extraction process compare to control (0.012%). Extraction efficiency of essential oil from lemongrass was improved by the ultrasonic treatment, but it was found much lower (P<0.0005) than the amount obtained by steam distillation (0.081%) followed by hydrodistillation (0.050%). As a consequence, ultrasonic pre-irradiation step may improved the yield in aqueous enzymatic extraction of lemongrass essential oil, however have to undergo further analysis such as determination of the right enzymes type, enzyme concentration, pH, temperature and others in order to compete the conventional method.

## 1. Introduction

Hydrodistillation and steam distillation are the conventional methods for isolation of essential oils. These processes cost inexpensive but can induce thermal degradation, hydrolysis and water solubilization of some fragrance constituents [1]. Another inexpensive method that use low energy and temperature requirements is aqueous enzymatic oil extraction (AEOE). AEOE is an emerging technology in fats and oils industry but less is known of it’s application efficiency in essential oil production. In order to extract essential oil from lemongrass, Cymbopogon citratus by using this technique, the enzyme that will be use in the extraction have to function as cell wall degradation. This is because in lemongrass, the essential oil is confined within specific lignified cells in parachymal tissues in the leaves [2], and may be released when the leaf tissues are softened by the enzymes [3].

Luqua-Garcia and Castro [4] have described a novel technique in which ultrasound was used in combination with soxhlet extraction and found that ultrasound irradiation cut down the process time at least by half for extraction of the total fat from seeds of sunflower, rape and soybean. Beside that, Sharma and Gupta [5] have explore the advantages of ultrasonic pre-irradiation for extraction of oil by AEOA. They have found this step have increased the oil yield and reduce the time required to extract oil from almond and apricot seeds. It is likely that such an effect is due to destruction of subcellular structure (thus acting in synergy with enzymes in this respect).

In this work, the extraction of lemongrass, C. citratus essential oil by combination of ultrasonic pre-irradiation and AEOE is described. The chemical composition of major monoterpenes especially citral, a combination of aldehydes geranial and neral will be compared at different irradiation time (0min, 5min, 10min, 15min), extraction process time (4hr, 6hr, 8hr) and conventional extraction method (steam distillation and hydrodistillation).

## 2 Materials and methods

Lemongrass leaves were obtained from USIM Fertigation House. Pectinex Ultra SP-L were bought from Novo Nordisk Ferment Ltd. Switzerland. Pectinex Ultra SP-L is a commercial enzyme preparation of Aspergillus niger containing three enzyme activity: Xylanase (404 U/ml), pectinase (338 U/ml) and cellulose (134 U/ml). All other chemicals and solvents used were analytical grade.

2.1 Aqueous enzymatic extraction of essential oil

Lemongrass leaves were dried for one week under room temperature, cut into small pieces and grinded with WARING Blender. 50g of the samples were dissolved in 400 ml distilled water. The pH of the dissolved samples were measured and 1% w/w of enzymes were added. For ultrasonic pre-irradiation treatment, samples were immersed into 42 kHz bath (Branson ultrasonic cleansing bath unit model 1510 DTH) and sonicated for 5, 10 and 15 min (Figure 1).

Figure 1 : Experiment set up for ultrasonic pre-irradiation treatment.

Each samples were made triplicates. The control and ultrasonic pre-irradiated samples were incubated at 50°C with constant shaking at 80 rpm for specified period. After incubation ended, the samples were filtered and rinsed with distilled water three times. The aqueous phase were separated from the oil layer in separation funnel by liquid-liquid extraction. 5 ml hexane were added and the funnel were shake vigorously for 2 minutes. The aqueous layer were decanted, and the hexane layer which contain the essential oil were later decanted in a beaker. The separation funnel were rinsed with hexane three times. 10-20 g Sodium sulphate anhydrous were added and stirred until no visual bubbles observed in order to trap the moisture residual. The samples were filtered and hexane were removed by gently heating at 65°C in water bath. The essential oil recovered were then dried in the oven at 70°C for overnight. The essential oil were weighted (g) and diluted to 5 ml with isopropanol for gas chromatography analysis.

2.2 Steam distillation and hydrodistillation

Lemongrass leaves were dried for one week under room temperature, cut into small pieces and grinded with WARING blender. 400g of the samples were submitted to steam distillation for 4 hour and 200g of the samples were submitted for hydro-distillation for 2 hour. Each samples were made triplicates. The volatiles were collected until no oil drop out. The distillate went through the same process as AEOE separate the oil from aqueous layer by liquid-liquid extraction in separation funnel. The essential oil recovered were then dried in the oven at 70°C for overnight. The essential oil were weight (g) and diluted to 5 ml with isopropanol for gas chromatography analysis.

2.3 Gas Chromatography Condition

Gas chromatography analysis were performed using an Agilent A7890 Gas Chromatograph equipped with a FID detector and a HP-5 fused-silica column (30 m X 0.32 mm i.d., film thickness 0.25µm, Agilent). Oven temperature was 60°C for 2 min, them programmed heating from 60 to 150°C at a rate of 3°C/min and hold at 150°C for 2 min resulting in the complete elution of all peaks analyzed. Injector and detector temperatures were 320°C. The carrier gas, helium was adjusted to linear velocity of 25 ml/min. All samples were diluted in isopropanol. Standards calibration curves of oil constituents were performed and run under the same condition.

2.4 Statistical analysis

The results of extracted chemical compound (geranial, neral, geraniol, nerol, trans pinane, cis pinane, limonene, linalool, geranyl acetate, citronellol and myrcene) from the GC analysis were analyzed using SAS® statiscal software. ANOVA test were run using Generalised Linear Model (GLM) with Duncan Multiple Ranges Test.

## 3 Results and discussion

3.1 Comparison of different ultrasonic pre-irradiation time

Ultrasonic pre-irradiation time were set into three different time (5, 10, 15 min) with control (0 min). Chart 1.1 showed ultrasonic pre-irradiation time at 15 minutes gave higher yield (0.008%) of essential oil (P<0.5) with major component were geranial (23.92%) and neral (21.14%). This was followed by 10 min (0.006%), 5 min (0.005%) and 0 min (0.004%). The longer ultrasonic pre-irradiation time increased the amount of essential oil yield, due to more plant cell wall disruption happened and released the oils out [5]. However, irradiation at 5 min showed geraniol (54.45%) and nerol (11.17%) were the major components due to the reduction of aldehydes geranial and neral under the anaerobic condition of the enzymatic extraction process [3] (Chart 2.1).

3.2 Comparison of different aqueous enzymatic extraction process time

Significant difference (P<0.0005) between extraction time were found in treated sample. Chart 1.2 have showed sample which have been irradiated with ultrasonic treatment gave the higher yield (0.014%) after 8 hour extraction process compare to control (0.012%) followed by 6 hour (0.008%) of extraction. Increases of oil yield in treated samples were related to the.

## (1)

## (2)

## (3)

Chart 1 : Comparison of weight and percent yield of lemongrass, Cymbopogon citratus essential oil at (1) different ultrasonic pre-irradiation time; (2) different extraction time and (3) different extraction method.

## (1)

## (2)

## (3)

Chart 2 : Analyzed chemical composition percentage in essential oil of lemongrass, Cymbopogon citratus by comparing (1) different ultrasonic pre-irradiation time; (2) different extraction time and (3) different extraction method.

enhanced extraction efficiency, because as extraction time becomes longer, the plant tissue become softening by the enzymes action and the essential oil which is confined within specific lignified cells in parenchymal tissues in the leaves were released [3].

Control sample gave no significant difference (Chart 2.2) between extraction time but major components i.e. geranial, neral, geraniol and nerol were significantly higher (P<0.0005) than treatment sample. Other than that, geranyl acetate were found much higher (34.12-46.32%; P<0.0005) in treatment sample compare to control

3.3 Comparison of AEOE with conventional steam distillation and hydro-distillation

Chart 1.3 showed steam distillation (SD) gave the highest yield (0.081%; P<0.0005) followed by hydrodistillation (HD) (0.050%). Enzymatic extraction either control (EC) and treated sample (EU) were the lowest and far left behind in producing essential oil. However the chemical composition in the essential oil extracted by enzymes gave a different combination compare to conventional method SD and HD. In control enzymatic extraction (EC), produced geranyl acetate as major components (39.6%) beside geranial (25.12%) and neral (20.75%), while in enzymatic extraction treated with ultrasonic pre-irradiation (EU) geraniol were the major components (39.9%) (Chart 2.3). In conventional methods, SD and HD still have geranial and neral as their major components (SD: 50.3% and 40.3%; HD: 55.4% and 36.0%). This difference combination of chemical compound were related to the principle of the extraction method. Enzymatic extraction provide an anaerobic condition which help the reduction of aldehydes geranial and neral to geraniol and nerol. As ultrasonic pre-irradiation treatment were added, it increased the extraction efficiency of geranyl acetate with help of enzymes soften the plant tissues.

## 4 Conclusion

From this finding, enzymatic extraction have a good potential to be used as a method to extract product of interest in lemongrass as citral (geranial and neral) can be reduce to geraniol and nerol. Geraniol and nerol have different smell from citral and have commercial value in cosmetics and perfume industry. Ultrasonic pre-irradiation step may improved the yield in aqueous enzymatic extraction of lemongrass essential oil, however have to undergo further analysis such as determination of the right enzymes type, enzyme concentration, pH, temperature and others in order to compete the conventional method.

## 5 Acknowledgement

We would like to thank Mr. Herman, S. from USIM Fertigation House for growing the lemongrass and Ms. Rohaya, Y. for helping prepare the samples. This work was fully support by USIM’s Faculty of Science and Technology grant for postgraduate student.