# characterization of normal and pathological breast tissue Using 1d ultrasound

Abstract – The present paper reports to investigate the effectiveness of one dimensional ultrasound in order to differentiate between normal and pathological breast tissue by analyzing the frequency dependence ultrasound attenuation, (FDUA) properties. 40 sample mice breast tissue was used in this study and the measurement were performed by using insertion loss method with transmission mode. From the result, FDUA is able to differentiate the normal and pathological tissue. It shows that, pathological tissue which contain high number of cell and collagen fibre will attenuates more ultrasound wave compare to the normal tissue.

Keywords: Normal and pathological breast tissue, 1D ultrasound , FDUA,

## Introduction

The epidemiological impact of breast cancer is reflected in the fact that it is the most common cancer in women. The breast cancer happen when the abnormal cell or cancerous cell are found in the breast. This cell will invade and spread surrounding tissue to other organ of the body and will affect its normal function. Cancerous cell are usually grow more rapidly and frequently life threatening. More cases were discovered and the rate was gradually rise during the past of 20 years. However, there is no reduction in the mortality rate from breast cancer, although there are options on improved treatments. The effective ways to reduce the breast cancer mortality is to detect the diseases in early stage. In the world of medical diagnostic, breast cancer of early detection has revolutionized as new research and studies unfold. Currently, the primary test used in the diagnosis of breast cancer is mammography. However, its usage is unsafe due to x-ray radiation. Hence, safer alternative method to diagnose breast cancer in earlier stages is needed. In this study, ultrasound is proposed for the breast cancer detection due to its safety and wide availability.

Ultrasound is widely used in health care for non-invasive diagnostics. The frequency ultrasounds used for medical purpose are in the range 1-20 MHz. The propagating of a wave in given medium can be generated by analyzing the transmitted or reflected signals. In medical diagnostics for example, ultrasound can be replace hazardous x-rays in many instances. It is useful for visualizing the fetus, measurement of the cornea, tissue characterization, skin and breast cancer detection and so on. For the detection breast cancer, ultrasound will transmit high-frequency sound waves through the breast which cannot hear by the human ear (above 20 kHz). The sound waves bounce off surfaces in the breast (tissue, air, fluid) and these "echoes" are recorded and transformed into video or photographic images. Ultrasound has many advantages compared to the x-ray mammography. For example, ultrasound are safer compare to the mammogram because ultrasound use a mechanical waves which use very low power and have short exposition time. Mammography use x-ray which have the negative effect for a patient. Ultrasound also can detect either the breast are malignant mass or a benign cist while mammography cannot do that. By using ultrasound, patient will not feel pain anymore. It also can scan the whole breast and detect the cancer either the patient have a denser breast or not.

Many types of biological tissue can be characterized by using ultrasonic parameter such as ultrasound velocity, FDUA and backscattered properties. Previous study shows that the FDUA has a very high potential to characterize the biological tissue [1]-[4]. When the sound propagate in tissue, its amplitude and intensity are gradually decreased due to the interaction between the sound waves and the medium. When ultrasound wave passing through tissue, it will loses its initial energy due to attenuation. Attenuation is an energy loss when the ultrasound wave travel through a medium as wave is converted to the heat when it reach and propagate in tissue. The most factors that contribute the attenuation of ultrasound in tissue is absorption due to the mechanical energy losses and the mechanical energy conversion to heat. The higher frequency the sound beam, the more it is attenuated. Hence, this study will investigate the effectiveness of 1D ultrasound to differentiate between normal and pathological breast tissue by analyzing the FDUA properties.

## Materials and Method

## 2.1 Mice Breast Model

In Biomedical research environment, the most widely used the animal models are mice. There are very common experimental animals in biology and psychology primarily because the mice are mammals that share a high percentage which is about 95% of their genes of homology with human as well as they are easier to handle and manipulate. Hence, the mice are an effective and efficient model for human diseases. In research environment, there is important to clearly understand the history and the origin of the mice strain that will be use to develop the successful research. The strain of inbred mice used nowadays in biomedical research can be founded at Jackson Laboratory .

For this study, two types of mice strain were used which is transgenic mice strain (FVB/N-Tg(MMTVPyVT)634Mul) and their control strain (FVB/N). For transgenic mice, the mating system was happen when noncarrier female were crossed to hemizygote male. The mice which carrying the (MMTV-PyVT) transgene are viable but it show loss of lactational ability same as transgene expression [10]. The tumor that we consider under this study is mammary adenocarcinoma. Mammary adenocarcinoma is a mammary tumors which appear in males and females mice. Female carries develop palpable mammary tumor start from five week of their age while for male start from 83 days of their age [10]. These tumor increased metastatic potential and arise in virgin and breeder mice. This type of tumor produce multifocal, highly fibrotic, and also involve the entire mammary gland. Transgene expression is detected at high levels in male and female mammary glands while the lower levels are detected in salivary gland, seminal vesicles, ovaries, and lungs.

## 2.2 Animal Tissue Preparation

The experiment was started with the preparation of animals tissue. The anesthetic drug was given to the mice intravenously via the mouse tail. After a few second, the fur around the breast mice area was shaved. Surgery procedure was continue by harvesting normal and pathological mammary tissue from the mice during their sleeping time. The physical appearance of mammary tissue was observed first before cutting down the tissue to a cylindrical shape with around 1mm thickness [1]. Then, the mice were killed by using drug overdose method.

## Ultrasonic Analysis

The experiment was set up by using one dimensional ultrasound signal. The ultrasound pulse generator was used to produces the ultrasound signal with frequency 10MHz with amplitude of 200 V. The measurement were done by using insertion loss method where the attenuation ultrasound propagate through oil and tissue is deducted by the attenuation ultrasound propagate through oil without tissue. This method can be measured using two mode which is through transmission mode and pulse echo mode [4]. Under this study, the transmission mode were be selected rather than pulse echo mode. The approach to measure the FDUA using this mode gives some advantages which can give an accurate data due to less noise produce[1]-[3]. Two separating transducer were use as transmitter and receiver where there are perpendicular to each other with some distance. In this study, 40 sample from each normal and pathological breast tissue of mice will be used. The sample tissue was immersed in oil which be located between the ultrasound transmitter and receiver which shown at Fig.1. The distance between the ultrasound transmitter and receiver was setting constant at 5mm. The ultrasound transmitter will be transmitting the ultrasound signal directly to the sample breast tissue and the signal will be captured by using ultrasound receiver. For each sample tissue, the data was collected for 5 times with difference tissue position. The experiment was repeated with the same technique using all sample tissue that has been stated early. The measurement also have been taken when the ultrasound propagates through the oil without tissue.

By using MATLAB software, the signal which recorded in time domain as shown in Fig.4 will be converted to frequency domain using FFT function for analysis. The absolute value of the FFT contain the information at a given frequency and the square of the absolute value is considered as the power spectrum of the signal. The low pass filter is also applied to remove noise in high frequency. The power spectrum at 10 MHz for each data were be analyzed to investigate the frequency attenuation. The statistical analysis of ultrasound parameter also will be done to measure the average, variance, standard deviation as well as the confident interval.

Fig. 1: Experiment set-up

## 3.0 Result And Discussion

## 3.1 Physical Appearance Of Tissue

Fig. 2: Pathological Mice Breast Tissue After Surgical Process.

Fig.3: Normal Mice Breast Tissue After Surgical Process

## 3.2 Result Analysis

Fig.4: Output Signal From Oscilloscope

TABLE 1

data analysis for normal and pathological mice breast tissue

Data analysis

Result

Mean oil

-26.501 db

Mean Pathological

-26.674dB

Mean normal

-28.044 dB

Attenuation Coefficient for pathological tissue

13.44 dB/mm/MHz

Attenuation coefficient for normal tissue

5.73 dB/mm/MHz

Fig.5: Mean value for Attenuation Coefficient for Normal and Cancerous Breast Tissue.

Table 1 shows the result of data analysis for normal and pathological mice breast tissue using statistically while Fig. 5 shows the plotted graph of mean attenuation coefficient value based on the data result from table 1 . The graph shows that pathological tissue attenuate more ultrasound compared to the normal tissue. The high attenuation value for pathological tissue is due to the presence of inhomogeneous of internal tissue and contain high number of cell as well as collagen fibre. Based on the previous study, the attenuation coefficient is lower for tissue with a large predominance of cells and its increase with collagen fibre content [1].

## 4.0 Conclusion

This study have been done to investigate the effectiveness of one dimensional ultrasound in order to differentiate between normal and pathological breast tissue by analyzing the FDUA properties. About 40 sample from normal and pathological mice breast tissue have been used to investigate the effectiveness of this parameter. Based on the result shows, the pathological tissue which contain high number of cell and collagen fibre will strongly attenuate the ultrasound wave compare to the normal tissue.