# jointed flexible object

### Background of the research

Inverse kinematics is the process of determining the parameters of a jointed flexible object in order to achieve a desired pose. Inverse kinematics is a tool utilized frequently by 3D artists. It is often easier for an artist to express the desired form rather than manipulate joint angles directly.

Inverse kinematics is a type of motion planning and related to game programming and animation where animators want to animate individual joints but it is difficult. For this problem, the animator to model the virtual joints and the computer automatically generates the required limb positions by using inverse kinematics.

Inverse kinematics as maximization of an objective function describes how desirable the pose is. Poses those are "similar" to the training data, using some automatic measure of similarity. Even if the set of training poses is very large, to optimize the objective function in real-time. It can generate well with small data. The similar measurement should be done automatically.

To represent this objective function over poses as a Probability Distribution Function (PDF) that describes the "likelihood" function over poses.

In order to meet the requirements of real-time IK, we represent the PDF over poses using a novel model called as a Scaled Gaussian Process Latent Variable Model (SGPLVM).All parameters of the SGPLVM are automatically from the training data, the SGPLVM works well with little data sets, and we show how the objective function can be optimized for new poses in real-time IK applications.

### The main idea of proposed algorithm

The Scaled Gaussian Process Latent Variable Model(SGPLVM) is a general technique for learning PDFs.Given a set of data points {yi}, we model the likelihood of these points with a scaled GP as above,in which the corresponding values {xi}(model parameters) are initially unknown �

### Results of the algorithm

with other kernels, or selecting kernels automatically based on the data set. Additionally, the current optimization algorithm employs some heuristics for convenience and speed; it would be desirable to have a more principled and efficient method for optimization. We find that the annealing heuristic for real-time synthesis requires some tuning, and it would be desirable to find a better procedure for real-time optimization

### Strength and limitation

### The main limitation of our style-based IK system is that

_ It requires suitable training data to be available; if the training data does not match the desired poses well, then more constraints will be needed.

_ The system does not explicitly model dynamics, or constraints from the original motion capture. Unfortunately, most poses that satisfy constraints The basic IK problem of finding the character pose is almost always underdetermined, meaning that many poses satisfy the constraints. This is the case even with motion capture processing where constraints frequently disappear due to occlusion. will appear unnatural.

### Strength

Even with a generic training data set (such as walking or calibration poses), the style-based IK produces much more natural poses than existing approaches. style-based IK can be used effectively for any problem where it is necessary to restrict the space of valid poses, including problems in computer vision as well as animation. For example, the SGPLVM could be used as a replacement for PCA and for RBFs in example-based animation methods.