# The Wi-Fi technology

Introduction

Amid the general tech collapse, theres one rising star: Wi-Fi, wireless networking. Its sales are going through the roof and its costs have plummeted. Why? Because where computers are useful, networks are often useful, too.

The only problem with traditional networks is their wires: You have to run lots of Ethernet wires in brand-new buildings (expensive), or retrofit existing buildings (very expensive). The solution is wireless networking and Wi-Fi-802.11b; to use its official name---- is far and away the most popular wireless solution today.

Here are some of the main benefits of Wi-Fi:

- Inexpensive  You can create a wireless network between your home computers for less than $200.

- Useful  You can remain connected to internet, other computers, and printers anywhere within the Wi-Fi broadcasting area.

- Scalable- Wi-Fi can service anything from two home computers to the whole university campus. Wi-Fi can either extend an existing wire network, or build a new network from scratch.

- Wise  Those in the know are using Wi-Fi, shouldnt you? Microsoft uses Wi-Fi to connect its entire Seattle campus.

802.11b is an intermediate - range wireless networking standard that runs at speeds comparable to standard Ethernet. The 802.11b specification includes a Medium-Access Control layer and a Physical layer using Direct Sequence Spread Spectrum technology.

The most immediate, obvious, and important application for 802.11b is wireless networking. If you've ever had to drill through walls to install a network, you'll appreciate that it's a lot easier and less expensive to use 802.11b wireless connectivity than to run wires, knock down walls, and do all that messy stuff. Because 802.1lb runs at speeds comparable to 10BASE-T Ethernet, there's really no performance trade-off for this convenience. In addition, 802.11b connects to laptops that are in the yard, on the roof, or beside the pool, not just fixed cubicle workstations. Finally, 802.1lb is an ideal technology for implementing networking in places such as coffee shops and hotel lobbies.

802.1lb networks have been installed in major corporate campuses, offices of all sizes, universities and schools, and in homes. In many cases, there's a kind of viral adoption in which 802.1lb networks are grafted onto existing corporate LANs on an ad hoc basis.

To set up an 802.11b, one needs an Access Point (AP) such as Apple's AirPort or Cisco's Aironet. The Access Point can connect to existing LAN resources, such as a switch or router. It then serves as a wireless router potentially allowing access to any computer equipped with an 802.11b card that is' within range.

Because even under ideal conditions the 802.11b range is limited to 300 feet, most extensive 802.11b networks require multiple Access Points, which can be spaced out so that all likely areas have coverage. Rooftop antennas and amplifying technology can also increase range.

It has been said that 802.1lb has set the cause of network security back at least 10 years. To understand why, consider that any mobile computer equipped with an 802.11b PCMIA card can potentially connect through an Access Point to internal network resources. This means you could connect to an unprotected corporate network from the street in front of the building.

Proper security precautions include using wireless encryption (WEP), even though this slows 802.1lb transmission rates and WEP security, alas, is not difficult to break. In addition, internal network resources should be protected from Access Points with a firewall. Users should only be able to obtain access through the firewall following authentication.

One of the most enticing aspects of 802.11b is its enabling of anytime, anywhere networking. (Whether you really want to work while you're poolside is another question.) In this spirit, Starbucks has announced that it will deploy 802.1lb in about 70% of its 4,000 North American locations. Anyone with an 802.1lb card in his or her laptop will be able to go into Starbucks for a latte and surf the Web.

Another example of a mobile application using 802.1 lb is a guest check-in application being launched by the Venetian Hotel in Las Vegas.

Hotel clerks will meet guests at building entrances, confirm their reservations via an 802.1 lb connection to a network server, and hand them keys on the spot. The goal is to eliminate check-in lines.

This particular application will use handheld devices that run the Palm OS and are strapped to the hotel clerks wrists. The handheld device includes a magnetic reader for credit cards, and the clerks will also carry an encoder for the room-key cards. Because of the huge room turnover at the Venetian, real time connectivity to the central server is required to be sure that room assignments are current.

Wi-Fi Concept

Moving data through a wireless network involves three separate elements: the radio signals, the data format, and the network structure. Each of these elements is independent of the other two, so its necessary to define all three when you invent a new network. In terms of the familiar OSI (Open Systems Interconnection) reference model, the radio signal operates at the Physical layer, and the data format controls several of the higher layers. The network structure includes the interface adapters and base stations that send and receive the radio signals.

In a wireless network, the network adapters in each computer convert digital data to radio signals, which they transmit to other devices on the network, and they convert incoming radio signals from other network elements back to digital data. The IEEE (Institute of Electrical and Electronics Engineers) has produced a set of standards and specifications for wireless networks under the title IEEE 802.11 that defines the format and structure of those signals.

Radio Signals

802.11b networks operate in a special band of radio frequencies around 2.4 GHz that have been reserved in most parts of the world for unlicensed point-to-point spread-spectrum radio services.

The unlicensed part means that anybody using equipment that complies with the technical requirements can send and receive radio signals on these frequencies, without the need for a radio station license. Unlike most radio services, require licenses that grant exclusive use of a frequency to a single user or group of users, and which restrict the use of that frequency to a specific type of service, an unlicensed service is a free-for-all, where everybody has an equal claim on the same piece of the spectrum. In theory, the technology of spread-spectrum radio makes it possible to coexist with other users (up to a point) without significant interference.

A point-to-point radio service operates a communication channel that carries information from a transmitter to a single receiver. The opposite of point-to-point is a broadcast service (such as a radio or television station) that sends the same signal to many receivers at the same time.

Spread spectrum is a family of methods for transmitting a single radio signal using a relatively wide segment of the radio spectrum. Wireless Ethernet networks use two different spread-spectrum radio transmission systems, called FHSS (frequency-hopping spread spectrum) and DSSS (direct-sequence spread spectrum). Some older 802.11 networks use the slower FHSS system, but the current generation of 802.11b and 802.11a wireless Ethernet networks uses DSSS.

Spread-spectrum radio offers some important advantages over other types of radio signals that use a single narrow channel. Spread spectrum is extremely efficient, so the radio transmitters can operate with very low power. Because they operate on a relatively wide band of frequencies, they are less sensitive to interference from other radio signals and electrical noise, which means that the signals are often able to get through in environments where a conventional narrow-band signal would be impossible to receive and understand, and because a frequency- hopping spread-spectrum signal shifts among multiple channels, it can be extremely difficult for an unauthorized listener to intercept and decode the contents of a signal.

Spread-spectrum technology has an interesting history. It was invented by the actress Hedy Lamarr and the American avant-garde composer George Antheil as a Secret Communication System for directing radio-controlled torpedoes that would not be subject to enemy jamming. Before she came to Hollywood, Lamarr had been married to an arms merchant in Austria, where she learned about the problems of torpedo guidance at dinner parties with her husbands customers. Years later, during World War II, she came up with the concept of changing radio frequencies to cut through interference.

Frequency-Hopping Spread Spectrum (FHSS)

As the name suggests, FHSS technology divides a radio signal into small segments and hops from one frequency to another many times per second as it transmits those segments. The transmitter and the receiver establish a synchronized hopping pattern that sets the sequence order in which they will use different sub channels.

FHSS systems overcome interference from other users by using a narrow carrier signal that changes frequency many times every second. Additional transmitter and receiver pairs can use different hopping patterns on the same set of sub channels at the same time. At any given point in time, each transmission is probably using a different subchannel, so theres no interference between signals. When a conflict does occur, the system resends the same packet until the receiver gets a clean copy and sends a confirmation back to the transmitting station.

For wireless data services, the unlicensed 2.4 GHz band is split into 75 sub-channels, each of them 1 MHz wide. Because each frequency hop adds overhead to the data stream, FHSS transmissions are relatively slow.

Direct-Sequence Spread Spectrum (DSSS)

DSSS technology uses a method called an 11-chip Barker sequence to spread the radio signal through a single 22 MHzwide channel without changing frequencies. Each DSSS link uses just one channel, without any hopping between frequencies.

A DSSS transmitter breaks each bit in the original data stream into a series of redundant bit patterns called chips and transmits them to a receiver that reassembles the chips back into a data stream that is identical to the original. Because most interference is likely to occupy a narrower bandwidth than a DSSS signal, and because each bit is divided into several chips, the receiver can usually identify noise and reject it before it decodes the signal.

Like other networking protocols, a DSSS wireless link exchanges handshaking messages within each data packet to confirm that the receiver can understand each packet. The standard data transmission rate in an 802.11b DSSS network is 11 Mbps, but when the signal quality wont support that speed, the transmitter and receiver use a process called dynamic rate shifting to drop the speed down to 5.5 Mbps. The speed might drop because theres a source of electrical noise near the receiver or because the transmitter and receiver are too far apart to support full-speed operation. If 5.5 Mbps is still too fast for the link to handle, it drops again, down to 2 Mbps, or even 1 Mbps.

Moving Data Around

So now we have a bunch of radio transmitters and receivers that all operate on the same frequencies and all use the same kind of modulation (modulation is the method a radio uses to add some kind of content, such as voice or digital data, to a radio wave). The next step is to send some network data through those radios.

Bits and Bytes

The processing unit of a computer can recognize only two information states: either a signal is present at the input to the processor, or there is no signal there. These two conditions are usually described as 1 and 0, or on and off, or mark and space. Each instance of a 1 or a 0 is a bit.

Individual bits are not particularly useful, but when you string eight of them together (into a byte), you can have 256 different combinations. Thats enough to assign different sequences to all the letters in the alphabet (both uppercase and lowercase), the ten digits from 0 to 9, spaces between words, and other symbols, such as punctuation marks and some letters used in foreign alphabets. A modern computer recognizes and processes several eight-bit bytes at the same time. When processing is complete, the computer uses the same bit code at its output. The output might be connected to a printer, a video display, or a data communications channel. Or it might be something else entirely, such as a series of flashing lights.

The inputs and outputs that were concerned about here are the ones that form a communications circuit. Like the computer processor, a data channel can recognize only one bit at a time. Either theres a signal on the line or there isnt.

Over short distances, its possible to send the data through a cable that carries eight (or some multiple of eight) signals in parallel through separate wires. Obviously, a parallel connection can be eight times faster than sending one bit through a single wire, but those eight wires cost eight times as much as a single wire. When youre trying to send the data over a long distance, that additional cost can be prohibitive. And when youre using existing circuits, such as telephone lines, you dont have any choice; you must find a way to send all eight bits through the same wire (or other media).

The solution is to transmit one bit at a time, with some additional bits and pauses that identify the beginning of each new byte. This is a serial data communications channel, because youre sending bits one after another. At this stage, it doesnt matter what medium you use to transmit those bits  it could be electrical impulses on a wire, or two different audio tones, or a series of flashing lights, or even a lot of notes attached to the legs of carrier pigeons but you must have a method for converting the output of the computer to the signals used by the transmission medium, and converting it back again at the other end.

Error Checking

In a perfect transmission circuit, the signal that goes in at one end will be absolutely identical to the one that comes out at the other end. But in the real world, theres almost always some kind of noise that can interfere with the original pure signal. Noise is defined as anything that is added to the original signal; it can be caused by a lightning strike, interference from another communications channel, or dirt on an electrical contact someplace in the circuit (or in the case of those carrier pigeons, an attack by a marauding hawk). Whatever the source, noise in the channel can interrupt the flow of data. In a modern communications system, those bits are pouring through the circuit extremely quickly  millions of them every second so even a noise hit for a fraction of a second can obliterate enough bits to turn your data into digital gibberish.

Therefore, you must include a process called error checking in your data stream. Error checking is accomplished by adding some kind of standard information called a checksum to each byte; if the receiving device discovers that the checksum is not what it expected, it instructs the transmitter to send the same byte again.

Handshaking

Of course, the computer that originates a message or a stream of data cant just jump online and start sending bytes. First it has to warn the device at the other end that it is ready to send and make sure the intended recipient is ready to accept data. To accomplish this, a series of handshaking requests and answers must surround the actual data.

Wi-Fi Architecture Layers

The 802.11b standard specifies two important parts, or layers: the Medium Access Control (MAC) and Physical (PHY). The MAC layer is a set of protocols that are responsible for maintaining order in the use of a shared medium. For example, data encryption is handled in the MAC.

The Physical layer handles transmission between nodes. In other words, it is primarily concerned with hardware.

These layers fit within the generalized OSI - Open System Interconnection - reference model. The OSI model is a way of describing how different applications and protocols interact on network-aware devices.

Physical Layer

The Physical layer handles transmission between nodes. In other words, it is primarily concerned with hardware.

In an 802.11 network, the radio transmitter adds a 144-bit preamble to each packet, including 128 bits that the receiver uses to synchronize the receiver with the transmitter and a 16-bit start-of-frame field. This is followed by a 48-bit header that contains information about the data transfer speed, the length of the data contained in the packet, and an error-checking sequence. This header is called the PHY preamble because it controls the Physical layer of the communications link.

Because the header specifies the speed of the data that follows it, the preamble and the header are always transmitted at 1 Mbps. Therefore, even if a network link is operating at the full 11 Mbps, the effective data transfer speed is considerably slower. In practice, the best you can expect is about 85 percent of the nominal speed. And, of course, the other types of overhead in the data packets reduce the actual speed even more.

That 144-bit preamble is a holdover from the older and slower DSSS systems, and it has stayed in the specification to ensure that 802.11b devices will still be compatible with the older standards, but it really doesnt accomplish anything useful. So theres an optional alternative that uses a shorter, 72-bit preamble. In a short preamble, the synchronization field has 56 bits combined with the same 16- bit start-of-frame field used in long preambles. The 72-bit preamble is not compatible with old 802.11 hardware, but that doesnt matter as long as all the nodes in a network can recognize the short preamble format. In all other respects, a short preamble works just as well as a long one.

It takes the network a maximum of 192 milliseconds to handle a long preamble, compared to 96 milliseconds for a short preamble. In other words, the short preamble cuts the overhead on each packet in half. This makes a significant difference to the actual data throughput, especially for things like streaming audio and video and voice-over-Internet services.

MAC Layer

The MAC layer controls the traffic that moves through the Wireless network- vents data collisions and conflicts by using a set of rules called Carrier Sense Multiple Access with Collision Avoidance (CSMA/CA), and it supports the security functions specified in the 802.11b standard. When the network includes more than one access point, the MAC layer associates each network client with the access point that provides the best signal quality.

When more than one node in the network tries to transmit data at the same time, CSMA/CA instructs all but one of the conflicting nodes to back off and try again later, and it allows the surviving node to send its packet. CSMA/CA works like this: when a network node is ready to send a packet, it listens for other signals first. If it doesnt hear anything, it waits for a random (but short) period of time and then listens again. If it still doesnt sense a signal, it transmits a packet. The device that receives the packet evaluates it, and if its intact, the receiving mode returns an acknowledgement. But if the sending node does not receive the acknowledgement, it assumes that there has been a collision with another packet, so it waits for another random interval and then tries again.

CSMA/CA also has an optional feature that sets an access point (the bridge between the wireless LAN and the backbone network) as a point coordinator that can grant priority to a network node that is trying to send time-critical data types, such as voice or streaming media.

The MAC layer can support two kinds of authentication to confirm that a net- work device is authorized to join the network: open authentication and shared key authentication. When you configure your network, all the nodes in the network must use the same kind of authentication.

Inter Frame Spaces

- SIFS-Short Inter Frame Space: used to separate transmission belonging to a single dialog (fragment ACK) and the value is 25 milli seconds.

- PIFS Point Coordination IFS: used by AP to gain access to the medium before any other station and the value is 78 milli sec.

- DIFS Distributed IFS: used by a station willing to start a new transaction and the value is 128 milli sec.

- EIFS Extended IFS: used by a station that has received a packet that could not understand, that is needed to prevent the station to avoid the Collision in future packet belonging to that dialog.

How does the station join an existing Cell?

When a station wants to join the Cell, it can know the synchronization information from the Access Point in two ways

- Passive scanning  waits to receive Beacon Frames from the AP.

- Active scanning  transmits the Probe request to find the AP and waiting for the Probe response from AP.

Authentication Process

- Interchanging the information where each side proves the knowledge of a given password.

- Two approaches to authenticate, those are:

- Open system authentication: without verifying the identity.

- Shared key authentication: based on WEP and requires that both devices implement the WEP.

### Association Process

- Exchanging the information between stations and the AP capabilities, to know the current position of station

- After the association, a station is capable of transmitting and receiving the information.

Re-association

- The process of moving an association from old BS to new BS in an ESS

- Over the air, the process is same as the association.

- On the back bone BS s are interact with each other to move frames.

- This re association procedure is initiated when the System detects that another BS has the stronger signal.

The network supports all of these housekeeping functions in the MAC layer by exchanging (or trying to exchange) a series of control frames before it allows the higher layers to send data. It also sets several options on the network adapter:

- Power mode -The network adapter supports two power modes: Continuous Aware Mode and Power Save Polling Mode. In Continuous Aware Mode, the radio receiver is always on and consuming power. In Power Save Polling Mode, the radio is idle much of the time, but it periodically polls the access point for new messages. As the name suggests, Power Save Polling Mode reduces the battery drain on portable devices such as laptop computers and PDAs.

- Access control- The network adapter contains the access control that keeps unauthorized users out of the network. An 802.11b network can use two forms of access control: the SSID (the name of the network), and the MAC address (a unique string of characters that identifies each network node). Each network node must have the SSID programmed into it, or the access point will not associate with that node. An optional table of MAC addresses can restrict access to radios whose addresses are on the list.

- WEP encryption -The network adapter controls the Wired Equivalent Privacy (WEP) encryption function. The network can use a 64-bit or a 128-bit encryption key to encode and decode data as it passes through the radio link.

Other Control Layers

All of the activity specified in the 802.11 standards takes place at the Physical and MAC layers. The higher layers control things like addressing and routing, data integrity, syntax, and the format of the data contained inside each packet. It doesnt make any difference to these higher layers whether theyre moving packets through wires, fiber optic lines, or radio links. Therefore, you can use an 802.11b network with any kind of LAN or other network protocol. The same radios can handle TCP/IP, Novell NetWare, and the other entire network protocols built into Windows, UNIX, Mac OS, and other operating systems equally well.

Network Devices

802.11b networks include two categories of radios: stations and access points. A station is a computer, or some other device such as a printer, connected to a wireless network through an internal or external wireless network interface adapter. An access point is the base station for a wireless network and a bridge between the wireless network and a traditional wired network.

Network Adapters

Network adapters for stations can take several physical forms:

- Plug-in PC Cards that fit the PCMCIA sockets in most laptop computers. To bypass the internal shielding in most computers, the antennas and status lights in most wireless PC Card adapters extend about an inch beyond the opening of the card socket. Other PC Card adapters have sockets for external antennas.

- Internal network adapters on PCI cards that fit inside a desktop computer Most PCI adapters are actually PCMCIA sockets that allow a user to plug a PC Card into the back of the computer, but a few are built directly on the PCI expansion cards. As an alternative to a rear-panel socket, separate PCMCIA sockets that fit a computers external front-panel drive bays are available from Actiontec and several other manufacturers.

- External USB adapters are often a better choice than PC Cards, because its almost always easier to move an adapter at the end of a cable to a position with the best possible signal path to the nearest access point.

- Internal wireless adapters built into laptop computers are modules that plug into the computers motherboard. They present the same appearance to the operating system as an external PC Card. The antennas for built-in radios are usually hidden inside the computers fold-over screen.

- Plug-in adapters for PDAs and other handheld devices.

- Internal network interfaces built into other devices, such as Internet-capable telephone sets and office or household appliances.

A network adapter should work with any operating system, as long as a driver for that adapter is available. In practice, that means you can find Windows drivers for just about everything, but you will have fewer choices if youre using a computer running Mac OS, Linux, or UNIX. You can find pointers to sources for Linux and UNIX drivers in the chapters devoted to those operating systems later in this book.

Access Points

Access points are often combined with other network functions. Its quite possible to find a stand-alone access point that just plugs into a wired LAN through a data cable, but there are plenty of other options. Common access-point configurations include the following:

- Simple base stations with a bridge to an Ethernet port for connection to a LAN.

- Base stations that include a switch, hub, or router with one or more wired Ethernet ports along with the wireless access point.

- Broadband routers that provide a bridge between a cable modem or DSL port and the wireless access point.

- Software access points that use one of the wireless network interface adapters as the base station.

- Residential gateways that support a limited number of operating channels.

Operating Modes

802.11b networks operate in two modes: ad hoc networks and infrastructure networks. As the name suggests, an ad hoc network is usually temporary. An ad hoc network is a self-contained group of stations with no connection to a larger LAN or the Internet. It includes two or more wireless stations with no access point or connection to the rest of the world. Ad hoc networks are also called peer-to-peer networks and Independent Basic Service Sets (IBSS). Figure 1.6 shows a simple ad hoc network.

Infrastructure networks have one or more access points, almost always connected to a wired network. Each wireless station exchanges messages and data with the access point, which relays them to other nodes on the wireless network or the wired LAN. Any network that requires a wired connection through an access point to a printer, a file server or an Internet gateway is an infrastructure network. Figure 1.7 shows an infrastructure network.

An infrastructure network with just one base station is also called a Basic Service Set (BSS). When the wireless network uses two or more access points, the network structure is an Extended Service Set (ESS).

A network with more than one access point (an Extended Service Set) creates several new complications. First, the network must include a way for only one base station to handle data from a particular station, even if the station is within range of more than one base station. And if the station is moving during a network session, or if some kind of local interference crops up near the first access point, the network might have to hand off the connection from one access point to another.

An 802.11b network handles this problem by associating a station with only one access point at a time and ignoring the signals from stations that are not associated. When the signal fades at one access point and improves at another, or the amount of traffic forces the network to rebalance the load, the network will re associate the station with a new access point that can provide acceptable service.